|  | BiomedE / EECS 458 |
| --- | --- |

Intro-Lab Addendum

From:	Nick Langhals

Re:	SR560

# Please complete this additional material and add to the Introductory Lab.  The purpose of this portion is to become familiar with filter properties and Bode Plots.

- First test the gain accuracy of the SRS.  Set the gain to 10, and then make a plot of gain vs. input voltage for a sufficient range to demonstrate the device’s characteristics.  You may also make a plot of gain error vs. the input voltage.

- Set the SRS as a 6 dB/octave low-pass filter with a cutoff of 3 kHz and gain of 1.  Make a Bode plot.

- Repeat step 2 with a gain of 10.

- Set the SRS as a 12 dB/octave high-pass filter with a cutoff of 100 Hz and gain of 1.  Make a Bode Plot.

- Set the SRS as a 6 dB/octave band-pass filter with cutoffs of 100 Hz – 30 kHz and a gain of 10.  Make a Bode Plot.

Notes:

  - For the Bode plot, Phase can be ignored if you so desire.

  - Please display the amplitude axis as 20 * log10 (Gain).  This will give you the gain in dB.  Where Gain = Output / Input.

  - Plot the frequency axis in a logarithmic scale.  Do not take the log of the frequencies, but use a scale such that the intervals between respective frequencies are a factor of 10.