Quiz 4 – EECS 270, Spring '07

Name: ____________________________________ unique name: ____________________

Honor code:

I have not given or received aid on this quiz, nor have I observed anyone else doing so:

Sign here:_____________________________________

This quiz is graded out of 100 points and is worth about 4% of your class grade.  You will have 25 minutes for this quiz.  Closed everything including calculators! To receive partial credit, work must be shown.

- Transistor problem. [30]

| A | B | C | OUT |
| --- | --- | --- | --- |
| 0 | 0 | 0 |  |
| 0 | 0 | 1 |  |
| 0 | 1 | 0 |  |
| 0 | 1 | 1 |  |
| 1 | 0 | 0 |  |
| 1 | 0 | 1 |  |
| 1 | 1 | 0 |  |
| 1 | 1 | 1 |  |

Fill in the above truth table with either

“1”, “0”, “Hi-Z” or “Smoke” (the last if

OUT is connected to both Vcc and Ground).

- Using only tri-state drivers and inverters, design a 3-input OR gate.  You can freely use “GND” and “Vcc” as needed.  For full points your design should use 8 or less devices. [35]

- Using a K-map, find the minimal sum-of-products of Σ(W,X,Y,Z) (0,2,4,6,11,12,14)+d(9,13).  Place a star (*) next to each distinguished 1 in your K-map. [35]

# Text boxes

A

B

C

A

B

C

OUT