Quiz 2 – Spring 2013 – EECS 270

Name: ____________________________________  uname: _________________

This quiz is graded out of 100 points and is worth about 4% of your class grade.  You will have 20 minutes for this quiz.  Closed everything including calculators! To receive partial credit, work must be shown.

- Say you have one input, X as well as a single output Y. Provide a state-transition diagram where Y goes high iff the last three values of X were “100”.  [30]

| Device | Min | Max |  |
| --- | --- | --- | --- |
| DFF: |  |
| Clock to Q | 12ps | 24ps |
| Set-up time | 30ps |
| Hold time | 10ps |
| AND/OR | 20ps | 40ps |
| NAND/NOR | 15ps | 30ps |
| XOR | 10ps | 55ps |
| NOT | 10ps | 20ps |

- Given the circuit and timing information above, what is the lowest clock period you can clock this circuit at?    (Hint: the hold time is met so you don’t need to add any inverter pairs.) You should assume that the inputs are coming from flip-flops and the outputs are going to flip-flops. Clearly show your work. [30]

3. Consider the following state-transition diagram:

There is one output, Z, which is 1 when in state A and 0 in states B and C.

Using only AND, OR, and NOT gates (including freely using bubbles) as well as D flip-flops, draw the state machine for the above state-transition diagram. You are to use an encoding of A=00, B=01, and C=10 for the states.  Finally, any unused state encodings should be treated as don’t cares.  You need not minimize your logic (though doing so may reduce your work…) [40]

# Text boxes

A

C

B

X

!X

!X

!X

X

X