## Slide 1
EECS 373
Design of Microprocessor-Based Systems
Ron Dreslinski
University of Michigan
Lecture 2: Architecture, Assembly, and ABI
Sept. 12, 2016
Slides developed in part by Prof. Dutta and Dr. Brehob

## Slide 2: Admin Stuff
Website URL (again)
  http://www.eecs.umich.edu/courses/eecs373/
HW1 Due on Wednesday
Schedule things:
  Group formation meeting Monday 10/10 6:30-8:00
  Midterm exam Monday 10/24 7:00-9:00 (sharp)
    Tentative
  373 Design Expo Monday 12/12
    Time TBA (11am-2 most likely)
  Final Exam, 12/21 1:30-3:30pm

## Slide 3: Today…
ARM assembly example
Walk though of the ARM ISA
Lab tool flow
Start on Application Binary Interface (ABI)

## Slide 4: Major elements of an Instruction Set Architecture (registers, memory, word size, endianess, conditions, instructions, addressing modes)
32-bits
32-bits
Endianess
mov r0, #1
ld r1, [r0,#5]
mem((r0)+5)
bne loop
subs r2, #1
Endianess

## Slide 5: The endianess religious war: 284 years and counting!
Modern version
  Danny Cohen
  IEEE Computer, v14, #10
  Published in 1981
  Satire on CS religious war
Historical Inspiration
  Jonathan Swift
  Gulliver's Travels
  Published in 1726
  Satire on Henry-VIII’s split with the Church
    Now a major motion picture!
Memory Value
Offset (LSB) (MSB)
====== ===========
uint8_t a = 1; 0x0000 01 02 FF 00
uint8_t b = 2;
uint16_t c = 255; // 0x00FF
uint32_t d = 0x12345678; 0x0004 78 56 34 12
Little-Endian
  LSB is at lower address
Big-Endian
  MSB is at lower address
Memory Value
Offset (LSB) (MSB)
====== ===========
uint8_t a = 1; 0x0000 01 02 00 FF
uint8_t b = 2;
uint16_t c = 255; // 0x00FF
uint32_t d = 0x12345678; 0x0004 12 34 56 78

## Slide 6: Addressing: Big Endian vs Little Endian (370 slide)
Endian-ness: ordering of bytes within a word
  Little - increasing numeric significance with increasing memory addresses
  Big – The opposite, most significant byte first
  MIPS is big endian, x86 is little endian

## Slide 7: Instruction encoding
ARMv7 ARM
Instructions are encoded in machine language opcodes
Sometimes
  Necessary to hand generate opcodes
  Necessary to verify assembled code is correct
How?
Instructions
movs r0, #10
movs r1, #0
Register Value Memory Value
001|00|000|00001010 (LSB) (MSB)
(msb) (lsb) 0a 20 00 21
001|00|001|00000000
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 8: Assembly example
data:
.byte 0x12, 20, 0x20, -1
func:
mov r0, #0
mov r4, #0
movw r1, #:lower16:data
movt r1, #:upper16:data
top: ldrb r2, [r1],#1
add r4, r4, r2
add r0, r0, #1
cmp r0, #4
bne top

## Slide 9: Instructions used
mov
  Moves data from register or immediate.
  Or also from shifted register or immediate!
    the mov assembly instruction maps to a bunch of different encodings!
  If immediate it might be a 16-bit or 32-bit instruction.
movw
  Actually an alias to mov.
    “w” is “wide”
    hints at 16-bit immediate.

## Slide 10: From the ARMv7-M Architecture Reference Manual (posted on the website under references)
There are similar entries for
move immediate, move shifted
(which actually maps to different
instructions) etc.

## Slide 11: Directives
#:lower16:data
  What does that do?
  Why?

## Slide 13: Loads!
ldrb -- Load register byte
  Note this takes an 8-bit value and moves it into a 32-bit location!
    Zeros out the top 24 bits.
ldrsb -- Load register signed byte
  Note this also takes an 8-bit value and moves it into a 32-bit location!
    Uses sign extension for the top 24 bits.

## Slide 14: Addressing Modes
Offset Addressing
  Offset is added or subtracted from base register
  Result used as effective address for memory access
  [<Rn>, <offset>]
Pre-indexed Addressing
  Offset is applied to base register
  Result used as effective address for memory access
  Result written back into base register
  [<Rn>, <offset>]!
Post-indexed Addressing
  The address from the base register is used as the EA
  The offset is applied to the base and then written back
  [<Rn>], <offset>
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 15: So what does the program _do_?
data:
.byte 0x12, 20, 0x20, -1
func:
mov r0, #0
mov r4, #0
movw r1, #:lower16:data
movt r1, #:upper16:data
top: ldrb r2, [r1],#1
add r4, r4, r2
add r0, r0, #1
cmp r0, #4
bne top

## Slide 16: Today…
ARM assembly example
Walk though of the ARM ISA
Tool Flow
Start on Application Binary Interface (ABI)

## Slide 17: An ISA defines the hardware/software interface
A “contract” between architects and programmers
Register set
Instruction set
  Addressing modes
  Word size
  Data formats
  Operating modes
  Condition codes
Calling conventions
  Really not part of the ISA (usually)
  Rather part of the ABI
  But the ISA often provides meaningful support.

## Slide 18: ARM Architecture roadmap

## Slide 19: A quick comment on the ISA: From: ARMv7-M Architecture Reference Manual

## Slide 20: ARM Cortex-M3 ISA
Register Set
Address Space
Branching
Data processing
Load/Store
Exceptions
Miscellaneous
Instruction Set
32-bits
32-bits
Endianess
Endianess

## Slide 21: Registers
Mode dependent

## Slide 22: Address Space

## Slide 23: Instruction Encoding ADD immediate

## Slide 25: Branch

## Slide 26: Data processing instructions
Many, Many More!

## Slide 27: Load/Store instructions

## Slide 28: Miscellaneous instructions

## Slide 29: Addressing Modes (again)
Offset Addressing
  Offset is added or subtracted from base register
  Result used as effective address for memory access
  [<Rn>, <offset>]
Pre-indexed Addressing
  Offset is applied to base register
  Result used as effective address for memory access
  Result written back into base register
  [<Rn>, <offset>]!
Post-indexed Addressing
  The address from the base register is used as the EA
  The offset is applied to the base and then written back
  [<Rn>], <offset>
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 30: <offset> options
An immediate constant
  #10
An index register
  <Rm>
A shifted index register
  <Rm>, LSL #<shift>
Lots of weird options…
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 31: Application Program Status Register (APSR)
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 32: Updating the APSR
SUB Rx, Ry
  Rx = Rx - Ry
  APSR unchanged
SUBS
  Rx = Rx - Ry
  APSR N, Z, C, V updated
ADD Rx, Ry
  Rx = Rx + Ry
  APSR unchanged
ADDS
  Rx = Rx + Ry
  APSR N, Z, C, V updated
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 33: Overflow and carry in APSR
unsigned_sum = UInt(x) + UInt(y) + UInt(carry_in);
signed_sum = SInt(x) + SInt(y) + UInt(carry_in);
result = unsigned_sum<N-1:0>; // == signed_sum<N-1:0>
carry_out = if UInt(result) == unsigned_sum then ’0’ else ’1’;
overflow = if SInt(result) == signed_sum then ’0’ else ’1’;

## Slide 34: Conditional execution: Append to many instructions for conditional execution
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 35: The ARM architecture “books” for this class

## Slide 36: The ARM software tools “books” for this class

## Slide 37: An ARM assembly language program for GNU
.equ STACK_TOP, 0x20000800
.text
.syntax unified
.thumb
.global _start
.type start, %function
_start:
.word STACK_TOP, start
start:
movs r0, #10
movs r1, #0
loop:
adds r1, r0
subs r0, #1
bne loop
deadloop:
b deadloop
.end

## Slide 38: A simple Makefile
all:
arm-none-eabi-as -mcpu=cortex-m3 -mthumb example1.s -o example1.o
arm-none-eabi-ld -Ttext 0x0 -o example1.out example1.o
arm-none-eabi-objcopy -Obinary example1.out example.bin
arm-none-eabi-objdump -S example1.out > example1.list

## Slide 39: An ARM assembly language program for GNU
.equ STACK_TOP, 0x20000800
.text
.syntax unified
.thumb
.global _start
.type start, %function
_start:
.word STACK_TOP, start
start:
movs r0, #10
movs r1, #0
loop:
adds r1, r0
subs r0, #1
bne loop
deadloop:
b deadloop
.end

## Slide 40: Disassembled object code
example1.out: file format elf32-littlearm
Disassembly of section .text:
00000000 <_start>:
0: 20000800 .word 0x20000800
4: 00000009 .word 0x00000009
00000008 <start>:
8: 200a movs r0, #10
a: 2100 movs r1, #0
0000000c <loop>:
c: 1809 adds r1, r1, r0
e: 3801 subs r0, #1
10: d1fc bne.n c <loop>
00000012 <deadloop>:
12: e7fe b.n 12 <deadloop>

## Slide 41: Today…
ARM assembly example
Walk though of the ARM ISA
Tool Flow
Start on Application Binary Interface (ABI)

## Slide 42: How does an assembly language program get turned into a executable program image?
Assembly
files (.s)
Object
files (.o)
as
(assembler)
ld
(linker)
Memory
layout
Linker
script (.ld)
Executable
image file
Binary program
file (.bin)
Disassembled
code (.lst)
objcopy
objdump

## Slide 43: What are the real GNU executable names for the ARM?
Just add the prefix “arm-none-eabi-” prefix
Assembler (as)
  arm-none-eabi-as
Linker (ld)
  arm-none-eabi-ld
Object copy (objcopy)
  arm-none-eabi-objcopy
Object dump (objdump)
  arm-none-eabi-objdump
C Compiler (gcc)
  arm-none-eabi-gcc
C++ Compiler (g++)
  arm-none-eabi-g++

## Slide 44: A simple (hardcoded) Makefile example
all:
arm-none-eabi-as -mcpu=cortex-m3 -mthumb example1.s -o example1.o
arm-none-eabi-ld -Ttext 0x0 -o example1.out example1.o
arm-none-eabi-objcopy -Obinary example1.out example1.bin
arm-none-eabi-objdump -S example1.out > example1.lst

## Slide 45: What information does the disassembled file provide?
.equ STACK_TOP, 0x20000800
.text
.syntax unified
.thumb
.global _start
.type start, %function
_start:
.word STACK_TOP, start
start:
movs r0, #10
movs r1, #0
loop:
adds r1, r0
subs r0, #1
bne loop
deadloop:
b deadloop
.end
example1.out: file format elf32-littlearm
Disassembly of section .text:
00000000 <_start>:
0: 20000800 .word 0x20000800
4: 00000009 .word 0x00000009
00000008 <start>:
8: 200a movs r0, #10
a: 2100 movs r1, #0
0000000c <loop>:
c: 1809 adds r1, r1, r0
e: 3801 subs r0, #1
10: d1fc bne.n c <loop>
00000012 <deadloop>:
12: e7fe b.n 12 <deadloop>
all:
arm-none-eabi-as -mcpu=cortex-m3 -mthumb example1.s -o example1.o
arm-none-eabi-ld -Ttext 0x0 -o example1.out example1.o
arm-none-eabi-objcopy -Obinary example1.out example1.bin
arm-none-eabi-objdump -S example1.out > example1.lst

## Slide 46: What are the elements of a real assembly program?
.equ STACK_TOP, 0x20000800 /* Equates symbol to value */
.text /* Tells AS to assemble region */
.syntax unified /* Means language is ARM UAL */
.thumb /* Means ARM ISA is Thumb */
.global _start /* .global exposes symbol */
/* _start label is the beginning */
/* ...of the program region */
.type start, %function /* Specifies start is a function */
/* start label is reset handler */
_start:
.word STACK_TOP, start /* Inserts word 0x20000800 */
/* Inserts word (start) */
start:
movs r0, #10 /* We’ve seen the rest ... */
movs r1, #0
loop:
adds r1, r0
subs r0, #1
bne loop
deadloop:
b deadloop
.end

## Slide 47: How are assembly files assembled?
$ arm-none-eabi-as -mcpu=cortex-m3 -mthumb example1.s -o example1.o
$ arm-none-eabi-as
  Useful options
    -mcpu
    -mthumb
    -o

## Slide 48: How does a mixed C/Assembly program get turned into a executable program image?
Assembly
files (.s)
Object
files (.o)
as
(assembler)
gcc
(compile
+ link)
Memory
layout
Linker
script (.ld)
Executable
image file
Binary program
file (.bin)
Disassembled
Code (.lst)
objcopy
objdump
ld
(linker)
Library object
files (.o)
C files (.c)

## Slide 49: Today…
ARM assembly example
Walk though of the ARM ISA
Tool Flow
Start on Application Binary Interface (ABI)

## Slide 50: Outline
ARM Cortex-M3 ISA and example
Tool flow
ABI (intro)

## Slide 52: ABI quote
A subroutine must preserve the contents of the registers r4-r8, r10, r11 and SP (and r9 in PCS variants that designate r9 as v6).

## Slide 53
Questions?
Comments?
Discussion?