## Slide 1
EECS 373
Design of Microprocessor-Based Systems
Ronald Dreslinski
University of Michigan
Sampling, ADCs, and DACs and more
Some slides adapted from Mark Brehob, Prabal Dutta, Jonathan Hui & Steve Reinhardt

## Slide 2: Outline
Sampling
ADC
DAC

## Slide 3: We live in an analog world
Everything in the physical world is an analog signal
  Sound, light, temperature, pressure
Need to convert into electrical signals
  Transducers: converts one type of energy to another
    Electro-mechanical, Photonic, Electrical, …
  Examples
    Microphone/speaker
    Thermocouples
    Accelerometers

## Slide 4: Transducers convert one form of energy into another
Transducers
  Allow us to convert physical phenomena to a voltage potential in a well-defined way.
A transducer is a device that converts one type of energy to another. The conversion can be to/from
electrical, electro-mechanical, electromagnetic, photonic, photovoltaic, or any other form of energy.
While the term transducer commonly implies use as a sensor/detector, any device which converts energy
can be considered a transducer. – Wikipedia.

## Slide 5: Convert light to voltage with a CdS photocell
Vsignal = (+5V) RR/(R + RR)
Choose R=RR at median of intended range
Cadmium Sulfide (CdS)
Cheap, low current
tRC = (R+RR)*Cl
  Typically R~50-200kW
  C~20pF
  So, tRC~20-80uS
  fRC ~ 10-50kHz
Source: Forrest Brewer

## Slide 6: Many other common sensors (some digital)
Force
  strain gauges - foil, conductive ink
  conductive rubber
  rheostatic fluids
    Piezorestive (needs bridge)
  piezoelectric films
  capacitive force
    Charge source
Sound
  Microphones
    Both current and charge versions
  Sonar
    Usually Piezoelectric
Position
  microswitches
  shaft encoders
  gyros
Acceleration
  MEMS
  Pendulum
Monitoring
  Battery-level
    voltage
  Motor current
    Stall/velocity
  Temperature
    Voltage/Current Source
Field
  Antenna
  Magnetic
    Hall effect
    Flux Gate
Location
  Permittivity
  Dielectric
Source: Forrest Brewer

## Slide 7: Going from analog to digital
What we want
How we have to get there
Software
Sensor
ADC
Physical
Phenomena
Voltage or
Current
ADC Counts
Engineering Units
Physical
Phenomena
Engineering Units

## Slide 8: Representing an analog signal digitally
How do we represent an analog signal?
  As a time series of discrete values
   On MCU: read the ADC data register periodically
V
Counts

## Slide 9: Choosing the horizontal range
What do the sample values represent?
  Some fraction within the range of values
   What range to use?
Range Too Small
Range Too Big
Ideal Range

## Slide 10: Choosing the horizontal granularity
Resolution
  Number of discrete values that represent a range of analog values
  MSP430: 12-bit ADC
    4096 values
    Range / 4096 = Step
  Larger range  less information
Quantization Error
  How far off discrete value is from actual
  ½ LSB  Range / 8192
  Larger range  larger error

## Slide 11: Choosing the sample rate
What sample rate do we need?
  Too little: we can’t reconstruct the signal we care about
  Too much: waste computation, energy, resources

## Slide 12: Shannon-Nyquist sampling theorem
If a continuous-time signal contains no frequencies higher than , it can be completely determined by discrete samples taken at a rate:
Example:
  Humans can process audio signals 20 Hz – 20 KHz
  Audio CDs: sampled at 44.1 KHz

## Slide 13: Converting between voltages, ADC counts, and engineering units
Converting: ADC counts  Voltage
Converting: Voltage  Engineering Units

## Slide 14: A note about sampling and arithmetic*
Converting values in fixed-point MCUs
  float vtemp = adccount/4095 * 1.5;
  float tempc = (vtemp-0.986)/0.00355;
   vtemp = 0! Not what you intended, even when vtemp is a float!
   tempc = -277 C
Fixed point operations
  Need to worry about underflow and overflow
Floating point operations
  They can be costly on the node
Notes: $ cat arithmetic.c
#include <stdio.h>
int main() {
int adccount = 2048;
float vtemp;
float tempc;
vtemp = adccount/4095 * 1.5;
tempc = (vtemp-0.986)/0.00355;
printf("vtemp: %f\n", vtemp);
printf("tempc: %f\n", tempc);
}
$ gcc arithmetic.c
$ ./a.out
vtemp: 0.000000
tempc: -277.746490

## Slide 15: Try it out for yourself…
$ cat arithmetic.c
#include <stdio.h>
int main() {
int adccount = 2048;
float vtemp;
float tempc;
vtemp = adccount/4095 * 1.5;
tempc = (vtemp-0.986)/0.00355;
printf("vtemp: %f\n", vtemp);
printf("tempc: %f\n", tempc);
}
$ gcc arithmetic.c
$ ./a.out
vtemp: 0.000000
tempc: -277.746490
Notes: $ cat arithmetic.c
#include <stdio.h>
int main() {
int adccount = 2048;
float vtemp;
float tempc;
vtemp = adccount/4095 * 1.5;
tempc = (vtemp-0.986)/0.00355;
printf("vtemp: %f\n", vtemp);
printf("tempc: %f\n", tempc);
}
$ gcc arithmetic.c
$ ./a.out
vtemp: 0.000000
tempc: -277.746490

## Slide 16: Use anti-aliasing filters on ADC inputs to ensure that Shannon-Nyquist is satisfied
Aliasing
  Different frequencies are indistinguishable when they are sampled.
Condition the input signal using a low-pass filter
  Removes high-frequency components
  (a.k.a. anti-aliasing filter)

## Slide 17: Do I really need to condition my input signal?
Short answer: Yes.
Longer answer: Yes, but sometimes it’s already done for you.
  Many (most?) ADCs have a pretty good analog filter built in.
  Those filters typically have a cut-off frequency just above ½ their maximum sampling rate.
    Which is great if you are using the maximum sampling rate, less useful if you are sampling at a slower rate.

## Slide 18: Designing the anti-aliasing filter
Note
  w is in radians
  w = 2pf
Exercise: Say you want the half-power point to be at 30Hz and you have a 0.1 μF capacitor. How big of a resistor should you use?
Notes: R = 1/(w*C) = 1/(2*pi*f*C) = 1/(2*pi*30*0.1e-6) = 1/(0.00001884) = 53K
53K
0.5 = 1/sqrt [1 + (2*pi*30)^2 + R^2 * (0.1e-6)^2]
[1 + (2*pi*30)^2 + R^2 + (0.1e-6)^2] = 2
R = 1/[60*pi)^2 * (0.1e-6)^2] = 53K

## Slide 19: Oversampling
One interesting trick is that you can use oversampling to help reduce the impact of quantization error.
  Let’s look at an example of oversampling plus dithering to get a 1-bit converter to do a much better job…

## Slide 20: Oversampling a 1-bit ADC w/ noise & dithering (cont)
1
0
Count
Voltage
500 mV
0 mV
375 mV
N1 = 11
N0 = 32
uniformly
distributed
random noise
±250 mV
“upper edge”
of the box
Vthresh = 500 mV
Vrand =
500 mV
Note:
N1 is the # of ADC counts that = 1 over the sampling window
N0 is the # of ADC counts that = 0 over the sampling window

## Slide 21: Oversampling a 1-bit ADC w/ noise & dithering (cont)
How to get more than 1-bit out of a 1-bit ADC?
Add some noise to the input
Do some math with the output
Example
  1-bit ADC with 500 mV threshold
  Vin = 375 mV  ADC count = 0
  Add ±250 mV uniformly distributed random noise to Vin
  Now, roughly
    25% of samples (N1) ≥ 500 mV  ADC count = 1
    75% of samples (N0) < 500 mV  ADC count = 0
  So, the “upper edge” of the box equals
    Vthresh + N1/(N1+N0) * Vrand = 0.5 + 11/(11+32)*0.5 = 0.628 V
  Middle of box (where our “signal” of 375 mV sits) equals
    0.628 V – Vrand/2 = 0.628 V – 0.25 = 0.378 V
  Real value is 0.375 V, so our estimate has < 1% error!

## Slide 22: Lots of other issues
Might need anti-imaging filter
Cost and power play a role
Might be able to avoid analog all together
  Think PWM when dealing with motors…

## Slide 23: How do ADCs and DACs work?
Next Time…

## Slide 24: DAC #1: Voltage Divider
2-to-4 decoder
2
Din
Vout
Fast
Size (transistors, switches)?
Accuracy?
Monotonicity?
Vref
R
R
R
R

## Slide 25: DAC #2: R/2R Ladder
D3 (MSB)
D2
D1
D0 (LSB)
2R
2R
2R
2R
R
R
R
2R
Iout
Vref
Size?
Accuracy?
Monotonicity? (Consider 0111 -> 1000)

## Slide 26: ADC #1: Flash
Vref
R
R
R
R
Vin
+
_
priority
encoder
3
2
1
0
Vcc
2
Dout
+
_
+
_

## Slide 27: ADC #2: Single-Slope Integration
+
_
Vin
n-bit counter
CLK
EN*
Vcc
done
Start: Reset counter, discharge C.
Charge C at fixed current I until Vc > Vin . How should C, I, n, and CLK be related?
Final counter value is Dout.
Conversion may take several milliseconds.
Good differential linearity.
Absolute linearity depends on precision of C, I, and clock.
C
I
Notes: DV = Vref / 2^n
DQ = C DV
I = DQ/DT
 I DT / C = Vref / 2^n

## Slide 28: ADC #3: Successive Approximation (SAR)
1 Sample  Multiple cycles
Requires N-cycles per sample where N is # of bits
Goes from MSB to LSB
Not good for high-speed ADCs

## Slide 29: Errors and ADCs
Figures and some text from:
  Understanding analog to digital converter specifications. By Len Staller
  http://www.embedded.com/showArticle.jhtml?articleID=60403334
Key concept here is that the specification provides worst case values.

## Slide 32
The integral nonlinearity (INL) is the deviation of an ADC's transfer function from a straight line.
This line is often a best-fit line among the points in the plot but can also be a line that connects
the highest and lowest data points, or endpoints. INL is determined by measuring the voltage
at which all code transitions occur and comparing them to the ideal. The difference between
the ideal voltage levels at which code transitions occur and the actual voltage is the INL error,
expressed in LSBs. INL error at any given point in an ADC's transfer function is the accumulation
of all DNL errors of all previous (or lower) ADC codes, hence it's called integral nonlinearity.
Integral nonlinearity

## Slide 33
DNL is the worst cases variation of actual step size vs. ideal step size. It’s a promise it won’t be worse than X.
Differential nonlinearity

## Slide 34
Sometimes the intentional ½ LSB shift is included here!

## Slide 35
Full-scale error is also sometimes called “gain error”
full-scale error is the difference between the ideal code transition to the highest output code and the actual transition to the output code when the offset error is zero.

## Slide 36: Errors
Once again: Errors in a specification are worst case.
  So if you have an INL of ±.25 LSB, you “know” that the device will never have more than .25 LSB error from its ideal value.
  That of course assumes you are opperating within the specification
    Temperature, input voltage, input current available, etc.
INL and DNL are the ones I expect you to work with
  Should know what full-scale error is