## Slide 1
EECS 373
Design of Microprocessor-Based Systems
Website: www.eecs.umich.edu/courses/eecs373/
Ronald Dreslinski
University of Michigan
Midterm Review
Slides developed in part by Prof. Dutta and Dr. Brehob

## Slide 2: What is an embedded system?

## Slide 3
What is driving the
embedded everywhere explosion?

## Slide 4: Moore’s Law (a statement about economics): IC transistor count doubles every 18-24 mo
Photo Credit: Intel

## Slide 5: Bell’s Law: A new computer class every decade
“Roughly every decade a new, lower priced computer class forms based on a new programming platform, network, and interface resulting in new usage and the establishment of a new industry.”
- Gordon Bell [1972,2008]
5

## Slide 6: What is driving Bell’s Law?
Technology Scaling
Moore’s Law
  Made transistors cheap
Dennard’s Scaling
  Made them fast
  And low-power
Result
  Holding #T’s constant
    Exponentially lower cost
    Exponentially lower power
  Small, cheap & low-power
    Microcontrollers
    Memory
    Radios
Technology Innovations
MEMS technology
  Micro-fabricated sensors
New memories
  New cell structures (11T)
  New tech (FeRAM, FinFET)
Near-threshold computing
  Minimize active power
  Minimize static power
New wireless systems
  Radio architectures
  Modulation schemes
Energy harvesting

## Slide 7
Why study 32-bit MCUs and FPGAs?

## Slide 8
What differentiates these
products from one another?
FPGA Microprocessor
===== =============

## Slide 9
MPU FPGA

## Slide 10: MCU-32 and PLDs are tied in embedded market share

## Slide 11: Major elements of an Instruction Set Architecture (registers, memory, word size, endianess, conditions, instructions, addressing modes)
32-bits
32-bits
Endianess
mov r0, #1
ld r1, [r0,#5]
r1=mem((r0)+5)
bne loop
subs r2, #1
Endianess

## Slide 12: The endianess religious war: 284 years and counting!
Modern version
  Danny Cohen
  IEEE Computer, v14, #10
  Published in 1981
  Satire on CS religious war
Historical Inspiration
  Jonathan Swift
  Gulliver's Travels
  Published in 1726
  Satire on Henry-VIII’s split with the Church
    Now a major motion picture!
Memory Value
Offset (LSB) (MSB)
====== ===========
uint8_t a = 1; 0x0000 01 02 FF 00
uint8_t b = 2;
uint16_t c = 255; // 0x00FF
uint32_t d = 0x12345678; 0x0004 78 56 34 12
Little-Endian
  LSB is at lower address
Big-Endian
  MSB is at lower address
Memory Value
Offset (LSB) (MSB)
====== ===========
uint8_t a = 1; 0x0000 01 02 00 FF
uint8_t b = 2;
uint16_t c = 255; // 0x00FF
uint32_t d = 0x12345678; 0x0004 12 34 56 78

## Slide 13: Addressing: Big Endian vs Little Endian (370 slide)
Endian-ness: ordering of bytes within a word
  Little - increasing numeric significance with increasing memory addresses
  Big – The opposite, most significant byte first
  MIPS is big endian, x86 is little endian

## Slide 14: Instruction encoding
Instructions are encoded in machine language opcodes
Sometimes
  Necessary to hand generate opcodes
  Necessary to verify assembled code is correct
How?
Instructions
movs r0, #10
movs r1, #0
ARMv7 ARM
Register Value Memory Value
001|00|000|00001010 (LSB) (MSB)
(msb) (lsb) 0a 20 00 21
001|00|001|00000000
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 15: Assembly example
data:
.byte 0x12, 20, 0x20, -1
func:
mov r0, #0
mov r4, #0
movw r1, #:lower16:data
movt r1, #:upper16:data
top: ldrb r2, [r1],1
add r4, r4, r2
add r0, r0, #1
cmp r0, #4
bne top

## Slide 16: An ISA defines the hardware/software interface
A “contract” between architects and programmers
Register set
Instruction set
  Addressing modes
  Word size
  Data formats
  Operating modes
  Condition codes
Calling conventions
  Really not part of the ISA (usually)
  Rather part of the ABI
  But the ISA often provides meaningful support.

## Slide 17: ARM Architecture roadmap

## Slide 18: ARM Cortex-M3 ISA
Register Set
Address Space
Branching
Data processing
Load/Store
Exceptions
Miscellaneous
Instruction Set
32-bits
32-bits
Endianess
Endianess

## Slide 19: Addressing Modes (again)
Offset Addressing
  Offset is added or subtracted from base register
  Result used as effective address for memory access
  [<Rn>, <offset>]
Pre-indexed Addressing
  Offset is applied to base register
  Result used as effective address for memory access
  Result written back into base register
  [<Rn>, <offset>]!
Post-indexed Addressing
  The address from the base register is used as the EA
  The offset is applied to the base and then written back
  [<Rn>], <offset>
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 20: Application Program Status Register (APSR)
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 22: ABI quote
A subroutine must preserve the contents of the registers r4-r8, r10, r11 and SP (and r9 in PCS variants that designate r9 as v6).

## Slide 23: ABI Basic Rules
A subroutine must preserve the contents of the registers r4-11 and SP
  Let’s be careful with r9 though.
Arguments are passed though r0 to r3
  If we need more, we put a pointer into memory in one of the registers.
    We’ll worry about that later.
Return value is placed in r0
  r0 and r1 if 64-bits.
Allocate space on stack as needed. Use it as needed.
  Put it back when done…
  Keep word aligned.

## Slide 24: Other useful factoids
Stack grows down.
  And pointed to by “sp”
Address we need to go back to in “lr”
And useful things for the example
Assembly instructions
  add adds two values
  mul multiplies two values
  bx branch to register

## Slide 25: Memory-mapped I/O
The idea is really simple
  Instead of real memory at a given memory address, have an I/O device respond.
    Huh?
Example:
  Let’s say we want to have an LED turn on if we write a “1” to memory location 5.
  Further, let’s have a button we can read (pushed or unpushed) by reading address 4.
    If pushed, it returns a 1.
    If not pushed, it returns a 0.

## Slide 26: Now…
How do you get that to happen?
  We could just say “magic” but that’s not very helpful.
  Let’s start by detailing a simple bus and hooking hardware up to it.
We’ll work on a real bus next time!

## Slide 27: Basic example
Discuss a basic bus protocol
  Asynchronous (no clock)
  Initiator and Target
  REQ#, ACK#, Data[7:0], ADS[7:0], CMD
    CMD=0 is read, CMD=1 is write.
    REQ# low means initiator is requesting something.
    ACK# low means target has done its job.

## Slide 28: A read transaction
Say initiator wants to read location 0x24
  Initiator sets ADS=0x24, CMD=0.
  Initiator then sets REQ# to low. (why do we need a delay? How much of a delay?)
  Target sees read request.
  Target drives data onto data bus.
  Target then sets ACK# to low.
  Initiator grabs the data from the data bus.
  Initiator sets REQ# to high, stops driving ADS and CMD
  Target stops driving data, sets ACK# to high terminating the transaction

## Slide 29: Read transaction
ADS[7:0]
CMD
Data[7:0]
REQ#
ACK#
??
??
0x24
??
??
0x55
A B C D E F G HI

## Slide 30: A write transaction (write 0xF4 to location 0x31)
  Initiator sets ADS=0x31, CMD=1, Data=0xF4
  Initiator then sets REQ# to low.
  Target sees write request.
  Target reads data from data bus. (Just has to store in a register, need not write all the way to memory!)
  Target then sets ACK# to low.
  Initiator sets REQ# to high & stops driving other lines.
  Target sets ACK# to high terminating the transaction

## Slide 31: The push-button (if ADS=0x04 write 0 or 1 depending on button)
ADS[7]
ADS[6]
ADS[5]
ADS[4]
ADS[3]
ADS[2]
ADS[1]
ADS[0]
REQ#
Button (0 or 1)
0
Data[7]
Data[0]
..
..
..
..
..
Delay
ACK#
Button (0 or 1)

## Slide 32: The push-button (if ADS=0x04 write 0 or 1 depending on button)
ADS[7]
ADS[6]
ADS[5]
ADS[4]
ADS[3]
ADS[2]
ADS[1]
ADS[0]
REQ#
Button (0 or 1)
0
Data[7]
Data[0]
..
..
..
..
..
Delay
ACK#
What about CMD?

## Slide 33: The LED (1 bit reg written by LSB of address 0x05)
ADS[5]
ADS[7]
ADS[6]
ADS[4]
ADS[3]
ADS[2]
ADS[1]
ADS[0]
REQ#
Flip-flop which controls LED
clock
D
DATA[5]
DATA[7]
DATA[6]
DATA[4]
DATA[3]
DATA[2]
DATA[1]
DATA[0]
Delay
ACK#

## Slide 34: Advanced Microcontroller Bus Architecture (AMBA) - Advanced High-performance Bus (AHB) - Advanced Peripheral Bus (APB)
AHB
High performance
Pipelined operation
Burst transfers
Multiple bus masters
Split transactions
APB
Low power
Latched address/control
Simple interface
Suitable of many peripherals

## Slide 35: Actel SmartFusion system/bus architecture

## Slide 36: Bus terminology
Any given transaction have an “initiator” and “target”
Any device capable of being an initiator is said to be a “bus master”
  In many cases there is only one bus master (single master vs. multi-master).
A device that can only be a target is said to be a slave device.
Some wires might be shared among all devices while others might be point-to-point connections (generally connecting the master to each target).

## Slide 37: Driving shared wires
It is commonly the case that some shared wires might have more than one potential device that needs to drive them.
  For example there might be a shared data bus that is used by the targets and the initiator. We saw this in the simple bus.
  In that case, we need a way to allow one device to control the wires while the others “stay out of the way”
    Most common solutions are:
      using tri-state drivers (so only one device is driving the bus at a time)
      using open-collector connections (so if any device drives a 0 there is a 0 on the bus otherwise there is a 1)

## Slide 38: Or just say no to shared wires.
Another option is to not share wires that could be driven by more than one device...
  This can be really expensive.
    Each target device would need its own data bus.
    That’s a LOT of wires!
  Not doable when connecting chips on a PCB as you are paying for each pin.
  Quite doable (though not pretty) inside of a chip.

## Slide 39: APB is a fairly simple bus designed to be easy to work with.
Low-cost
Low-power
Low-complexity
Low-bandwidth
Non-pipelined
Ideal for peripherals

## Slide 40: APB bus signals
PCLK
  Clock
PADDR
  Address on bus
PWRITE
  1=Write, 0=Read
PWDATA
  Data written to the I/O device. Supplied by the bus master/processor.

## Slide 41: APB bus signals
PSEL
  Asserted if the current bus transaction is targeted to this device
PENABLE
  High during entire transaction other than the first cycle.
PREADY
  Driven by target. Similar to our #ACK. Indicates if the target is ready to do transaction. Each target has it’s own PREADY

## Slide 42: So what’s happening here?

## Slide 43: A read transfer with wait states
Setup phase begins
with this rising edge
Setup
Phase
Access
Phase
Wait
State
Wait
State

## Slide 44: Interrupts
Interrupt (a.k.a. exception or trap):
An event that causes the CPU to stop executing the current program and begin executing a special piece of code called an interrupt handler or interrupt service routine (ISR). Typically, the ISR does some work and then resumes the interrupted program.
Interrupts are really glorified procedure calls, except that they:
  can occur between any two instructions
  are transparent to the running program (usually)
  are not explicitly requested by the program (typically)
  call a procedure at an address determined by the type of interrupt, not the program

## Slide 45: Two basic types of interrupts (1/2)
Those caused by an instruction
  Examples:
    TLB miss
    Illegal/unimplemented instruction
    div by 0
  Names:
    Trap, exception

## Slide 46: Two basic types of interrupts (2/2)
Those caused by the external world
  External device
  Reset button
  Timer expires
  Power failure
  System error
Names:
  interrupt, external interrupt

## Slide 47: How it works
Something tells the processor core there is an interrupt
Core transfers control to code that needs to be executed
Said code “returns” to old program
Much harder then it looks.
  Why?

## Slide 48: … is in the details
How do you figure out where to branch to?
How do you ensure that you can get back to where you started?
Don’t we have a pipeline? What about partially executed instructions?
What if we get an interrupt while we are processing our interrupt?
What if we are in a “critical section?”

## Slide 49: Where
If you know what caused the interrupt then you want to jump to the code that handles that interrupt.
  If you number the possible interrupt cases, and an interrupt comes in, you can just branch to a location, using that number as an offset (this is a branch table)
  If you don’t have the number, you need to poll all possible sources of the interrupt to see who caused it.
    Then you branch to the right code

## Slide 50
Enabling and disabling interrupt sources

## Slide 51: Polling-Driven Application
Recall pushbutton-LED example
  mov r0, #0x4 % PBS MMIO address
  mov r1, #0x5 % LED MMIO address
  loop: ldr r2, [r0, #0] % Read value from switch [1 cycle]
  str r2 [r1, #0] % Save value to LED [1 cycle]
  b loop % Repeat these steps [1 cycle]
This is a polling-driven application
Software constantly loops, polling and (re)acting
However, it doesn’t do anything else useful!
Notes: mov r0, #0x4 % PB
mov r1, #0x5 % LED
loop: ldr r2, [r0, #0]
str r2 [r1, #0]
b loop

## Slide 52: The Problem with Polling
If we want to do other work, we might call a routine:
  mov r0, #0x4 % PBS MMIO address
  mov r1, #0x5 % LED MMIO address
  loop: ldr r2, [r0, #0] % Read value from switch [1 cycle]
  str r2 [r1, #0] % Save value to LED [1 cycle]
  bl do_some_work % Do some other work [100 cycles]
  b loop % Repeat these steps [1 cycle]
Polling affects the responsiveness of PBS  LED path!
  Whenever we’re “doing some work,” we not polling PBS
  And the more “other work” we do, the worse the latency gets
And it affects the efficiency of the processor
  The ldr/str values don’t change very either much
  So, the processor is mostly wasting CPU cycles (and energy)
Notes: LDR % Assume PBS changes just after sampling, so latency = 1 cycle
STR % latency += 1 cycle
B % latency += 1 cycle
Delay? So LDR (1, just missed) + STR (1) + B (1) + LDR (1) + STR (1) ~ 5 cycles asymptotic worst case
Efficiency? Well, its basically zero since we’re not doing any useful work, so ~ 0%
LDR % Assume PBS changes just after sampling, so latency = 1 cycle
STR % latency += 1 cycle
BL % latency += 100 cycles
B % latency += 1 cycle
Delay? So LDR (1, just missed) + STR (1) + BL (100) + B (1) + LDR (1) + STR (1) ~ 105 cycles asymptotic worst case
Efficiency? BL (100) / [LDR (1) + STR (1) + BL (100) + B (1)] ~ 100/103, so ~ 97%

## Slide 53: Polling trades off efficiency and responsiveness
mov r0, #0x4 % PBS MMIO address
mov r1, #0x5 % LED MMIO address
loop: ldr r2, [r0, #0] % Read value from switch [1 cycle]
str r2 [r1, #0] % Save value to LED [1 cycle]
bl do_some_work % Do some other work [100 cycles]
b loop % Repeat these steps [1 cycle]
Efficiency
Responsiveness
Efficiency
  Minimizing useless work
  Maximizing useful work
  Saving cycles & energy
Responsiveness
  Minimizing latency
  Tight event-action coupling
Can we do better? Yes!

## Slide 54: Level-triggered interrupts
Basics:
  Signaled by asserting a line low or high
  Interrupting device drives line low or high and holds it there until it is serviced
  Device deasserts when directed to or after serviced
    Requires some way to tell it to stop.
Sharing?
  Can share the line among multiple devices
  Often open-collector or HiZ
    Active devices assert the line, inactive devices let the line float
  Easy to share line w/o losing interrupts
  But servicing increases CPU load
  And requires CPU to keep cycling through to check
  Different ISR costs suggests careful ordering of ISR checks
  Can’t detect a new interrupt when one is already asserted
Notes: PCI originally mandated level-triggered due to this

## Slide 55: Edge-triggered interrupts
Basics:
  Signaled by a level *transition* (e.g. rising/falling edge)
  Interrupting device drives a pulse onto INT line
Sharing *is* possible
  INT line has a pull up and all devices are OC/OD.
  Could we miss an interrupt? Maybe...if close in time
  What happens if interrupts merge? Need one more ISR pass
  Easy to detect "new interrupts”
  Pitfalls: spurious edges, missed edges
Source of "lockups" in early computers
Notes: PCI originally mandated level-triggered due to this

## Slide 56: Basic interrupt processing
Stacking
  Automatically by CPU
  Maintains ABI semantics
  ISRs can be C functions
Vector Fetch
  We’ll see this next
Exit: update of SP, LR, PC
SP
xPSR
PC
LR
R12
R3
R2
R1
R0
Previous
stacked
data
Free
stack
space

Higher Addresses
Lower Addresses

The stack (PSP or MSP)

## Slide 57: NVIC/Interrupt configuration registers
ICTR Interrupt Controller Type Register (RW)
ISER Interrupt Set-Enable Register (RW)
ICER Interrupt Clear-Enable Register (RW)
ISPR Interrupt Set-Pending Register (RW)
ICPR Interrupt Clear-Pending Register (RW)
IABR Interrupt Active Bit Register (RO)
IPR Interrupt Priority Register (RW)
AIRC Application Interrupt and Reset Control
Notes: ICTR: shows the number of interrupt lines the NVIC supports (up to 240)
ISER/ICER: enable/disable external interrupts
ISPR/ICPR: Set and cleared by HW and/or SW
IABR: Set and cleared by hardware automatically (verify)
IPR: Sets priorities for the interrupts
AIRC: vector access key, priority group, reset request, etc.

## Slide 58: Enabling and disabling interrupt sources
Notes: Set corresponding bit to

## Slide 61: Pending interrupts
The normal case. Once Interrupt request is seen, processor puts it in
“pending” state even if hardware drops the request.
IPS is cleared by the hardware once we jump to the ISR.
This figure and those following are from The Definitive Guide to the ARM Cortex-M3, Section 7.4

## Slide 62
In this case, the processor never took the interrupt because we cleared the
IPS by hand (via a memory-mapped I/O register)

## Slide 65: Answer

## Slide 66: Interrupt pulses before entering ISR

## Slide 67: Answer

## Slide 69: Interrupt Priority
What do we do if several interrupts arrive simultaneously?
NVIC allows priorities for (almost) every interrupt
3 fixed highest priorities, up to 256 programmable priorities
  128 preemption levels
  Not all priorities have to be implemented by a vendor
  SmartFusion has 32 priority levels, i.e. 0x00, 0x08, … , 0xF8
Higher priority interrupts can pre-empt lower priorities
Priority can be sub-divided into priority groups
  Splits priority register into two halves, preempt priority & subpriority
  Preempt priority: indicates if an interrupt can preempt another
  Subpriority: used to determine which is served first if two interrupts of same group arrive concurrently

## Slide 70: Interrupt Priority (2)
Interrupt priority level registers
  Range: 0xE000E400 to 0xE000E4EF

## Slide 71: Preemption Priority and Subpriority

## Slide 72: PRIMASK, FAULTMASK, and BASEPRI registers
What if we quickly want to disable all interrupts?
Write 1 into PRIMASK to disable all interrupts except NMI
  MOV R0, #1
  MSR PRIMASK, R0 ; MSR and MRS are special instructions
Write 0 into PRIMASK to enable all interrupts
FAULTMASK is the same as PRIMASK, but it also blocks hard faults (priority = -1)
What if we want to disable all interrupts below a certain priority?
Write priority into BASEPRI register
  MOV R0, #0x60
  MSR BASEPRI, R0

## Slide 73: Masking

## Slide 74: Interrupt Service Routines
Automatic saving of registers upon exception
  PC, PSR, R0-R3, R12, LR
  This occurs over data bus
While data bus busy, fetch exception vector
  i.e. target address of exception handler
  This occurs over instruction bus
Update SP to new location
Update IPSR (low part of xPSR) with exception new #
Set PC to vector handler
Update LR to special value EXC_RETURN
Several other NVIC registers gets updated
Latency can be as short as 12 cycles (w/o mem delays)

## Slide 75: The xPSR register layout

## Slide 76: ARM interrupt summary
We’ve got a bunch of memory-mapped registers that control things (NVIC)
  Enable/disable individual interrupts
  Set/clear pending
  Interrupt priority and preemption
We’ve got to understand how the hardware interrupt lines interact with the NVIC
And how we figure out where to set the PC to point to for a given interrupt source.

## Slide 77: 1. NVIC registers (example)

## Slide 78: 1. More registers (example)

## Slide 79: 1. Yet another part of the NVIC registers!

## Slide 80: 2. How external lines interact with the NVIC
The normal case. Once Interrupt request is seen, processor puts it in
“pending” state even if hardware drops the request.
IPS is cleared by the hardware once we jump to the ISR.
This figure and those following are from The Definitive Guide to the ARM Cortex-M3, Section 7.4

## Slide 81: 3. How the hardware figures out what to set the PC to
g_pfnVectors:
.word _estack
.word Reset_Handler
.word NMI_Handler
.word HardFault_Handler
.word MemManage_Handler
.word BusFault_Handler
.word UsageFault_Handler
.word 0
.word 0
.word 0
.word 0
.word SVC_Handler
.word DebugMon_Handler
.word 0
.word PendSV_Handler
.word SysTick_Handler
.word WdogWakeup_IRQHandler
.word BrownOut_1_5V_IRQHandler
.word BrownOut_3_3V_IRQHandler
.............. (they continue)

## Slide 82: What happens when we return from an ISR?
Interrupt exiting process
  System restoration needed (different from branch)
  Special LR value could be stored (0xFFFFFFFx)
Tail chaining
  When new exception occurs
  But CPU handling another exception of same/higher priority
  New exception will enter pending state
  But will be executed before register unstacking
  Saving unnecessary unstacking/stacking operations
  Can reenter hander in as little as 6 cycles
Late arrivals (ok, so this is actually on entry)
  When one exception occurs and stacking commences
  Then another exception occurs before stacking completes
  And second exception of higher preempt priority arrives
  The later exception will be processed first

## Slide 83: What happens when we return from an ISR?
Interrupt exiting process
  System restoration needed (different from branch)
  Special LR value could be stored (0xFFFFFFFx)
Walkthrough a few examples, simplified system assumptions:
  5 Interrupt Levels (0-4)
  256 Priority Levels (0 Highest, 256 Lowest)
First time presenting, so errors in the animation are unintentional but may be present (lets find out together)

## Slide 84: Single Interrupt
Program
Interrupt on Level 4
Execution Time
HW
SW
0
0
0
0
0
4
0
Pending
0
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
8
10
5
3
6
0
1
2
3
4
Priority Table
Base Priority
256

## Slide 85: Single Interrupt
Program
Stack
Interrupt on Level 4
Execution Time
HW
SW
PC
PSR
LR
R0-R3, R12
1
0
0
0
0
4
0
Pending
0
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
8
10
5
3
6
0
1
2
3
4
Priority Table
6
Base Priority

## Slide 86: Single Interrupt
Program
ISR-LVL4
Stack
Interrupt on Level 4
Execution Time
HW
SW
Program
Stack
PC
PSR
LR
R0-R3, R12
0
0
0
0
0
4
0
Pending
1
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
ISR-LVL4
Stack
8
10
5
3
6
0
1
2
3
4
Priority Table
6
Base Priority

## Slide 87: Single Interrupt
Program
ISR-LVL4
Stack
Interrupt on Level 4
bx lr
Execution Time
HW
SW
PC
PSR
LR
R0-R3, R12
0
0
0
0
0
4
0
Pending
1
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
8
10
5
3
6
0
1
2
3
4
Priority Table
6
Base Priority

## Slide 88: Single Interrupt
Program
ISR-LVL4
Stack
Unstack
Interrupt on Level 4
bx lr
Execution Time
HW
SW
0
0
0
0
0
4
0
Pending
0
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
8
10
5
3
6
0
1
2
3
4
Priority Table
6
Base Priority

## Slide 89: Single Interrupt
Program
ISR-LVL4
Stack
Unstack
Program
Interrupt on Level 4
bx lr
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
0
0
0
0
0
4
0
Pending
0
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
256
Base Priority

## Slide 90: Nested Interrupts
  When new exception occurs
  And CPU handling another exception of lower priority (incoming request is higher priority)
  New exception will interrupt the current ISR
  Will generate a new ISR stack on the stack

## Slide 91: Nested Interrupt
Program
ISR-LVL4
Stack
Interrupt on Level 4
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
0
0
0
0
0
4
0
Pending
1
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
6
Interrupt on Level 3
PC
PSR
LR
R0-R3, R12
ISR-LVL4
Stack
Base Priority

## Slide 92: Nested Interrupt
Program
ISR-LVL4
Stack
Interrupt on Level 4
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
0
1
0
0
0
4
0
Pending
1
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
6
Interrupt on Level 3
Stack
PC
PSR
LR
R0-R3, R12
ISR-LVL4
Stack
PC
SP
LR
R0-R4, R12
Base Priority

## Slide 93: Nested Interrupt
Program
ISR-LVL4
Stack
Interrupt on Level 4
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
0
0
0
0
0
4
0
Pending
1
1
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
3
Interrupt on Level 3
ISR-LVL3
Stack
PC
PSR
LR
R0-R3, R12
ISR-LVL4
Stack
PC
PSR
LR
R0-R3, R12
ISR-LVL3
Stack
Base Priority

## Slide 94: Nested Interrupt
Program
ISR-LVL4
Stack
Unstack
Interrupt on Level 4
bx lr
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
0
0
0
0
0
4
0
Pending
1
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
6
Interrupt on Level 3
ISR-LVL3
Stack
PC
PSR
LR
R0-R3, R12
ISR-LVL4
Stack
Base Priority

## Slide 95: Nested Interrupt
Program
ISR-LVL4
Stack
Unstack
Interrupt on Level 4
bx lr
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
0
0
0
0
0
4
0
Pending
0
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
256
Interrupt on Level 3
ISR-LVL3
Stack
ISR-LVL4
Unstack
bx lr
Base Priority

## Slide 96: Tail Chaining
  When new exception occurs
  But CPU handling another exception of same/higher priority (incoming request is lower priority)
  New exception will enter pending state
  But will be executed before register unstacking
  Saving unnecessary unstacking/stacking operations
  Can reenter hander in as little as 6 cycles

## Slide 97: Tail-Chaining
Program
ISR-LVL4
Stack
Interrupt on Level 4
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
0
0
0
1
0
4
0
Pending
1
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
6
Interrupt on Level 1
PC
PSR
LR
R0-R3, R12
ISR-LVL4
Stack
Base Priority

## Slide 98: Tail-Chaining
Program
ISR-LVL4
Stack
Interrupt on Level 4
bx lr
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
0
0
0
1
0
4
0
Pending
0
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
6
Interrupt on Level 1
PC
PSR
LR
R0-R3, R12
Don’t Unstack
Base Priority

## Slide 99: Tail-Chaining
Program
ISR-LVL4
Stack
Interrupt on Level 4
bx lr
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
0
0
0
0
0
4
0
Pending
0
0
0
1
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
10
Interrupt on Level 1
ISR-LVL1
PC
PSR
LR
R0-R3, R12
ISR-LVL1
Stack
Base Priority

## Slide 100: Tail-Chaining
Program
ISR-LVL4
Stack
Program
Interrupt on Level 4
bx lr
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
0
0
0
0
0
4
0
Pending
0
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
256
Interrupt on Level 1
ISR-LVL1
Unstack
bx lr
Base Priority

## Slide 101: Late Arrival
Late arrivals (ok, so this is actually on entry)
  When one exception occurs and stacking commences
  Then another exception occurs before stacking completes
  And second exception of higher preempt priority arrives
  The later exception will be processed first

## Slide 102: Late Arrival
Program
Stack
Interrupt on Level 4
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
1
1
0
0
0
4
0
Pending
0
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
256
Interrupt on Level 3
PC
PSR
LR
R0-R3, R12
Once stacking complete, find vector for highest priority pending
Base Priority

## Slide 103: Late Arrival
Program
Stack
Interrupt on Level 4
bx lr
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
1
0
0
0
0
4
0
Pending
0
1
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
3
Interrupt on Level 3
ISR-LVL3
PC
PSR
LR
R0-R3, R12
ISR-LVL3
Stack
Base Priority

## Slide 104: Late Arrival
Program
ISR-LVL4
Stack
Program
Interrupt on Level 4
bx lr
Execution Time
HW
SW
8
10
5
3
6
0
1
2
3
4
Priority Table
0
0
0
0
0
4
0
Pending
0
0
0
0
0
4
0
Active
1
1
1
1
1
4
0
Enabled
Program
Stack
256
Interrupt on Level 3
ISR-LVL3
Unstack
bx lr
Tail Chaining used to service lower priority request
Base Priority

## Slide 105: Virtual Timers
You never have enough timers.
  Never.
So what are we going to do about it?
  How about we handle in software?

## Slide 106: Virtual Timers
Simple idea.
  Maybe we have 10 events we might want to generate.
    Just make a list of them and set the timer to go off for the first one.
      Do that first task, change the timer to interrupt for the next task.

## Slide 107: Problems?
Only works for “compare” timer uses.
Will result in slower ISR response time
  May not care, could just schedule sooner…

## Slide 108: Implementation Issues
Shared user-space/ISR data structure.
  Insertion happens at least some of the time in user code.
  Deletion happens in ISR.
    We need critical section (disable interrupt)
How do we deal with our modulo counter?
  That is, the timer wraps around.
  Why is that an issue?
What functionality would be nice?
  Generally one-shot vs. repeating events
  Might be other things desired though
What if two events are to happen at the same time?
  Pick an order, do both…

## Slide 109: Implementation Issues (continued)
What data structure?
  Data needs be sorted
    Inserting one thing at a time
  We always pop from one end
  But we add in sorted order.

## Slide 110: Data structures

## Slide 111: Some loose ends…glitches and all that

## Slide 112: Timing delays and propagation
Full adder (from Wikipedia)
Assume
  XOR delay = 0.2ns
  AND delay = 0.1ns
  OR delay = 0.1 ns
What is the worst case propagation delay for this circuit?
x
y
z

## Slide 113: Glitches
x
y
z
Full adder (from Wikipedia)
Consider the adjacent circuit diagram. Assuming the XOR gates have
a delay of 0.2ns while AND and OR gates have a delay of 0.1ns, fill in
the following chart.
Only selected causality
arrows shown…

## Slide 114: Glitching: a summary
When input(s) change
  The output can be wrong for a time
  However, that time is bounded
And more so, the output can change during this “computation time” even if the output ends up where it started!

## Slide 115: Effect of Glitches
Think back to EECS 370.
  Why don’t glitches cause errors?
  The trick is that the inputs all change at the same time
    In this case, the ID/EX registers all change some time shortly after the rising edge of the clock.
  And we’ve chosen the clock period such that the next edge doesn’t happen until the combinational logic has stopped glitching.
    In fact, we use the worst-case combinational logic delay in the whole system when determining the clock period!
Notes: Note the animation here. I didn’t want the text to show up on the printed slides.

## Slide 116: So, how can glitches hurt us?
There are a handful of places:
  Asynchronous resets
    If you’ve got a flip-flop that has an asynchronous reset (or “preset”) you need to be sure the input can’t glitch.
      That pretty much means you need a flip-flop driving the input (which means you probably should have used a sync. reset!)
  Clocks
    If you are using combinational logic to drive a clock, you are likely going to get extra clock edges.
Traditionally, CLR is used
to indicate async reset. “R”
or “reset” for sync. reset.
If clk is high and cond
glitches, you get extra
edges!

## Slide 117: Design rules
Thou shalt not use asynchronous resets
Thou shalt not drive a clock with anything other than a clock or directly off of a flip-flop’s output
X
X

## Slide 118: Really? Seriously?
People do use asynchronous resets and clock gating!
  Yep. And people use goto in C programs.
    Sometimes they are the right thing.
      But you have to think really hard about them to insure that they won’t cause you problems.
  Our “simple” bus used combinational logic for the clock
    Works because REQ goes low only after everything else has stopped switching
      So no glitch.
    Not fun to reason about…
Avoid unless you must
  Then think really carefully.

## Slide 119: Setup and hold time
The idea is simple.
  When the clock is changing if the data is also changing it is hard to tell what the data is.
    Hardware can’t always tell
      And you can get meta-stable behavior too (very unlikely but…)
  So we have a “guard band” around the clock rising time during which we don’t allow the data to change.
    See diagram. We call the time before the clock-edge “setup time” and the time after “hold time”
Notes: Using dropping erasers thing. Drop 2 erasers, ask which hit first. The point being that it can be hard to tell even though they didn’t happen at the same time (no two things do). Makes sense we want some type of band around when the clock is changing so that the data isn’t so we grab the right thing.

## Slide 120: Example: Fast and slow paths; impact of setup and hold time
Notes: From http://www.eecs.umich.edu/courses/eecs270/refs.html

## Slide 121: So what happens if we violate set-up or hold time?
Often just get one of the two values.
  And that often is just fine.
    Consider getting a button press from the user.
    If the button gets pressed at the same time as the clock edge, we might see the button now or next clock.
      Either is generally fine when it comes to human input.
  But bad things could happen.
    The flip-flop’s output might not settle out to a “0” or a “1”
      That could cause later devices to mess up.
    More likely, if that input is going to two places, one might see a “0” the other a “1”
Important: don’t feed an async input to multiple places!

## Slide 122: Example
A common thing to do is reset a state machine using a button.
  User can “reset” the system.
Because the button transition could violate set-up or hold time, some state bits of the state machine might come out of reset at different times.
  And you quickly end up at a wrong or illegal state.
Notes: Insert story about the E100 here.

## Slide 123: So…
Dealing with inputs not synchronized to our local clock is a problem.
  Likely to violate setup or hold time.
    That could lead to things breaking.
So we need a clock synchronization circuit.
  First flip-flop might have problems.
  Second should be fine.
  Sometimes use a third if really paranoid
    Safety-critical system for example.
Figure from http://www.eeweb.com/electronics-quiz/solving-metastability-design-issues, we use the same thing to deal with external inputs too!

## Slide 124: Design rules
Thou shalt use a clock synchronization circuit when changing clock domains or using unclocked inputs!

/* Synchonization of Asynchronous switch input */ always@(posedge clk) begin sw0_pulse[0] <= sw_port[0]; sw0_pulse[1] <= sw0_pulse[0]; sw0_pulse[2] <= sw0_pulse[1]; end
always @(posedge clk) SSELr <= {SSELr[1:0], SSEL};
Notes: Code from lab 3 and from http://www.fpga4fun.com/SPI2.html