## Slide 1: EECS 470
Tomasulo’s Algorithm
Lecture 4 – Winter 2024
Slides developed in part by Profs. Austin, Brehob, Falsafi, Hill, Hoe, Lipasti, Martin, Roth, Shen, Smith, Sohi, Tyson, Vijaykumar, and Wenisch of Carnegie Mellon University, Purdue University, University of Michigan, University of Pennsylvania, and University of Wisconsin.

## Slide 2: Announcements
Programming assignment #1 due today
Homework #2 posted by end of the day
  Due Friday 2/2
  Can do some of it now, and should be able to do all by Tuesday of next week.

## Slide 3: Readings
  H & P Chapter 3.4-3.5

## Slide 4: Basic Anatomy of an OoO Scheduler

## Slide 5: New Pipeline Terminology
In-order pipeline
  Often written as F,D,X,W (multi-cycle X includes M)
  Example pipeline: 1-cycle int (including mem), 3-cycle pipelined FP
regfile
D$
I$
B
P

## Slide 6: New Pipeline Diagram
Insn | D | X | W
ldf X(r1),f1 | c1 | c2 | c3
mulf f0,f1,f2 | c3 | c4+ | c7
stf f2,Z(r1) | c7 | c8 | c9
addi r1,4,r1 | c8 | c9 | c10
ldf X(r1),f1 | c10 | c11 | c12
mulf f0,f1,f2 | c12 | c13+ | c16
stf f2,Z(r1) | c16 | c17 | c18
Alternative pipeline diagram (we will see two approaches in class)
  Down: instructions executing over time
  Across: pipeline stages
  In boxes: the specific cycle of activity, for that instruction
  Basically: stages  cycles
  Convenient for out-of-order
Notes: Mention that we will examine this with two approaches…

## Slide 7: Anatomy of OoO: Instruction Buffer
Insn buffer (many names for this buffer)
  Basically: a bunch of latches for holding insns
  Candidate pool of instructions
Split D into two pieces
  Accumulate decoded insns in buffer in-order
  Buffer sends insns down rest of pipeline out-of-order
regfile
D$
I$
B
P
insn buffer
D2
D1

## Slide 8: Anatomy of OoO: Dispatch and Issue
Dispatch (D): first part of decode
  Allocate slot in insn buffer
    New kind of structural hazard (insn buffer is full)
  In order: stall back-propagates to younger insns
Issue (S): second part of decode
  Send insns from insn buffer to execution units
  Out-of-order: wait doesn’t back-propagate to younger insns
regfile
D$
I$
B
P
insn buffer
S
D

## Slide 9: Dispatch and Issue with Floating-Point
regfile
D$
I$
B
P
insn buffer
S
D
F-regfile
E/
E
+
E
+
E*
E*
E*

## Slide 10: Dynamic Scheduling Algorithms
  Register scheduler: scheduler driven by register dependences
Book covers two register scheduling algorithms
  Scoreboard: No register renaming  limited scheduling flexibility
  Tomasulo: Register renaming  more flexibility, better performance
  We focus on Tomasulo’s algorithm in the lecture
  No test questions on scoreboarding
    Do note that it is used in certain GPUs.
Big simplification in this lecture: memory scheduling
  Pretend register algorithm magically knows memory dependences
  A little more realism later in the term

## Slide 11: Key OoO Design Feature: Issue Policy and Issue Logic
Issue
  If multiple instructions are ready, which one to choose? Issue policy
    Oldest first? Safe
    Longest latency first? May yield better performance
  Select logic: implements issue policy
    Most projects use random.

## Slide 12: Eliminating False Dependencies with Register Renaming

## Slide 13: True Data dependencies
True data dependency
  RAW – Read after Write
    R1=R2+R3
    R4=R1+R5
True dependencies prevent reordering
  (Mostly) unavoidable
Dynamic execution
Hazards
Renaming

## Slide 14: False Data Dependencies
False or Name dependencies
  WAW – Write after Write
    R1=R2+R3
    R1=R4+R5
  WAR – Write after Read
    R2=R1+R3
    R1=R4+R5
False dependencies prevent reordering
  Can they be eliminated? (Yes, with renaming!)
Dynamic execution
Hazards
Renaming

## Slide 15: Data Dependency Graph: Simple example
R1=MEM[R2+0] // A
R2=R2+4 // B
R3=R1+R4 // C
MEM[R2+0]=R3 // D
RAW WAW WAR
A
D
C
B
Dynamic execution
Hazards
Renaming

## Slide 16: Data Dependency Graph: More complex example
R1=MEM[R3+4] // A
R2=MEM[R3+8] // B
R1=R1*R2 // C
MEM[R3+4]=R1 // D
MEM[R3+8]=R1 // E
R1=MEM[R3+12] // F
R2=MEM[R3+16] // G
R1=R1*R2 // H
MEM[R3+12]=R1 // I
MEM[R3+16]=R1 // J
A
E
D
C
B
H
F
G
J
I
RAW WAW WAR
Dynamic execution
Hazards
Renaming

## Slide 17
Eliminating False Dependencies
R1=MEM[R3+4] // A
R2=MEM[R3+8] // B
R1=R1*R2 // C
MEM[R3+4]=R1 // D
MEM[R3+8]=R1 // E
R1=MEM[R3+12] // F
R2=MEM[R3+16] // G
R1=R1*R2 // H
MEM[R3+12]=R1 // I
MEM[R3+16]=R1 // J
Well, logically there is no reason for F-J to be dependent on A-E. So…..
    ABFG
    CH
    DEIJ
  Should be possible.
But that would cause either C or H to have the wrong reg inputs
How do we fix this?
  Remember, the dependency is really on the name of the register
  So… change the register names!
A
E
D
C
B
H
F
G
J
I
Dynamic execution
Hazards
Renaming

## Slide 18: Register Renaming Concept
  The register names are arbitrary
  The register name only needs to be consistent between writes.
    R1= …..
    …. = R1 ….
    ….= … R1
    R1= ….
The value in R1 is “alive” from when the value is
written until the last read of that value.
Dynamic execution
Hazards
Renaming

## Slide 19: So after renaming, what happens to the dependencies?
P1=MEM[R3+4] //A
P2=MEM[R3+8] //B
P3=P1*P2 //C
MEM[R3+4]=P3 //D
MEM[R3+8]=P3 //E
P4=MEM[R3+12] //F
P5=MEM[R3+16] //G
P6=P4*P5 //H
MEM[R3+12]=P6 //I
MEM[R3+16]=P6 //J
A
E
D
C
B
H
F
G
J
I
RAW WAW WAR
Dynamic execution
Hazards
Renaming

## Slide 20: Register Renaming Approach
Every time an architected register is written we assign it to a physical register
  Until the architected register is written again, we continue to translate it to the physical register number
  Leaves RAW dependencies intact
It is really simple, let’s look at an example:
  Names: r1,r2,r3
  Locations: p1,p2,p3,p4,p5,p6,p7
  Original mapping: r1p1, r2p2, r3p3, p4–p7 are “free”
MapTable |  |  |  | FreeList |  | Orig. insns |  | Renamed insns
r1 | r2 | r3 |  |  |  |  |  | 
p1 | p2 | p3 |  | p4,p5,p6,p7 |  | add r2,r3,r1 |  | add p2,p3,p4
p4 | p2 | p3 |  | p5,p6,p7 |  | sub r2,r1,r3 |  | sub p2,p4,p5
p4 | p2 | p5 |  | p6,p7 |  | mul r2,r3,r3 |  | mul p2,p5,p6
p4 | p2 | p6 |  | p7 |  | div r1,4,r1 |  | div p4,4,p7
Dynamic execution
Hazards
Renaming

## Slide 21
R1=MEM[P7+4] // A
R2=MEM[R3+8] // B
R1=R1*R2 // C
MEM[R3+4]=R1 // D
MEM[R3+8]=R1 // E
R1=MEM[R3+12] // F
R2=MEM[R3+16] // G
R1=R1*R2 // H
MEM[R3+12]=R1 // I
MEM[R3+16]=R1 // J
P1=MEM[R3+4]
P2=MEM[R3+8]
P3=P1*P2
MEM[R3+4]=P3
MEM[R3+8]=P3
P4=MEM[R3+12]
P5=MEM[R3+16]
P6=P4*P5
MEM[R3+12]=P6
MEM[R3+16]=P6
Arch | V? | Physical
1 | 1 | 
2 | 1 | 
3 | 1 | 
Dynamic execution
Hazards
Renaming

## Slide 22: Tomasulo’s Scheduling Algorithm

## Slide 23: Tomasulo’s Scheduling Algorithm
Tomasulo’s algorithm
  Reservation stations (RS): instruction buffer
  Common data bus (CDB): broadcasts results to RS
  Register renaming: removes WAR/WAW hazards
First implementation: IBM 360/91 [1967]
  Dynamic scheduling for FP units only
  Bypassing
Our example: “Simple Tomasulo”
  Dynamic scheduling for everything, including load/store
  No bypassing
  5 RS: 1 ALU, 1 load, 1 store, 2 FP (3-cycle, pipelined)

## Slide 24: Tomasulo Data Structures
Reservation Stations (RS#)
  FU, busy, op, R: destination register name
  T: destination register tag (RS# of this RS)
  T1,T2: source register tags (RS# of RS that will produce value)
  V1,V2: source register values
Rename Table/Map Table/RAT
  T: tag (RS#) that will write this register
Common Data Bus (CDB)
  Broadcasts <RS#, value> of completed insns
Tags interpreted as ready-bits++
  T==0  Value is ready somewhere
  T!=0  Value is not ready, wait until CDB broadcasts T

## Slide 25: Simple Tomasulo Data Structures
  Insn fields and status bits
  Tags
  Values
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==

## Slide 26: Simple Tomasulo Pipeline
New pipeline structure: F, D, S, X, W
  D (dispatch)
    Structural hazard ? stall : allocate RS entry
  S (issue)
    RAW hazard ? wait (monitor CDB) : go to execute
  W (writeback)
    Write register (sometimes…), free RS entry
    W and RAW-dependent S in same cycle
    W and structural-dependent D in same cycle

## Slide 27: Tomasulo Dispatch (D)
Stall for structural (RS) hazards
  Allocate RS entry
  Input register ready ? read value into RS : read tag into RS
  Rename output register to RS # (represents a unique value “name”)
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==
Notes: Add note about when register file gets written… (when Map matches)

## Slide 28: Tomasulo Issue (S)
Wait for RAW hazards
  Read register values from RS
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==

## Slide 29: Tomasulo Execute (X)
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==

## Slide 30: Tomasulo Writeback (W)
Wait for structural (CDB) hazards
  if Map Table rename still matches ? Clear mapping, write result to regfile
  CDB broadcast to RS: tag match ? clear tag, copy value
  Free RS entry
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==
Notes: When does the register value get written back

## Slide 31: Register Renaming for Tomasulo
What in Tomasulo implements register renaming?
  Value copies in RS (V1, V2)
  Insn stores correct input values in its own RS entry
  Future insns can overwrite master copy in regfile, doesn’t matter
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==

## Slide 32: Value/Copy-Based Register Renaming
Tomasulo-style register renaming
  Called “value-based” or “copy-based”
  Names: architectural registers
  Storage locations: register file and reservation stations
    Values can and do exist in both
    Register file holds master (i.e., most recent) values
    RS copies eliminate WAR hazards
  Storage locations referred to internally by RS# tags
    Register table translates names to tags
    Tag == 0 value is in register file
    Tag != 0 value is not ready and is being computed by RS#
  CDB broadcasts values with tags attached
    So insns know what value they are looking at

## Slide 33: Simple Tomasulo Data Structures
RS:
  Status information
    R: Destination Register
    op: Operand (add, etc.)
  Tags
    T1, T2: source operand tags
  Values
    V1, V2: source operand values
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==
Map table (also RAT: Register Alias Table)
  Maps registers to tags
Regfile (also ARF: Architected Register File)
  Holds value of register if no value in RS

## Slide 34: Tomasulo Data Structures (Timing Free Example)
Map Table | 
Reg | T
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | R | op | T1 | T2 | V1 | V2
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
CDB | 
T | V
ARF | 
Reg | V
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Instruction
r0=r1*r2
r1=r2*r3
r2=r4+1
r1=r1+r1

## Slide 35: Tomasulo Data Structures (Timing Free Example #2)
Map Table | 
Reg | Tag
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
CDB | 
T | V
ARF | 
Reg | V
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Instruction
r0=r1*r2
r1=r0*r3
r0=r4+1
r1=r1+r0

## Slide 36: Questions
Where can we get values for a given instruction from?
  A)
  B)
When do we update the ARF? (This is a bit tricky)
  How do we know there isn’t anyone else who needs the value we overwrite?
What do we do on a branch mispredict?

## Slide 37: Example with timing
This set of slides is here for you to look over outside of class.
I generally prefer to not worry about timing issues too much at this point.
  They are implementation-specific and get more involved than I think is useful.
  That said, a number of students get the general case better if they have a specific case to look at.

## Slide 38: Example:Tomasulo with timing
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
addi r1,4,r1 |  |  |  | 
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | 
f2 | 
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | no |  |  |  |  |  | 
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V

## Slide 39: Tomasulo: Cycle 1
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
addi r1,4,r1 |  |  |  | 
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | 
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | f1 | - | - | - | [r1]
3 | ST | no |  |  |  |  |  | 
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate

## Slide 40: Tomasulo: Cycle 2
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 |  | 
mulf f0,f1,f2 | c2 |  |  | 
stf f2,Z(r1) |  |  |  | 
addi r1,4,r1 |  |  |  | 
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#4
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | f1 | - | - | - | [r1]
3 | ST | no |  |  |  |  |  | 
4 | FP1 | yes | mulf | f2 | - | RS#2 | [f0] | -
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate

## Slide 41: Tomasulo: Cycle 3
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | 
mulf f0,f1,f2 | c2 |  |  | 
stf f2,Z(r1) | c3 |  |  | 
addi r1,4,r1 |  |  |  | 
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#4
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | f1 | - | - | - | [r1]
3 | ST | yes | stf | - | RS#4 | - | - | [r1]
4 | FP1 | yes | mulf | f2 | - | RS#2 | [f0] | -
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate

## Slide 42: Tomasulo: Cycle 4
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 |  | 
stf f2,Z(r1) | c3 |  |  | 
addi r1,4,r1 | c4 |  |  | 
ldf X(r1),f1 |  |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#4
r1 | RS#1
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | yes | addi | r1 | - | - | [r1] | -
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | - | RS#4 | - | - | [r1]
4 | FP1 | yes | mulf | f2 | - | RS#2 | [f0] | CDB.V
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
RS#2 | [f1]
allocate
ldf finished (W)
clear f1 RegStatus
CDB broadcast
free
RS#2 ready 
grab CDB value

## Slide 43: Tomasulo: Cycle 5
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5 | 
stf f2,Z(r1) | c3 |  |  | 
addi r1,4,r1 | c4 | c5 |  | 
ldf X(r1),f1 | c5 |  |  | 
mulf f0,f1,f2 |  |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#4
r1 | RS#1
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | yes | addi | r1 | - | - | [r1] | -
2 | LD | yes | ldf | f1 | - | RS#1 | - | -
3 | ST | yes | stf | - | RS#4 | - | - | [r1]
4 | FP1 | yes | mulf | f2 | - | - | [f0] | [f1]
5 | FP2 | no |  |  |  |  |  | 
CDB | 
T | V
allocate

## Slide 44: Tomasulo: Cycle 6
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5+ | 
stf f2,Z(r1) | c3 |  |  | 
addi r1,4,r1 | c4 | c5 | c6 | 
ldf X(r1),f1 | c5 |  |  | 
mulf f0,f1,f2 | c6 |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | 
f2 | RS#4RS#5
r1 | RS#1
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | yes | addi | r1 | - | - | [r1] | -
2 | LD | yes | ldf | f1 | - | RS#1 | - | -
3 | ST | yes | stf | - | RS#4 | - | - | [r1]
4 | FP1 | yes | mulf | f2 | - | - | [f0] | [f1]
5 | FP2 | yes | mulf | f2 | - | RS#2 | [f0] | -
CDB | 
T | V
allocate
no D stall on WAW: scoreboard would
overwrite f2 RegStatus
anyone who needs old f2 tag has it

## Slide 45: Tomasulo: Cycle 7
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5+ | 
stf f2,Z(r1) | c3 |  |  | 
addi r1,4,r1 | c4 | c5 | c6 | c7
ldf X(r1),f1 | c5 | c7 |  | 
mulf f0,f1,f2 | c6 |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#5
r1 | RS#1
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | f1 | - | RS#1 | - | CDB.V
3 | ST | yes | stf | - | RS#4 | - | - | [r1]
4 | FP1 | yes | mulf | f2 | - | - | [f0] | [f1]
5 | FP2 | yes | mulf | f2 | - | RS#2 | [f0] | -
CDB | 
T | V
RS#1 | [r1]
addi finished (W)
clear r1 RegStatus
CDB broadcast
RS#1 ready 
grab CDB value
no W wait on WAR: scoreboard would
anyone who needs old r1 has RS copy
D stall on store RS: structural

## Slide 46: Tomasulo: Cycle 8
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5+ | c8
stf f2,Z(r1) | c3 | c8 |  | 
addi r1,4,r1 | c4 | c5 | c6 | c7
ldf X(r1),f1 | c5 | c7 | c8 | 
mulf f0,f1,f2 | c6 |  |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#5
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | yes | ldf | f1 | - | - | - | [r1]
3 | ST | yes | stf | - | RS#4 | - | CDB.V | [r1]
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | yes | mulf | f2 | - | RS#2 | [f0] | -
CDB | 
T | V
RS#4 | [f2]
mulf finished (W)
don’t clear f2 RegStatus
already overwritten by 2nd mulf (RS#5)
CDB broadcast
RS#4 ready 
grab CDB value

## Slide 47: Tomasulo: Cycle 9
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5+ | c8
stf f2,Z(r1) | c3 | c8 | c9 | 
addi r1,4,r1 | c4 | c5 | c6 | c7
ldf X(r1),f1 | c5 | c7 | c8 | c9
mulf f0,f1,f2 | c6 | c9 |  | 
stf f2,Z(r1) |  |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | RS#2
f2 | RS#5
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | - | - | - | [f2] | [r1]
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | yes | mulf | f2 | - | RS#2 | [f0] | CDB.V
CDB | 
T | V
RS#2 | [f1]
RS#2 ready 
grab CDB value
2nd ldf finished (W)
clear f1 RegStatus
CDB broadcast

## Slide 48: Tomasulo: Cycle 10
Insn Status |  |  |  | 
Insn | D | S | X | W
ldf X(r1),f1 | c1 | c2 | c3 | c4
mulf f0,f1,f2 | c2 | c4 | c5+ | c8
stf f2,Z(r1) | c3 | c8 | c9 | c10
addi r1,4,r1 | c4 | c5 | c6 | c7
ldf X(r1),f1 | c5 | c7 | c8 | c9
mulf f0,f1,f2 | c6 | c9 | c10 | 
stf f2,Z(r1) | c10 |  |  | 
Map Table | 
Reg | T
f0 | 
f1 | 
f2 | RS#5
r1 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 | ALU | no |  |  |  |  |  | 
2 | LD | no |  |  |  |  |  | 
3 | ST | yes | stf | - | RS#5 | - | - | [r1]
4 | FP1 | no |  |  |  |  |  | 
5 | FP2 | yes | mulf | f2 | - | - | [f0] | [f1]
CDB | 
T | V
free  allocate
stf finished (W)
no output register  no CDB broadcast

## Slide 49: Can We Add Bypassing?
Yes, but it’s more complicated than you might think
  Scheduler must work in advance of computation
  Requires knowledge of the latency of instructions, not always possible
  Accurate bypass is a key advancement in scheduling in last 10 years
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==

## Slide 50: Can We Add Superscalar?
Dynamic scheduling and multiple issue are orthogonal
  E.g., Pentium4: dynamically scheduled 5-way superscalar
  Two dimensions
    N: superscalar width (number of parallel operations)
    W: window size (number of reservation stations)
What do we need for an N-by-W Tomasulo?
  RS: N tag/value w-ports (D), N value r-ports (S), 2N tag CAMs (W)
  Select logic: WN priority encoder (S)
  MT: 2N r-ports (D), N w-ports (D)
  RF: 2N r-ports (D), N w-ports (W)
  CDB: N (W)
  Which are the expensive pieces?

## Slide 51: Superscalar Select Logic
Superscalar select logic: WN priority encoder
  Somewhat complicated (N2 logW)
  Can simplify using different RS designs
Split design
  Divide RS into N banks: 1 per FU?
  Implement N separate W/N1 encoders
  Simpler: N * logW/N
  Less scheduling flexibility
FIFO design [Palacharla+]
  Can issue only head of each RS bank
  Simpler: no select logic at all
  Less scheduling flexibility (but surprisingly not that bad)

## Slide 52: Dynamic Scheduling Summary
Dynamic scheduling: out-of-order execution
  Higher pipeline/FU utilization, improved performance
  Easier and more effective in hardware than software
    More storage locations than architectural registers
    Dynamic handling of cache misses
Instruction buffer: multiple F/D latches
  Implements large scheduling scope + “passing” functionality
  Split decode into in-order dispatch and out-of-order issue
    Stall vs. wait
Dynamic scheduling algorithms
  Scoreboard: no register renaming, limited out-of-order
  Tomasulo: copy-based register renaming, full out-of-order

## Slide 53: Are we done?
When can Tomasulo go wrong?
  Lack of instructions to choose from!!
    Need a really really really good branch predictor
  Exceptions!!
    No way to figure out relative order of instructions in RS

## Slide 54: And… a bit of terminology
Issue can be thought of as a two-stage process: “wakeup” and “select”.
  When the RS figures out it has it’s data and is ready to run it is said to have “woken up” and the process of doing so is called wakeup
    But there may be a structural hazard—no EX unit available for a given RS
      When?
  Thus, in addition to be woken up, and RS needs to be selected before it can go to the execute unit (EX stage).
    This process is called select