## Slide 1: EECS 470
Branches: Address prediction and recovery (And interrupt recovery too.)
Lecture 6 – Winter 2024
Slides developed in part by Profs. Austin, Brehob, Falsafi, Hill, Hoe, Lipasti, Martin, Roth, Shen, Smith, Sohi, Tyson, Vijaykumar, and Wenisch of Carnegie Mellon University, Purdue University, University of Michigan, University of Pennsylvania, and University of Wisconsin.

## Slide 2: Warning: Crazy times coming
P2 due today!
HW2 due on Friday 2/2
Will do group formation and project materials on Tuesday 2/6.
Group formation will be done in class on Thursday 2/8
P3 is due on Sunday 2/9
  It’s a lot of work (20 hours?)
Proposal is due on Tuesday 2/13
  It’s not a lot of work (1 hour?) to do the write-up, but you’ll need to meet with your group and discuss things.
    Don’t worry too much about getting this right. You’ll be allowed to change (we’ll meet the following Friday). Just a line in the sand. Will discuss on 2/6.
HW3 is due on Wednesday 2/14. No late homework. Answers posted right after it’s due!
Midterm is on Thursday 2/15 in the evening
  Review session over that weekend (date/time TBA)
  Q&A in class 2/15
  Best way to study is look at old exams (posted on-line later this week)
20 minute proposal meetings on Friday 2/16 rather than lab

## Slide 4: Announcements:
Combining Branch Predictors, S. McFarling, WRL Technical Note TN-36, June 1993.
  On the website
  Part of HW2.
  Expect a (likely brief) question on the midterm.

## Slide 5: Last time:
Started on branch predictors
  Branch prediction consists of
    Branch taken predictor
    Address predictor
    Mis-predict recovery.
  Discussed direction predictors and started looking at some variations

## Slide 6: Today
Predictors
    Bimodal
    Local history predictor
    Global history predictor
    Gshare
    Tournament
      Do detailed example
Start on the “P6 scheme”

## Slide 7: What are the limitations of Tomasulo’s Algorithm?
Branches are a pain.
Instructions that might throw an exception are a pain.

## Slide 8: Using history—bimodal
1-bit history (direction predictor)
  Remember the last direction for a branch
branchPC
NT
T

## Slide 9: Using history—bimodal
2-bit history (direction predictor)
branchPC
SN
NT
T
ST

## Slide 10: Using History Patterns
~80 percent of branches are either heavily TAKEN or heavily NOT-TAKEN
For the other 20%, we need to look a patterns of reference to see if they are predictable using a more complex predictor
Example: gcc has a branch that flips each time
T(1) NT(0) 10101010101010101010101010101010101010

## Slide 11: Local history
branchPC
NT
T
10101010
Pattern History
Table
Branch History
Table
What is the prediction
for this BHT 10101010?
When do I update the tables?

## Slide 12: Local history
branchPC
NT
T
01010101
Pattern History
Table
Branch History
Table
On the next execution of this
branch instruction, the branch
history table is 01010101,
pointing to a different pattern
What is the accuracy of a flip/flop branch 0101010101010…?

## Slide 13: Global history
01110101
Pattern History
Table
Branch History
Register
if (aa == 2)
aa = 0;
if (bb == 2)
bb = 0;
if (aa != bb) { …
How can branches interfere with each other?

## Slide 14: Relative performance (Spec ‘89)

## Slide 15: Gshare predictor
Ref: Combining Branch Predictors
branchPC
01110101
Pattern History
Table
Branch History
Register
xor
Must read!

## Slide 16: Hybrid predictors
Local predictor
(e.g. 2-bit)
Global/gshare predictor
(much more state)
Prediction
1
Prediction
2
Selection table
(2-bit state machine)
How do you select which predictor to use?
How do you update the various predictor/selector?
Prediction

## Slide 17: “Trivial” example: Tournament Branch Predictor
Local
  8-entry 3-bit local history table indexed by PC
  8-entry 2-bit up/down counter indexed by local history
Global
  8-entry 2-bit up/down counter indexed by global history
Tournament
  8-entry 2-bit up/down counter indexed by PC

## Slide 18
Tournament selector 00=local, 11=global | 
ADR[4:2] | Pred. state
0 | 00
1 | 01
2 | 00
3 | 10
4 | 11
5 | 00
6 | 11
7 | 10
Local predictor 1st level table (BHT) 0=NT, 1=T | 
ADR[4:2] | History
0 | 001
1 | 101
2 | 100
3 | 110
4 | 110
5 | 001
6 | 111
7 | 101
Local predictor 2nd level table (PHT) 00=NT, 11=T | 
History | Pred. state
0 | 00
1 | 11
2 | 10
3 | 00
4 | 01
5 | 01
6 | 11
7 | 11
Global predictor table 00=NT, 11=T | 
History | Pred. state
0 | 11
1 | 10
2 | 00
3 | 00
4 | 00
5 | 11
6 | 11
7 | 00
Branch
History
Register

## Slide 19
Tournament selector 00=local, 11=global | 
ADR[4:2] | Pred. state
0 | 00
1 | 01
2 | 00
3 | 10
4 | 11
5 | 00
6 | 11
7 | 10
Local predictor 1st level table (BHT) 0=NT, 1=T | 
ADR[4:2] | History
0 | 001
1 | 101
2 | 100
3 | 110
4 | 110
5 | 001
6 | 111
7 | 101
Local predictor 2nd level table (PHT) 00=NT, 11=T | 
History | Pred. state
0 | 00
1 | 11
2 | 10
3 | 00
4 | 01
5 | 01
6 | 11
7 | 11
Global predictor table 00=NT, 11=T | 
History | Pred. state
0 | 11
1 | 10
2 | 00
3 | 00
4 | 00
5 | 11
6 | 11
7 | 00
r1=2, r2=6, r3=10, r4=12, r5=4
Address of joe =0x100 and each instruction is 4 bytes.
Branch History Register = 110
joe: add r1 r2 r3
beq r3 r4 next
bgt r2 r3 skip // if r2>r3 branch
lw r6 4(r5)
add r6 r8 r8
skip: add r5 r2 r2
bne r4 r5 joe
next: noop

## Slide 20: Overriding Predictors
Big predictors are slow, but more accurate
Use a single cycle predictor in fetch
Start the multi-cycle predictor
  When it completes, compare it to the fast prediction.
    If same, do nothing
    If different, assume the slow predictor is right and flush pipline.
Advantage: reduced branch penalty for those branches mispredicted by the fast predictor and correctly predicted by the slow predictor

## Slide 21
Address
Prediction

## Slide 22: BTB (Chapter 3.9)
Branch Target Buffer
  Addresses predictor
  Lots of variations
Keep the target of “likely taken” branches in a buffer
  With each branch, associate the expected target.

## Slide 23
Branch PC | Target address
0x05360AF0 | 0x05360000
… | …
… | …
… | …
… | …
… | …
BTB indexed by current PC
  If entry is in BTB fetch target address next
Generally set associative (too slow as FA)
Often qualified by branch taken predictor

## Slide 24: So…
BTB lets you predict target address during the fetch of the branch!
If BTB gets a miss, pretty much stuck with not-taken as a prediction
  So limits prediction accuracy.
Can use BTB as a predictor.
  If it is there, predict taken.
Replacement is an issue
  LRU seems reasonable, but only really want branches that are taken at least a fair amount.
What branches will a BTB struggle with?
  How to address that?

## Slide 25: Pipeline recovery is pretty simple
Squash and restart fetch with right address
  Just have to be sure that nothing has “committed” its state yet.
In our 5-stage pipe, state is only committed during MEM (for stores) and WB (for registers)

## Slide 26: Tomasulo’s
Recovery seems really hard
  What if instructions after the branch finish after we find that the branch was wrong?
    This could happen. Imagine
      R1=MEM[R2+0]
      BEQ R1, R3 DONE  Predicted not taken
      R4=R5+R6
  So we have to not speculate on branches or not let anything pass a branch
    Which is really the same thing.
    Branches become serializing instructions.
      Note that can be executing some things before and after the branch once branch resolves.

## Slide 27: What we need is:
Some way to not commit instructions until all branches before it are committed.
  Just like in the pipeline, something could have finished execution, but not updated anything “real” yet.

## Slide 28
Interrupt!!!

## Slide 29: Interrupts
These have a similar problem.
  If we can execute out-of-order a “slower” instruction might not generate an interrupt until an instruction in front of it has finished.
This sounds like the end of out-of-order execution
  I mean, if we can’t finish out-of-order, isn’t this pointless?

## Slide 30: Exceptions and Interrupts
Exception Type | Sync/Async | Maskable? | Restartable?
I/O request | Async | Yes | Yes
System call | Sync | No | Yes
Breakpoint | Sync | Yes | Yes
Overflow | Sync | Yes | Yes
Page fault | Sync | No | Yes
Misaligned access | Sync | No | Yes
Memory Protect | Sync | No | Yes
Machine Check | Async/Sync | No | No
Power failure | Async | No | No

## Slide 31: Precise Interrupts
Implementation approaches
  Don’t
    E.g., Cray-1
  Buffer speculative results
    E.g., P4, Alpha 21264
    History buffer
    Future file/Reorder buffer
Instructions
Completely
Finished
No Instruction
Has Executed
At All
PC
Precise State
Speculative State

## Slide 32: Precise Interrupts via the Reorder Buffer
MEM
@ Alloc
  Allocate result storage at Tail
@ Sched
  Get inputs (ROB T-to-H then ARF)
  Wait until all inputs ready
@ WB
  Write results/fault to ROB
  Indicate result is ready
@ CT
  Wait until inst @ Head is done
  If fault, initiate handler
  Else, write results to ARF
  Deallocate entry from ROB
IF
ID
Alloc
Sched
EX
ROB
CT
Head
Tail
PC
Dst regID
Dst value
Except?
Reorder Buffer (ROB)
  Circular queue of spec state
  May contain multiple definitions of same register
In-order
In-order
Any order
ARF

## Slide 33: Reorder Buffer Example
Code Sequence
f1 = f2 / f3
r3 = r2 + r3
r4 = r3 – r2
Initial Conditions
- reorder buffer empty
- f2 = 3.0
- f3 = 2.0
- r2 = 6
- r3 = 5
ROB
Time
H
T
regID: f1
result: ?
Except: ?
H
T
regID: f1
result: ?
Except: ?
regID: r3
result: ?
Except: ?
H
T
regID: f1
result: ?
Except: ?
regID: r3
result: 11
Except: N
regID: r4
result: ?
Except: ?
r3
regID: r8
result: 2
Except: n
regID: r8
result: 2
Except: n
regID: r8
result: 2
Except: n

## Slide 34: Reorder Buffer Example
Code Sequence
f1 = f2 / f3
r3 = r2 + r3
r4 = r3 – r2
Initial Conditions
- reorder buffer empty
- f2 = 3.0
- f3 = 2.0
- r2 = 6
- r3 = 5
ROB
Time
H
T
regID: f1
result: ?
Except: ?
regID: r3
result: 11
Except: n
regID: r4
result: 5
Except: n
H
T
regID: f1
result: ?
Except: y
regID: r3
result: 11
Except: n
regID: r4
result: 5
Except: n
regID: r8
result: 2
Except: n
regID: r8
result: 2
Except: n
H
T
regID: f1
result: ?
Except: y
regID: r3
result: 11
Except: n
regID: r4
result: 5
Except: n

## Slide 35: Reorder Buffer Example
Code Sequence
f1 = f2 / f3
r3 = r2 + r3
r4 = r3 – r2
Initial Conditions
- reorder buffer empty
- f2 = 3.0
- f3 = 2.0
- r2 = 6
- r3 = 5
ROB
Time
H
T
H
T
first inst
of fault
handler

## Slide 36: There is more complexity here
Rename table needs to be cleared
  Everything is in the ARF
  Really do need to finish everything which was before the faulting instruction in program order.
What about branches?
  Would need to drain everything before the branch.
    Why not just squash everything that follows it?

## Slide 37: And while we’re at it…
Does the ROB replace the RS?
  Is this a good thing? Bad thing?

## Slide 38: ROB
ROB
  ROB is an in-order queue where instructions are placed.
  Instructions complete (retire) in-order
  Instructions still execute out-of-order
  Still use RS
    Instructions are issued to RS and ROB at the same time
    Rename is to ROB entry, not RS.
    When execute done instruction leaves RS
  Only when all instructions in before it in program order are done does the instruction retire.

## Slide 39: Adding a Reorder Buffer

## Slide 40: Tomasulo Data Structures (Timing Free Example)
Map Table | 
Reg | Tag
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Reservation Stations (RS) |  |  |  |  |  |  |  | 
T | FU | busy | op | RoB | T1 | T2 | V1 | V2
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
CDB | 
T | V
ARF | 
Reg | V
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Instruction
r0=r1*r2
r1=r2*r3
Branch if r1=0
r0=r1+r1
r2=r2+1
Reorder Buffer (RoB) |  |  |  |  |  |  | 
RoB Number | 0 | 1 | 2 | 3 | 4 | 5 | 6
Dest. Reg. |  |  |  |  |  |  | 
Value |  |  |  |  |  |  | 

## Slide 41: Review Questions
Could we make this work without a RS?
  If so, why do we use it?
Why is it important to retire in order?
Why must branches wait until retirement before they announce their mispredict?
  Any other ways to do this?

## Slide 42: More review questions
What is the purpose of the RoB?
Why do we have both a RoB and a RS?
  Yes, that was pretty much on the last page…
Misprediction
  When to we resolve a mis-prediction?
  What happens to the main structures (RS, RoB, ARF, Rename Table) when we mispredict?
What is the whole purpose of OoO execution?

## Slide 43: Can We Add Superscalar?
Dynamic scheduling and multiple issue are orthogonal
  E.g., Pentium4: dynamically scheduled 5-way superscalar
  Two dimensions
    N: superscalar width (number of parallel operations)
    W: (number of reservation stations)
What do we need for an N-by-W Tomasulo?
  RS: N tag/value w-ports (D), N value r-ports (S), 2N tag CAMs (W)
  Select logic: WN priority encoder (S)
  MT: 2N read-ports (D), N write-ports (D)
  RF: 2N read-ports (D), N write-ports (W)
  CDB: N (W)
  Which are the expensive pieces?

## Slide 44: Superscalar Select Logic
Superscalar select logic: WN priority encoder
  Somewhat complicated (N2 logW)
  Can simplify using different RS designs
Split design
  Divide RS into N banks: 1 per FU?
  Implement N separate W/N1 encoders
  Simpler: N * logW/N
  Less scheduling flexibility
FIFO design [Palacharla+]
  Can issue only head of each RS bank
  Simpler: no select logic at all
  Less scheduling flexibility (but surprisingly not that bad)