## Slide 1: EECS 470
RS/ROB examples
True Physical Registers?
Project
Lecture 8 – Winter 2024
Slides developed in part by Profs. Austin, Brehob, Falsafi, Hill, Hoe, Lipasti, Martin, Roth, Shen, Smith, Sohi, Tyson, Vijaykumar, and Wenisch of Carnegie Mellon University, Purdue University, University of Michigan, University of Pennsylvania, and University of Wisconsin.

## Slide 2: Today
RS/ROB
  A bit more detail
True physical registers: Removing the ARF
  How and why
  Probably will only get started on this, we’ll see.
Project discussion
  Help me to stop the above at 1pm.

## Slide 3: Reminder
In the original Tomasulo’s algorithm you should only update the ARF if you overwrite the data in the RAT.
In the P6 scheme you always write to the ARF.

## Slide 4: Tomasulo Data Structures (Timing Free Example, “P6 scheme”)
Map Table | 
Reg | Tag
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Reservation Stations (RS) |  |  |  |  |  |  |  | 
T | FU | busy | op | RoB | T1 | T2 | V1 | V2
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
CDB | 
T | V
ARF | 
Reg | V
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Instruction
r0=r1*r2
r1=r2*r3
Branch if r1=0
r0=r1+r1
r2=r2+1
Reorder Buffer (RoB) |  |  |  |  |  |  | 
RoB Number | 0 | 1 | 2 | 3 | 4 | 5 | 6
Dest. Reg. |  |  |  |  |  |  | 
Value |  |  |  |  |  |  | 

## Slide 5: Review Questions
Could we make this work without the RS?
  If so, why do we do that?
Why is it important to retire in order?
Why must branches wait until retirement before they announce their mispredict?
  Any other ways to do this?

## Slide 6: More review questions
What is the purpose of the RoB?
Why do we have both a RoB and a RS?
  Yes, that was pretty much on the last page…
Misprediction
  When to we resolve a mis-prediction?
  What happens to the main structures (RS, RoB, ARF, Rename Table) when we mispredict?
What is the whole purpose of OoO execution?

## Slide 7: And yet more review questions!
What is the purpose of the RoB?
Why do we have both a RoB and a RS?
Misprediction
  When to we resolve a mis-prediction?
  What happens to the main structures (RS, RoB, ARF, Rename Table) when we mispredict?
What is the whole purpose of OoO execution?

## Slide 8: When an instruction is dispatched how does it impact each major structure?
Rename table?
ARF?
RoB?
RS?

## Slide 9: When an instruction completes execution how does it impact each major structure?
Rename table?
ARF?
RoB?
RS?

## Slide 10: When an instruction retires how does it impact each major structure?
Rename table?
ARF?
RoB?
RS?

## Slide 11: Topic change
Why on earth are we doing this?
  Why do we think it helps?
Homework 2 problems 5 and 6 made the argument.
  Only need to obey true data dependencies.
    Huge speedup potential.

## Slide 12: Optimizing CPU Performance
Golden Rule: tCPU = Ninst*CPI*tCLK
Given this, what are our options
  Reduce the number of instructions executed
  Reduce the cycles to execute an instruction
  Reduce the clock period
Our first focus: Reducing CPI
  Approach: Instruction Level Parallelism (ILP)

## Slide 13: Why ILP?
Vs.
Requirements
  Parallelism
  Large window
  Limited control deps
  Eliminate “false” deps
  Find run-time deps

## Slide 14: How Much ILP is There? (Chapter 3.10)

## Slide 15: How Large Must the “Window” Be?

## Slide 16: ALU Operation GOOD, Branch BAD
Expected Number of Branches
Between Mispredicts
E(X) ~ 1/(1-p)
E.g., p = 95%, E(X) ~ 20 brs, 100-ish insts

## Slide 17: How Accurate are Branch Predictors?

## Slide 18: Impact of Physical Storage Limitations
Each instruction “in flight” must have storage for its result
  Really worse than this because of mispeculation…

## Slide 19: Registers GOOD, Memory BAD
Benefits of registers
  Well described deps
  Fast access
  Finite resource
Memory loses these benefits for flexibility
  *p = …
  *q = …
  … = *p
?

## Slide 20: “Bottom Line” for an Ambitious Design

## Slide 21: P6 reviewed
Steps are:
  Dispatch to the OoO system
  Issue to functional units
    Wakeup
    Select
  Complete Execute
  Retire

## Slide 22: We added a Reorder Buffer

## Slide 23: Let’s lose the ARF! (R10K scheme)
Why?
  Currently have two structures that may hold values (ROB and ARF)
  Need to write back to the ARF after every instruction!
Other motivations?
  ROB currently holds result (which needs to be accessible to all) as well as other data (PC, etc.) which does not.
    So probably two separate structures anyways
  Many ROB entry result fields are unused (stores, branches)

## Slide 24: Physical Register file Version 1.0
Keep a “Physical register file”
  If you want to get the ARF back you need to use the RAT.
But the RAT has speculative information in it!
  We need to be able to undo the speculative work!
    How?

## Slide 25: How?
Remove
  The value field of the ROB
  The whole ARF
Add
  A “retirement RAT” (RRAT)
  A “Physical Register File” (PRF)
Actions:
  When you finish executing, send data to the PRF
  When you retire, update the RRAT as if you were dispatching and updating the RAT.
  (Other stuff we need to think about goes here.)
  On a mis-predict, update the RAT with the RRAT when squashing.

## Slide 26: RAT/RRAT Example
AR | PR
0 | 1
1 | 2
2 | 3
3 | 4
4 | 10
Assembly
R1=R2*R3
R3=R1+R3
RAT
AR | PR
0 | 1
1 | 2
2 | 3
3 | 4
4 | 10
RRAT

## Slide 27: RAT/RRAT Example
AR | PR
0 | 1
1 | 0
2 | 3
3 | 5
4 | 10
In-flight
Assembly
R1=R2*R3
R3=R1+R3
Renamed
P0=P3*P4
P5=P0+P4
RAT
AR | PR
0 | 1
1 | 2
2 | 3
3 | 4
4 | 10
RRAT

## Slide 28: This seems sorta okay but…
There seem to be some problems
  When can I free a physical register?
  If I’m writing to the physical register file at execute doesn’t that mean I committing at that point?
  How do I squash instructions?
  How do I recover architected state in the event of an exception?

## Slide 29: Freedom
Freeing the PRF
  How long must we keep each PRF entry?
    Until we are sure no one else will read it before the corresponding Architected Register is again written.
    Once the instruction overwriting the Architected Register commits we are certain safe.
  So free the PR when the instruction which overwrites it commits.
    In other words: when an instruction commits, it frees the PR it overwrites in the RRAT.
We could do better (?)
  The value is dead once it is no longer needed.
    Right now waiting until the AR is overwritten…
  Freeing earlier would reduce the number of PRs needed.
  But unclear how to do given speculation and everything else.

## Slide 30: Sidebar
One thing that must happen with the PRF is that a “free list” must exist letting the processor know which physical registers are available.
  Maintaining these free lists can be a pain!

## Slide 31
A: R1=MEM[R2+0]
B: R2=R3/R1
C: R3=R2+R0
D: Branch (if R1!=0)
E: R3=R1+R3
F: R3=R3+R0
G: R3=R3+19
H: R1=R7+R6
AR | Target
0 | 
1 | 
2 | 
3 | 
RRAT
AR | Target
0 | 4
1 | 2
2 | 7
3 | 1
RAT
RoB
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
3 | 2 | 44 | 56 | 3 | 66 | 7 | 11 | 8 | 20
PRF

## Slide 32: Resolving Branches Early: A variation
Keep a RAT copy for each branch in a RS!
  If mis-predict, can recover RAT quickly.
  Free lists also

## Slide 33: Project Overview
Grade breakdown
  22 points: Basics
    Out-of-order and something works
  20 points: Correctness
    Measured by how many tests you pass.
  17 points: Advanced features
  20 points: Performance
    Measured against your peers and previous semesters.
  10 points: Analysis
    Measuring something interesting. Ideally the impact of an advanced feature.
  6 points: Documentation
    You’ll do this at the end, don’t worry about it now.
  3 points: Milestone 1
    You’ll turn in some self-testing code. We’ll see if it does a good job.
  2 points: Peer feedback
    Do it on time & take it seriously you’ll get these points.

## Slide 34: Advanced features
17 points of advanced feature stuff.
  We suggest you consider one big thing in the core and a few small things outside of the core.
    Superscalar execution (3-way*, arbitrary **)
    Simultaneous Multi-threading (SMT) ***
    Multi-core with a shared, coherent and consistent write-back L2 cache. ***
    Exception handling?
    Early branch resolution (before the branch hits the head of the RoB)
    Multi-path execution on low-confidence branches (this may not help performance much…)

## Slide 35: Non-core features
Much of this we haven’t covered yet.
Better caches
  Associative, longer cache lines, etc.
  Non-blocking caches
    Harder than it looks
Better predictors
  Gshare, tournament, etc.
Prefetching

## Slide 36: Psuedo-core features
Adding instructions
  Say cmov
    This probably involves rewriting at least one benchmark.
Checkers
  Tricky.

## Slide 37: Wacky features
Think of something interesting and run with it.
  We’ve had weird schedulers for EX units and other things..

## Slide 38: Performance
Simple measure of how long it takes to finish a program.
  Doesn’t include flushing caches etc.
  Only get credit for right answers.
    If you don’t synthisize, we can’t know your clock period, so few if any points here.
You’d like to pick your features so you double-dip.
  Hint: Prefetching instructions is good.

## Slide 39: Analysis
Think about what you want to measure.
  Impact of a better cache?
  How full your RoB is?
  How much your early branch resolution helps.
Do a good job grabbing the data.
  Be sure you can distinguish testbenches that are good for measuring performance vs. those that are good for correctness!

## Slide 40: Report
Only thing to think about now is that we like things which show us how a feature works.
  So having your debug data be readable could be handy.

## Slide 41: Forming teams
We’ll post a signup sheet for teams tomorrow.
Teams are groups of 5
  We may have one group of 6?
We’ll finish about 5 minutes early on Thursday to finish team formation.