## Slide 1: EECS 470
R10K scheme, Tclk
Lecture 9 – Winter 2024
Slides developed in part by Profs. Austin, Brehob, Falsafi, Hill, Hoe, Lipasti, Martin, Roth, Shen, Smith, Sohi, Tyson, Vijaykumar, and Wenisch of Carnegie Mellon University, Purdue University, University of Michigan, University of Pennsylvania, and University of Wisconsin.

## Slide 2: Warning: Crazy times coming
P3 is due on Sunday (2/9)
  It’s a lot of work (20 hours?)
Proposal is due on Tuesday (2/13)
  It’s not a lot of work (1 hour?) to do the write-up, but you’ll need to meet with your group and discuss things.
    Don’t worry too much about getting this right. You’ll be allowed to change. Just a line in the sand. Will discuss on Friday (2/16).
HW3 is due on Wednesday (2/14)
  It’s a fair bit of work (4 hours?)
  Answers will be posted right after it’s due, no late assignments!

## Slide 3: Warning: Crazy times coming
P3 is due on Sunday (2/9)
  It’s a lot of work (20 hours?)
Proposal is due on Tuesday (2/13)
  It’s not a lot of work (1 hour?) to do the write-up, but you’ll need to meet with your group and discuss things.
    Don’t worry too much about getting this right. You’ll be allowed to change. Just a line in the sand. Will discuss on Friday (2/16).
HW3 is due on Wednesday (2/14)
  It’s a fair bit of work (4 hours?)
  Answers will be posted right after it’s due, no late assignments!
Midterm is on Thursday 2/15, 7-9pm
  Open book, open notes. No computers, phones, etc.
  Exam Q&A, Monday 2/12 7-8:30pm, Tuesday 6-8:30pm
    Print exams and bring them.
  Q&A in class Thursday 2/15
  Best way to study is look at old exams (on website)
15 minute group meetings on Friday 2/16 (rather than inlab)

## Slide 4: Let’s lose the ARF!
Why?
  Currently have two structures that may hold values (ROB and ARF)
  Need to write back to the ARF after every instruction!
Other motivations?
  ROB currently holds result (which needs to be accessible to all) as well as other data (PC, etc.) which does not.
    So probably two separate structures anyways
  Many ROB entry result fields are unused (stores, branches)

## Slide 5: Physical Register file Version 1.0
Keep a “Physical register file”
  If you want to get the ARF back you need to use the RAT.
But the RAT has speculative information in it!
  We need to be able to undo the speculative work!
    How?

## Slide 6: How?
Remove
  The value field of the ROB
  The whole ARF
Add
  A “Retirement RAT1” (RRAT) that is updated by retiring instructions the same way the RAT is by issuing instructions
Actions:
  When you finish execution, update the PRF as well as the ROB (ROB just gets “done” message now)
  When you retire, update the RRAT
  (Other stuff we need to think about goes here.)
1http://www.ecs.umass.edu/ece/koren/ece568/papers/Pentium4.pdf

## Slide 7: Example
AR | PR
0 | 1
1 | 2
2 | 3
3 | 4
4 | 10
Dispatch:
Assembly
R1=R2*R3
R3=R1+R3
RAT
AR | PR
0 | 1
1 | 2
2 | 3
3 | 4
4 | 10
RRAT

## Slide 8: Example
AR | PR
0 | 1
1 | 0
2 | 3
3 | 5
4 | 10
In-flight
Assembly
R1=R2*R3
R3=R1+R3
Renamed
P0=P3*P4
P5=P0+P4
RAT
AR | PR
0 | 1
1 | 2
2 | 3
3 | 4
4 | 10
RRAT

## Slide 9: Resolving Branches
RRAT
  On mispredict at head of queue copy retirement RAT into RAT.
Early resolution? (briefly)
  BRAT
    Keep a RAT copy for each branch in a RS!
      If mispredict can recover RAT quickly.
      ROB easy to fix, RS’s a bit harder.

## Slide 10: Freedom
Freeing the PRF
  How long must we keep each PRF entry?
    Until we are sure no one else will read it before the corresponding AR is again written.
    Once the instruction overwriting the Arch. Register commits we are certain safe.
  So free the PR when the instruction which overwrites it commits.
    In other words: when an instruction commits, Free the thing overwritten in the RRAT.
We could do better
  Freeing earlier would reduce the number of PRs needed.
  But unclear how to do given speculation and everything else.

## Slide 11: Sidebar
One thing that must happen with the PRF as well as the RS is that a “free list” must exist letting the processor know which resources are available.
  Maintaining these free lists can be a pain!
    Let’s talk a bit about how one would do this.

## Slide 12: R10K scheme
What are we doing?
  Removing the ARF
  Removing the value field of the RoB.
  Adding a Physical Register File (~sum ARF and RoB)
  Adding a Retirement RAT (RRAT)

## Slide 13
A: R1=MEM[R2+0]
B: R2=R1/R3
C: R3=R2+R0
D: Branch (R1==0)
E: R3=R1+R3
F: R3=R3+R0
G: R3=R3+19
H: R1=R7+R6
AR | Target
0 | 
1 | 
2 | 
3 | 
RRAT
AR | Target
0 | 4
1 | 2
2 | 7
3 | 1
RAT
RoB
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
3 | 2 | 44 | 55 | 3 | 66 | 7 | 11 | 8 | 20
PRF

## Slide 14: Alternative option (v0.9?)
Use “back pointers” instead of RRAT.
  Record, in the ROB, which value in the RAT you overwrote.
    On commit, free that value (it will be the same as the one you would have overwritten in the RAT!)
    On mispredict, “undo” each step in reverse order (from tail to head).
  This gives same functionality as RRAT.
    Slower to handle mispredict that is at the head of the RoB.
      But could in theory handle mispredict as

## Slide 15
Optimizing CPU Performance
Golden Rule: tCPU = Ninst*CPI*tCLK
Given this, what are our options
  Reduce the number of instructions executed
  Reduce the cycles to execute an instruction
  Reduce the clock period
Our first focus: Reducing CPI
  Approach: Instruction Level Parallelism (ILP)

## Slide 16
Tclock

## Slide 17: tCLK
Recall: tCPU = Ninst*CPI*tCLK
What defines tCLK?
  Critical path latency (= logic + wire latency)
  Latch latency
  Clock skew
  Clock period design margins
In current and future generation designs
  Wire latency becoming dominant latency of critical path
  Due to growing side-wall capacitance
  Brings a spatial dimension to architecture optimization
    E.g., How long are the wires that will connect these two devices?

## Slide 18: Determining the Latency of a Wire
scale
shrinks
grows

## Slide 19: But reality is worse…. (Fringe)
For Intel 0.25u process
W~=0.64
T~=0.48
H is around 0.9.
www.ee.bgu.ac.il/~Orly_lab/courses/Intro_Course/Slides/Lecture02-2-Wire.ppt

## Slide 20: Moral of the “tCLK" story
As we shrink wire delay starts to dominate
  Agarwal et. al. Clock Rate versus IPC: the End of the Road for Conventional Microarchitectures, ISCA 2000
  d

## Slide 21: And reducing the number of instructions executed…
Sorry, wrong class.
  Compilers can help with this (a lot in some cases)
  So can ISA design, but usually not too much.
  Making instructions too complex hurts ILP and tCLK
So on the whole reducing # of instructions doesn’t look to be viable.
  So ILP would seem to be “where it’s at”

## Slide 22
Optimizing CPU Performance
Golden Rule: tCPU = Ninst*CPI*tCLK
Given this, what are our options
  Reduce the number of instructions executed
  Reduce the cycles to execute an instruction
  Reduce the clock period
Our first focus: Reducing CPI
  Approach: Instruction Level Parallelism (ILP)

## Slide 23
Early Branch
Resulution

## Slide 24: BRAT
Simple idea:
  When we mispredict we need to recover things to the state when the branch finished issuing.
    RAT:
      Just make a copy
      Free list is non-trivial
    RS
      Can we just make a copy?
    RoB
      Easy money.
Note: the literature usually calls this “map table checkpoints” or “branch stack” or some such. I find that unwieldy so BRAT or BMAP will be used here. See “Checkpoint Processing and Recovery: Towards Scalable Large Instruction Window Processors” for
a nice overview of options on branch misprediction recovery.

## Slide 25
RoB
RS1 | 
RS2 | 
RS3 | 
RS4 | 
AR | Target
0 | 0
1 | 1
2 | 2
3 | 3
RAT
AR | Target
0 | 
1 | 
2 | 
3 | 
BRAT
PRF freelist:

## Slide 26: Group formation