## Slide 1
EECS 470
Memory Speculation
Winter 2024
Slides developed in part by Profs. Austin, Brehob, Falsafi, Hill, Hoe, Lipasti, Martin, Roth, Shen, Smith, Sohi, Tyson, Vijaykumar, Wenisch of Carnegie Mellon University, Purdue University, University of Michigan, Univerity of Pennsylvania, and University of Wisconsin.

## Slide 2: Tomasulo-Style Scheduler Implementation
Scheduler
Logic
Results
Input/Result Networks
Reservation Stations
Inputs
Network
Control
Valid
Bits
Tag
Tag
V
V
Value
Value
Flags
Op
Synchronization managed by scheduler logic
Communication through input/output networks
Infrastructure geared towards register communication

## Slide 3: Out-of-Order Memory Operations
Scheduling is straightforward in out-of-order…
  Register inputs only
  Register renaming captures all true dependences
  Tags tell you exactly when you can execute
… except with loads and stores
  Speculative stores cannot modify memory
    Unless you can fix a mis-speculated store somehow!
  Register renaming does not tell you all dependences for loads
    There are some in memory
  How do loads find older in-flight stores to same address (if any)?
  Issue of finding if addresses match is called “memory disambiguation”

## Slide 4: The Good: Register Communication
Directly specified dependencies (contained in inst)
  Accurate description of communication
    no false or missing dependency edges
    permits realization of dataflow schedule
  Early description of communication
    know dependencies upon decode
    allows scheduler logic to be pipelined without impacting speed of communication
Small communication name space (32-64 usually)
  Fast access to communication storage
    possible to map entire communication space (no tags)
    possible to bypass communication storage
      Forwarding

## Slide 5: The Bad (and the ugly): Memory Scheduling
Recall how we handle dependencies in registers
  We address false dependencies with register renaming.
  We address true dependencies with the out-of-order machine
    CDB broadcast and wakeup
Why can’t we do the same things with memory?
  What would rename look like for memory?
    Why might it be hard to pull off?
  What about wakeup?
    What’s tricky here?
Cannot directly use the same techniques
  Indirectly specified memory dependencies
  Large communication space (232-64 bytes!)
  Memory latency is variable
    Complicates scheduling

## Slide 6: Requirements for a Solution
Accurate description of memory dependencies
  No (or few) missing or false dependencies
  Permit realization of dataflow schedule
Early presentation of dependencies
  Permit pipelining of scheduler logic
Fast access to communication space
  Preferably as fast as register communication (zero cycles)

## Slide 7: The Three Dependency “Flows”

## Slide 8: Implementation
Several hardware realizations:
  Unified LSQ (easier to understand, but nasty hardware)
  Separate LQ* and SQ (more complicated, but fairly elegant)
We’ll start with a unified LSQ and move to separate LB and SQ.
*Likely would end up with a load buffer (LB) rather than a queue…

## Slide 9: In-order Load/Store Scheduling
Idea: Schedule all loads and stores in program order
  This cannot violate true data dependencies (non-speculative)
Capabilities/limitations:
  Overly restrictive – likely to add many false dependencies
  Early presentation of dependencies (no addresses)
  Not fast, all communication through memory structures
Found in in-order issue pipelines
st X
ld Y
st Z
ld X
ld Z
true
realized
Dependencies
program order

## Slide 10: Consider the LSQ cases
Slot | LSQ addresses (top is head)
A | Store 0x44
B | Load 0x20
C | Load 0x44
D | Store ????
E | Load 0x44
F | Store 0x20
G | Load 0x20
H | Load 0x60
Which of the loads are we sure we will fulfill via D$/Memory?
Which of the loads will we fulfill via load-to-store forwarding?
Which aren’t we sure of?
Identify what to do with each load.

## Slide 11: Unified Load/Store Queue
Operates as a circular FIFO
  Allocate on dispatch
  De-allocate on retirement
Calc address in register dataflow order
A NxN comparator matrix detects memory address dependence (also considers relative age of entries)
  Store ops are held until retirement
  Load ops are issued when no dependency exists & all older store addresses known
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
=
address
calculation+
translation

## Slide 12: Unified Load/Store Queue Questions
When do we search for store-to-load forwarding?
  As soon as we have the load address
What could happen once we have the load address?
  There is a store whose data we’ll use
  There is no store whose data we’ll use
  We aren’t sure which store’s data, if any, we’ll use.
What should we do for each of those three cases?

## Slide 13: Split LQ and SQ
D$/TLB + structures to handle in-flight loads/stores
  Performs four functions
  In-order store retirement
    Writes stores to D$ in order
    Basic, implemented by store queue (SQ)
  Store-load forwarding
    Allows loads to read values from older un-retired stores
    Data provided to LQ from SQ.
  Memory ordering violation detection
    Checks load speculation (more later)
    Advanced, implemented by load queue (LQ)
  Memory ordering violation avoidance
    Advanced, implemented by dependence predictors

## Slide 14: Simple Data Memory FU: D$/TLB + SQ
Just like any other FU
  2 register inputs (addr, data in)
  1 register output (data out)
  1 non-register input (load pos)?
Store queue (SQ)
  In-flight store address/value
  In program order (like ROB)
  Addresses associatively searchable
  Size heuristic: 15-20% of ROB
But what does it do?
value
address
==
==
==
==
==
==
==
==
age
D$/TLB
head
tail
load position
address
data in
data out
Store Queue (SQ)

## Slide 15: When should a load access memory?
When to go to memory?
Only at the head of the ROB (in order!)
Only no stores between it and head of LSQ/ROB
Only when there are no stores of the same address (or unknown address) between it and the head of the LSB/ROB.
Load goes to memory at address calculation, gets fixed if there is a conflicting store

## Slide 16: When should a load go to the CDB?
Once you know you have the right data
Once you get some data
  If you get this wrong, you need to squash it and all(?) following instructions.
Based on a confidence predictor or other additional information.
  “Memory dependence prediction”

## Slide 17: How to get data from stores?
Forwarding:
  If there is a conflicting store, get the data from it.
    This isn’t trivial.

## Slide 18: Yet another idea…
Let’s use a predictor
Predict if a load is likely to be forwarding from a store
  If not, get it from D$ and send it to the CDB
  If so, wait.
Thoughts on cost/benefit of speculation?
  How should that impact our predictor?
“Memory dependence prediction”