## Slide 1: Multiprocessors continued
Quad-core Kentsfield package
IBM's Power7 with eight cores and 32 Mbytes eDRAM

## Slide 2: Quick overview
Why do we have multi-processors?
What type of programs will work well? What type work poorly?

## Slide 3: Overview of today’s lecture
Performance expectations
  Amdahl’s law.
Review
  Shared memory vs. message passing
  Interconnection networks
  Thread-level parallelism
Context
  Bandwidth
Coherence
  Directory-based consistency protocols
Consistency
  Sequential (strong) consistency, weak consistency

## Slide 4: Let’s (re)start at the top: Performance Expectations
Amdahl's Law:
  If a fraction P of your program can be sped up by a factor of S, then your performance is:
  So if P=0.3 and S=2 we get (1/(.7+.15)) 1/.85 which is about 1.17.
Question:
  If you have a program in which 10% can’t be done in parallel (i.e. must be serial) and you’ve got 64 processors, what’s the best speed up you could hope for?
Review
Notes: 8.77, best possible is 10.

## Slide 5: Review: Thread-Level Parallelism
Thread-level parallelism (TLP)
  Collection of asynchronous tasks: not started and stopped together
  Data shared loosely, dynamically
Example: database/web server (each query is a thread)
  accts is shared, can’t register allocate1 even if it were scalar
  id and amt are private variables, register allocated to r1, r2
struct acct_t { int bal; };
shared struct acct_t accts[MAX_ACCT];
int id,amt;
if (accts[id].bal >= amt)
{
accts[id].bal -= amt;
spew_cash();
}
0: addi r1,accts,r3
1: ld 0(r3),r4
2: blt r4,r2,6
3: sub r4,r2,r4
4: st r4,0(r3)
5: call spew_cash
6: ... ... ...
Review: TLP
1Keyword in C is “volatile”

## Slide 6: Thread level parallelism (TLP)
We exploited parallelism at the instruction level (ILP)
  Hardware can’t find TLP.
    Complier/programmer needs to find it (we lack the window size)
    Compilers getting better at this.
  But hardware can take advantage of TLP
    Run on multiple cores
    If data is shared, provide rules to the software about what it can assume about shared data.
Review: TLP

## Slide 7: Review: Why Shared Memory?
Pluses:
  For applications looks like multitasking uniprocessor
  For OS only evolutionary extensions required
  Easy to do communication without OS
  Software can worry about correctness first then performance
Minuses:
  Proper synchronization is complex
  Communication is implicit so harder to optimize
  Hardware designers must implement
Result:
  Traditionally bus-based Symmetric Multiprocessors (SMPs), and now the CMPs are the most success parallel machines ever
  And the first with multi-billion-dollar markets
Review: Shared memory vs. message passing

## Slide 8: Alternative to shared memory?
Explicit message passing
  Rather difficult to code
We’ll not be doing anything with it
  But while not a 470 topic, it is important.
    Graduate level parallel programming class covers this in detail.
Review: Shared memory vs. message passing

## Slide 9: But shared memory systems have their own problems
Two in particular
  Cache coherence
  Memory consistency model
Different solutions depending on interconnect
  So let’s do interconnect now, and jump back to these two later.
Review: Shared memory vs. message passing

## Slide 10: Review: Interconnect
There are many ways to connect processors.
  Shared network
    Bus-based
    Crossbar
  Point-to-point
    More topologies than I want to think about
      Mesh (in any amount of dimensionality)
      Torus (in any amount of dimensionality)
      nCube
      Tree
      etc. etc. etc. etc.
Review: Interconnect
Notes: 8.77, best possible is 10.

## Slide 11: Shared vs. Point-to-Point Networks
Shared network: e.g., bus (left)
  Low latency
  Low bandwidth: doesn’t scale beyond ~8 processors
  Shared property simplifies cache coherence protocols (later)
Point-to-point network: e.g., mesh or ring (right)
  Longer latency: may need multiple “hops” to communicate
  Higher bandwidth: scales to 1000s of processors
  Cache coherence protocols are complex
CPU($)
Mem
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
R
R
R
R
Review: Interconnect

## Slide 12: Organizing Point-To-Point Networks
Network topology: organization of network
  Tradeoff performance (connectivity, latency, bandwidth)  cost
Router chips
  Networks that require separate router chips are indirect
  Networks that use processor/memory/router packages are direct
    Fewer components, “Glueless MP”
Point-to-point network examples
  Indirect tree (left)
  Direct mesh or ring (right)
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
R
R
R
R
R
R
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R
Review: Interconnect

## Slide 13: Context: Bandwidth
As in the uniprocessor we need caches
  To reduce average memory latency.
But recall caches are also important for reducing bandwidth.
  And now we’ve got (say) 4x as many requests
    And the total amount of bandwidth is shrinking (why?)
  We’ve probably got a bandwidth problem.
    It’s important that caches work well!
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
R
R
R
R
Review: Bandwidth!

## Slide 14: Hardware Cache Coherence
Coherence controller:
  Examines bus traffic (addresses and data)
  Executes coherence protocol
    What to do with local copy when you see different things happening on bus
CPU
D$ data
D$ tags
CC
bus
Review: Coherence!

## Slide 15: Scalability problems of Snoopy Coherence
Prohibitive bus bandwidth
  Required bandwidth grows with # CPUS…
  … but available BW per bus is fixed
  Adding busses makes serialization/ordering hard
Prohibitive processor snooping bandwidth
  All caches do tag lookup when ANY processor accesses memory
  Inclusion limits this to L2, but still lots of lookups
Upshot: bus-based coherence doesn’t scale beyond 8–16 CPUs
Coherence: Bus-based bandwidth issues

## Slide 16: Scalable Cache Coherence
Scalable cache coherence: two part solution
Part I: bus bandwidth
  Replace non-scalable bandwidth substrate (bus)…
  …with scalable bandwidth one (point-to-point network, e.g., mesh)
Part II: processor snooping bandwidth
  Interesting: most snoops result in no action
  Replace non-scalable broadcast protocol (spam everyone)…
  …with scalable directory protocol (only spam processors that care)
Review: Coherence!

## Slide 17: Directory Coherence Protocols
Observe: physical address space statically partitioned
  Can easily determine which memory module holds a given line
    That memory module sometimes called “home”
  Can’t easily determine which processors have line in their caches
  Bus-based protocol: broadcast events to all processors/caches
    Simple and fast, but non-scalable
Directories: non-broadcast coherence protocol
  Extend memory to track caching information
  For each physical cache line whose home this is, track:
    Owner: which processor has a dirty copy (I.e., M state)
    Sharers: which processors have clean copies (I.e., S state)
  Processor sends coherence event to home directory
    Home directory only sends events to processors that care
Coherence: Directory-based

## Slide 18: Read Processing
Read A (miss)
Node #1
Directory
Node #2
Read A
Fill A
A: Shared, #1
Coherence: Directory-based

## Slide 19: Write Processing
Read A (miss)
Node #1
Directory
Node #2
Read A
Fill A
A: Shared, #1
ReadExclusive A
Invalidate A
Fill A
Trade-offs:
Longer accesses (3-hop between Processor, directory, other Processor)
Lower bandwidth  no snoops necessary
Makes sense either for CMPs (lots of L1 miss traffic) or large-scale servers (shared-memory MP > 32 nodes)
Inv Ack A
A: Mod., #2
Coherence: Directory-based

## Slide 20: Serialization and Ordering
Let A and flag be initially 0
P1 P2
A += 5 while (flag == 0)
flag = 1 print A
Assume A and flag are in different cache blocks
What happens?
How do you implement it correctly?
Coherence: Directory-based

## Slide 21: Coherence vs. Consistency
Intuition says loads should return latest value
  what is latest?
Coherence concerns only one memory location
Consistency concerns apparent ordering for all locations
A Memory System is Coherent if
  can serialize all operations to that location such that,
  operations performed by any processor appear in program order
    program order = order defined program text or assembly code
  value returned by a read is value written by last store to that location
Coherence vs. Consistency
Notes: 3

## Slide 22: Why Coherence != Consistency
/* initial A = B = flag = 0 */
P1 P2
A = 1; while (flag == 0); /* spin */
B = 1; print A;
flag = 1; print B;
Intuition says printed A = B = 1
Coherence doesn’t say anything. Why?
Your uniprocessor ordering mechanisms (ld/st queue) hurts here. Why?
Coherence vs. Consistency
Notes: 4

## Slide 23: Sequential Consistency (SC)
switch randomly set
after each memory op
provides single sequential
order among all operations
processors
issue memory ops
in program order
P1
P2
P3
Memory
Consistency
Notes: 5

## Slide 24: Sufficient Conditions for SC
Every proc. issues memory ops in program order
Memory ops happen (start and end) atomically
  must wait for store to complete before issuing next memory op
  after load, issuing proc waits for load to complete, before issuing next op
Easily implemented with a shared bus
Consistency
Notes: 6

## Slide 25: Relaxed Memory Models
Motivation with Directory Protocols
  Misses have longer latency (do cache hits to get to next miss)
  Collecting acknowledgements can take even longer
Recall SC has
  Each processor generates at total order of its reads and writes (R-->R, R-->W, W-->W, & W-->R)
  That are interleaved into a global total order
Example Relaxed Models
PC: Relax ordering from writes to (other proc’s) reads
RC: Relax all read/write orderings (but add “fences”)
Consistency

## Slide 26: Locks
Locks

## Slide 27: Lock-based Mutual Exclusion
xfer
Crit. sec
release
Acquire starts
wait
wait
xfer
Crit. sec
release
xfer
Crit. sec
Acquire done
Release starts
Release done
Synchronization
period
No contention:
Want low latency
Contention:
Want low period
Low traffic
Fairness
Locks

## Slide 28: How Not to Implement Locks
LOCK
  while (lock_variable == 1);
  lock_variable = 1
UNLOCK
  lock_variable = 0;
Context switch!
Locks

## Slide 29: Solution: Atomic Read-Modify-Write
Test&Set(r,x)
  {r=m[x]; m[x]=1;}
Fetch&Op(r1,r2,x,op)
  {r1=m[x]; m[x]=op(r1,r2);}
Swap(r,x)
  {temp=m[x]; m[x]=r; r=temp;}
Compare&Swap(r1,r2,x)
  {temp=r2; r2=m[x]; if r1==r2 then m[x]=temp;}
r is register
m[x] is memory location x
Locks

## Slide 30: Write a lock and unlock with test-and-set
Lock:
unlock:
Locks

## Slide 31: Implementing RMWs
Bus-based systems:
  Hold bus and issue load/store operations without any intervening accesses by other processors
Scalable systems
  Acquire exclusive ownership via cache coherence
  Perform load/store operations without allowing external coherence requests
Locks

## Slide 32: Test-and-Set Spin Lock (T&S)
Lock is “acquire”, Unlock is “release”
acquire(lock_ptr):
  while (true):
    // Perform “test-and-set”
    old = compare_and_swap(lock_ptr, UNLOCKED, LOCKED)
    if (old == UNLOCKED):
      break // lock acquired!
    // keep spinning, back to top of while loop
release(lock_ptr):
  store[lock_ptr] <- UNLOCKED
Performance problem
  CAS is both a read and write; spinning causes lots of invalidations
Locks

## Slide 33: Load Locked / Store Conditional (LL/SC)
Sometimes having an atomic read/modify/write operation isn’t viable.
  Maybe your memory system just doesn’t support it
  Maybe it involves a very expensive “lock out” that prevents any other memory operation until the lock finishes.
Still possible to manage with a two step process
  Do a special load called a “load lock” or load “link”.
    Works like a normal load but it tells the hardware to watch for a store to that same address.
  Do a “store conditional” to the same address
    If there was a store to that location since the load lock, the store “fails” and that failure is communicated to the programmer (store has a destination register)
      Failed store doesn’t write to memory
  Now we know if the load and store was effectively atomic.

## Slide 34: Load-Locked Store-Conditional
Load-locked
  Issues a normal load…
  …and sets a flag and address field
Store-conditional
  Checks that flag is set and address matches
    If so, performs store and sets store register to 1.
    Otherwise sets store register to 0.
Flag is cleared by
  Invalidation
  Cache eviction
  Context switch
lock: lda r2, #1 ll r1, lock_variable
sc lock_variable, r2
beqz r2, lock
neqz r1, lock // branch not equal to zero
unlock:st lock_variable, #0
Locks

## Slide 35: Next up: Static Optimizations
Why might we want to start loads early?
  Moving loads to happen earlier is called “hoisting”
What three things limits a complier’s ability to hoist a load?