## Slide 1: Static Optimizations (aka: the complier)
Dr. Mark Brehob
EECS 470

## Slide 2: Announcements
Quiz
  Tuesday 4/2
  Coverage the same as the last homework
    Or maybe a bit from earlier

## Slide 3: The big picture
We’ve spent a lot of time learning about dynamic optimizations
  Finding ways to improve ILP in hardware
    Out-of-order execution
    Branch prediction
But what can be done statically (at compile time)?
  As hardware architects it behooves us to understand this.
    Partly so we are aware what things software is likely to be better at.
    But partly so we can find ways to find hardware/software “synergy”

## Slide 4: Some ways a compiler can help
Improve locality of data
Remove instructions that aren’t needed
Reduce number of branches executed
Many others

## Slide 5: Improve locality of reference
Examples:
  Loop interchange—flip inner and outer loops
  Loop fission—split into multiple loops
Some examples taken from Wikipedia
for i from 0 to 10
for j from 0 to 20
a[j,i] = i + j
for j from 0 to 20
for i from 0 to 10
a[j,i] = i + j

## Slide 6: Removing code (1/2)
Register optimization
  Registers are fast, and doing “spills and fills” is slow.
  So keep the data likely to be used next in registers.
Loop invariant code motion
  Move recomputed statements outside of the loop.
for (int i=0; i<n; i++) {
x = y+z;
a[i] = 6*i+x*x;
}
x = y+z;
for (int i=0; i<n; i++) {
a[i] = 6*i+x*x;
}

## Slide 7: Removing code (2/2)
Common sub-expression elimination
  (a + b) - (a + b)/4
    Just compute a+b once.
Constant folding
  Replace (3+5) with 8.

## Slide 8: Reducing number of branches executed
Using predicates or CMOVs instead of short branches
Loop unrolling
for(i=0;i<10000;i++)
{
  A[i]=B[i]+C[i];
  }
for(i=0;i<10000;i=i+2)
{
  A[i]=B[i]+C[i];
  A[i+1]=B[i+1]+C[i+1];
  }

## Slide 9: We’ll mostly focus on one thing
“Hoist” loads
  That is move the loads up so if there is a miss we can hide that latency.
    Very similar goal to our OoO processor.
xxxxx
xxxxx
LD R1=MEM[x]
R2=R1+R3
LD R1=MEM[x]
xxxxx
xxxxx
R2=R1+R3

## Slide 10: What limits our ability to hoist a load?
  ________________________________________
  _________________________________________
  _________________________________________
Notes: Can’t move past branches
if statements (due to possible exception problems)
loops (also due to exceptions, also unclear how to do it with fixed registers)
Possibly conflicting stores (get wrong value)
Creates more live values at a time, so more spills and fills.

## Slide 11: Create room to move code around
Loop unrolling
  The idea is to take a loop (usually a short loop) and do two or more iterations in a single loop body.
Initial
Loop
body
for i=1 to 10000
{
}
for i=1 to 5000
{
Loop body
Loop body
}
“Glue” logic

## Slide 12: Unroll this loop
for(i=0;i<10000;i++)
  {
  A[i]=B[i]+C[i];
  n+=A[i];
  }
  Glue logic? Reduce operations?

## Slide 13: What does unrolling buy us?
Reduces number of branches
Reduces number of branches
  Less to (mis-)predict
  If not predicting branches (say cheap embedded processor) very helpful!
  If limited number of branches allowed in ROB at a time, reduces this problem.
Can schedule for pipeline better
  If superscalar might be best to combine certain operations. Loop unrolling adds flexibility

## Slide 14: What does it cost us?
Code space.
  Mainly worried about impact on I-cache hit rate. But L2 or DRAM impact if unroll too much!
If loop body has branches in it can hurt branch prediction performance.
Other?

## Slide 15: Another one to unroll.
for(i=0;i<99999;i++)
  {
  A[i]=B[i]+C[i];
  B[i+1]=C[i]+D[i];
  }

## Slide 16
One more to do
while (B[i]!=0)
  {
  i++;
  A[i]=B[i]+C[i];
  B[i+1]=C[i]+D[i];
  }

## Slide 17: How about this code?
Loop: r1=MEM[r2+0]
r1=r1*2
MEM[r2+0]=r1
r2=r2+4
bne r2 r3 Loop
We’ll come back to this later…

## Slide 18: Other ILP techniques
Consider an in-order superscalar processor executing the following code:
    R1=16 //A
    R2=R1+5 //B
    R3=14 //C
    R4=R3+5 //D
  Without OoO we would execute A, BC, D.
  Note that A&B are independent of C&D. So ordering ACBD would let us do AC, BD.
Thus, the simple action of reordering instructions can increase ILP.

## Slide 19: So…
We can expose ILP by
  Unrolling loops
  Reordering code
    To increase # of independent instructions near each other
    To move a load (or other high-latency instruction) from its use.
  What limits reordering options?

## Slide 20: The limits of hoisting loads (again)
Moving code outside of its “basic block” is scary
  In other words, moving code past branches or branch targets can give wrong execution
    Loads or stores might go to invalid locations
    Need to be sure don’t trash a needed register.
Also
  Moving loads past stores is scary
    What if store wrote to that address
The problem is that we don’t have the recovery mechanisms we do in hardware
  After all, the program specifies behavior! How do we know when the specified behavior is “wrong”?
    In hardware it is fairly easy…

## Slide 21: Static dependency checking
A superscalar processor has to do certain dependency checking at issue (or dispatch)
  Is a given set of instructions dependent on each other?
  If ALU resources are shared are there enough resources?
Many of these issues can be resolved at compile time.
  What can’t be resolved?
  Once resolved, how do you tell the CPU?

## Slide 22: One static solution: VLIW
Have a bunch of pipelines, usually with different functional units.
  Each “instruction” actually contains directions for all the pipelines.
  (Thus the “very long instruction”)
Pipe1 – int
Pipe2 – int
Pipe3 – fp
Pipe4 – ld/st
Pipe5 – branch
VLIW
Instruction
word

## Slide 23: What’s good about VLIW?
Compiler does all dependency checking, including structural hazards!
  No dependence checking makes the hardware a lot simpler!
    Reduces mis-prediction penalty.
    Saves power
    May save area!
Since the compiler can also reorder instructions we may be able to make good use of the pipes.

## Slide 24: So what’s bad?
Code density
  If you can’t fill a given pipe, need a no-op.
  To get the ILP needed to be able to fill the pipe, often need to unroll loops.
When a newer processor comes out, 100% compatibility is hard
  Word length may need to change
  Structural dependencies may be different

## Slide 25: Conditional execution
Conditional execution (we’ve done this before!)
bne r1 r2 skip
r4=r5+r6
skip: r7=r4+r12
r8=cmp(r1,r2)
if(r8) r4=r5 + r6
r7=r4+r12
-or-
r8=cmp(r1,r2)
r9=r5+r6
cmov (r8, r4  r9)
r7=r4+r12

## Slide 26: Software pipelining

## Slide 27: Code example from before
Loop: r1=MEM[r2+0]
r1=r1*2
MEM[r2+0]=r1
r2=r2+4
bne r2 r3 Loop
And one name
dependency on r2.
Also the store is dependent on r2 but hidden…

## Slide 28: ILP?
r1=MEM[r2+0] //A
r1=r1*2 //B
MEM[r2+0]=r1 //C
r2=r2+4 //D
bne r2 r3 Loop //E
Currently no two instructions can be executed in parallel on a statically scheduled machine.
  (With branch prediction A and E could be executed in parallel)
On a dynamically scheduled machine could execute instructions from different iterations at once.

## Slide 29: What would OoO do?
r1=MEM[r2+0] //A
r1=r1*2 //B
MEM[r2+0]=r1 //C
r2=r2+4 //D
bne r2 r3 Loop //E
A perfect, dynamically scheduled, speculative computer would find the following:
Let A1 indicate the execution of A in the first iteration of the loop.
A1 | D1 |  |  | 
B1 | A2 | D2 | E1 | 
C1 | B2 | A3 | D3 | E2
C2 | B3 | A4 | D4 | E3
….. | ….. | ….. | ….. | …..

## Slide 30: Software Pipeline
r1=MEM[r2+0] //A
r1=r1*2 //B
MEM[r2+0]=r1 //C
r2=r2+4 //D
bne r2 r3 Loop //E
With “software pipelining” we can do the same thing in software.
MEM[r2+0]=r1 //C(n)
r1=r4*2 //B(n+1)
r4=MEM[r2+8] //A(n+2)
r2=r2+4 //D(n)
bne r2 r3 Loop //E(n)
What problems could arise?
“Speculative load” might cause an exception.
Latency of load could be too slow.

## Slide 31: Prolog and epilog
r3=r3-8 // Needed to check legal! r4=MEM[r2+0] //A(1)
r1=r4*2 //B(1)
r4=MEM[r2+4] //A(2)
Loop: MEM[r2+0]=r1 //C(n)
r1=r4*2 //B(n+1)
r4=MEM[r2+8] //A(n+2)
r2=r2+4 //D(n)
bne r2 r3 Loop //E(n)
MEM[r2+0]=r1 // C(x-1)
r1=r4*2 // B(x)
MEM[r2+0]=r1 // C(x)
r3=r3+8 // Could have used tmp var.

## Slide 32
Software Pipelining example
Execution Code Layout Action
Flow
Stage A
Stage B
Stage C
Stage A
Stage B
Stage A
Stage C
Stage C
Stage B
Stage C
Stage D
Stage D
Stage D
Stage C
Stage B
Stage A
iter1
iter0
II
Prologue
Kernel
Epilogue
itern-2
itern-1

## Slide 33: Example, just to be sure.
r4=MEM[r2+0] //A1
r1=r4*2 //B1
r4=MEM[r2+4] //A2
Loop: MEM[r2+0]=r1 //C(n)
r1=r4*2 //B(n+1)
r4=MEM[r2+8] //A(n+2)
r2=r2+4 //D(n)
bne r2 r3 Loop //E(n)
ADDR | DATA
12 | 55
16 | 23
20 | 19
24 | -5
R2=12, r3=28
R4=_______ R1= _______

## Slide 34: Next step
Parallel execution
  It isn’t clear how D and E of any iteration can be executed in parallel on a statically scheduled machine
What if load latency is too long?
  Will be stalling a lot…
  Fix by unrolling loop some.
r1=MEM[r2+0] //A
r1=r1*2 //B
MEM[r2+0]=r1 //C
r2=r2+4 //D
bne r2 r3 Loop //E

## Slide 35: NEXT…
Let’s now jump from Software Pipelining to IA-64.
  We will come back to Software Pipelining in the context of IA-64…
  We will redo the IA-64 stuff from the start for next lecture
    Not sure how far I’ll get into it today.

## Slide 36: IA-64
128 64-bit registers
  Use a register window similarish to SPARC
128 82 bit fp registers
64 1 bit predicate registers
8 64-bit branch target registers

## Slide 37: Explicit Parallelism
Groups
  Instructions which could be executed in parallel if hardware resources available.
Bundle
  Code format. 3 instructions fit into a 128-bit bundle.
  5 bits of template, 41*3 bits of instruction.
    Template specifies what execution units each instruction requires.

## Slide 38: Instructions
41 bits
  4 high order specify opcode (combined with template for bundle)
  6 low order bits specify predicate register number.
Every instruction is predicated!
Also NaT bits are used to handle speculated exceptions.

## Slide 39
Speculative Load
Traditional
IA-64
Load instruction (ld.s) can be moved outside of a basic block even if branch target is not known
Speculative loads does not produce exception - it sets the NaT
Check instruction (chk.s) will jump to fix-up code if NaT is set

## Slide 40
Propagation of NaT
IF ( NaT[r3] || NaT[r4] ) THEN set NaT[r6]
IF ( NaT[r6] ) THEN set NaT[r5]
Require check on NaT[r5] only since the NaT is inherited
Reduce number of checks
Fix-up will execute the entire chain
Only single check required
NaT[reg] = NaT bit of reg

## Slide 41: Advanced loads
ld.a – Advanced load
  Performs the load, puts it into the “ALAT”
    If any following store writes to the same address, this is noted with a single bit.
    When a ld.c is executed, if that bit is set, we refetch.
    When chk.a is executed, if bit is set, fix up code is run. (Useful if load result already used.)
    Both also cause any deferred exception to occur.

## Slide 42: Software pipelining on IA-64
Lots of tricks
  Rotating registers
  Special counters
Often don’t need Prologue and Epilog.
  Special counters and prediction lets us only execute those instructions we need to.