## Slide 1: Multithreading Processors and Static Optimization Review
Adapted from Bhuyan, Patterson, Eggers, probably others

## Slide 2: Class stuff
CATME due today.
  It’s probably the most points per unit effort in the class. Do it.
Quiz hopefully graded by tomorrow.
HW5 out tomorrow, pushing due date to 4/23
MS3 due Thursday 4/11
  Meetings optional-ish.
Lecture schedule:
  4/4: Multithreaded processors
  4/9: ISA
  4/11: Instruction scheduling (with a paper)
  4/16: No lecture (probably)
  4/18 Exam review
  4/23 Oral Presentations

## Slide 3: Today
Finish IA-64
Review Complier stuff
SMT

## Slide 4: IA-64
128 64-bit registers
  Use a register window similarish to SPARC
128 82 bit fp registers
64 1 bit predicate registers
8 64-bit branch target registers

## Slide 5: Explicit Parallelism
Groups
  Instructions which could be executed in parallel if hardware resources available.
Bundle
  Code format. 3 instructions fit into a 128-bit bundle.
  5 bits of template, 41*3 bits of instruction.
    Template specifies what execution units each instruction requires.

## Slide 6: Instructions
41 bits
  4 high order specify opcode (combined with template for bundle)
  6 low order bits specify predicate register number.
Every instruction is predicated!
Also NaT bits are used to handle speculated exceptions.

## Slide 7
Speculative Load
Traditional
IA-64
Load instruction (ld.s) can be moved outside of a basic block even if branch target is not known
Speculative loads does not produce exception - it sets the NaT
Check instruction (chk.s) will jump to fix-up code if NaT is set

## Slide 8
Propagation of NaT
IF ( NaT[r3] || NaT[r4] ) THEN set NaT[r6]
IF ( NaT[r6] ) THEN set NaT[r5]
Require check on NaT[r5] only since the NaT is inherited
Reduce number of checks
Fix-up will execute the entire chain
Only single check required
NaT[reg] = NaT bit of reg

## Slide 9: Advanced loads
ld.a – Advanced load
  Performs the load, puts it into the “ALAT”
    If any following store writes to the same address, this is noted with a single bit.
    When a ld.c is executed, if that bit is set, we refetch.
    When chk.a is executed, if bit is set, fix up code is run. (Useful if load result already used.)
    Both also cause any deferred exception to occur.

## Slide 10: Software pipelining on IA-64
Lots of tricks
  Rotating registers
  Special counters
Often don’t need Prologue and Epilog.
  Special counters and prediction lets us only execute those instructions we need to.

## Slide 11: Static optimization and IA64 review
There are many important compiler techniques
  We focused on hoisting loads.
  But other include:
    Register allocation (to reduce spills and fills)
    Common sub-expression elimination
  Wikipedia’s article on optimizing compliers provides a nice overview of standard optimizations.

## Slide 12: How does static compare to dynamic?
Static
  Has “a larger window” as it can see the whole program at once.
  Can change the instructions executed.
Dynamic
  Has dynamic information
  “Can be wrong”

## Slide 13: That said problems are similar
Static can reduce number of instructions, but for a given set of instructions, it is trying to optimize ILP just as dynamic does.
  That will mean reordering instructions.
  Suffers the same problems hardware does
    Memory dependencies and branches.

## Slide 14: Why can hoisting loads help?
  add r15 = r2,r3 //A
  mult r4 = r15,r2 //B
  mult r4 = r4,r4 //C
  st8 [r12] = r4 //D
  ld8 r5 = [r15] //E
  div r6 = r5,r7 //F
  add r5 = r6,r2 //G
  Assume latencies are:
    add, store: +0
    mult, div: +3
    ld: +4
A:1
D:1
G:1
C:4
E:5
B:4
F:4
20
11
10

## Slide 15: IA 64 support
Why is hoisting above a branch hard?
  _____________________
  IA64 solution?
    Speculative load
Why is hoisting above a store hard?
  __________________________
  IA64 solution:
    Advanced load
Notes: could cause an exception if we execute a load that wasn’t going to really happen.
Could get wrong data from memory.

## Slide 16: Other things we did
Software pipelining
  Idea, example
Discussed register pressure
  Idea, examples where optimization make it worse, IA64 “solution” (lots of registers…)
Briefly discussed caching
  Code size increase is a common side effect of complier optimizations
  Optimizing for locality is good.

## Slide 17: On to multi-threading

## Slide 18: Pipeline Hazards
LW r1, 0(r2)
LW r5, 12(r1)
ADDI r5, r5, #12
SW 12(r1), r5
Each instruction may depend on the next
  Without forwarding, need stalls
  LW r1, 0(r2)
  LW r5, 12(r1)
  ADDI r5, r5, #12
  SW 12(r1), r5
Bypassing/forwarding cannot completely eliminate interlocks or delay slots

## Slide 19: Multithreading
How can we guarantee no dependencies between instructions in a pipeline?
  One way is to interleave execution of instructions from different program threads on same pipeline
Interleave 4 threads, T1-T4, on non-bypassed 5-stage pipe
T1: LW r1, 0(r2)
T2: ADD r7, r1, r4
T3: XORI r5, r4, #12
T4: SW 0(r7), r5
T1: LW r5, 12(r1)

## Slide 20: CDC 6600 Peripheral Processors (Cray, 1965)
First multithreaded hardware
10 “virtual” I/O processors
fixed interleave on simple pipeline
pipeline has 100ns cycle time
each processor executes one instruction every 1000ns
accumulator-based instruction set to reduce processor state

## Slide 21: Simple Multithreaded Pipeline
Have to carry thread select down pipeline to ensure correct state bits read/written at each pipe stage

## Slide 22: Multithreading Costs
Appears to software (including OS) as multiple slower CPUs
Each thread requires its own user state
  GPRs
  PC
Other costs?

## Slide 23: Thread Scheduling Policies
Fixed interleave (CDC 6600 PPUs, 1965)
  each of N threads executes one instruction every N cycles
  if thread not ready to go in its slot, insert pipeline bubble
Software-controlled interleave (TI ASC PPUs, 1971)
  OS allocates S pipeline slots amongst N threads
  hardware performs fixed interleave over S slots, executing whichever thread is in that slot
Hardware-controlled thread scheduling (HEP, 1982)
  hardware keeps track of which threads are ready to go
  picks next thread to execute based on hardware priority
  scheme

## Slide 24: What “Grain” Multithreading?
So far assumed fine-grained multithreading
  CPU switches every cycle to a different thread
  When does this make sense?
Coarse-grained multithreading
  CPU switches every few cycles to a different thread
  When does this make sense?

## Slide 25: Multithreading Design Choices
Context switch to another thread every cycle, or on hazard or L1 miss or L2 miss or network request
Per-thread state and context-switch overhead
Interactions between threads in memory hierarchy

## Slide 26: Denelcor HEP (Burton Smith, 1982)
First commercial machine to use hardware threading in main CPU
  120 threads per processor
  10 MHz clock rate
  Up to 8 processors
  precursor to Tera MTA (Multithreaded Architecture)

## Slide 27: Tera MTA Overview
Up to 256 processors
Up to 128 active threads per processor
Processors and memory modules populate a 3D torus interconnection fabric
Flat, shared main memory
  No data cache
  Sustains one main memory access per cycle per processor
50W/processor @ 260MHz

## Slide 28: MTA Instruction Format
Three operations packed into 64-bit instruction word (short VLIW)
One memory operation, one arithmetic operation, plus one arithmetic or branch operation
Memory operations incur ~150 cycles of latency
Explicit 3-bit “lookahead” field in instruction gives number of subsequent instructions (0-7) that are independent of this one
  c.f. Instruction grouping in VLIW
  allows fewer threads to fill machine pipeline
  used for variable- sized branch delay slots
Thread creation and termination instructions

## Slide 29: MTA Multithreading
Each processor supports 128 active hardware threads
  128 SSWs, 1024 target registers, 4096 general-purpose registers
Every cycle, one instruction from one active thread is launched into pipeline
Instruction pipeline is 21 cycles long
At best, a single thread can issue one instruction every 21 cycles
  Clock rate is 260MHz, effective single thread issue rate is 260/21 = 12.4MHz

## Slide 30: Speculative, Out-of-Order Superscalar Processor

## Slide 31
P6 Performance: uops commit/clock
Average
0: 55%
1: 13%
2: 8%
3: 23%
Integer
0: 40%
1: 21%
2: 12%
3: 27%

## Slide 32: Superscalar Machine Efficiency
Why horizontal waste?
Why vertical waste?

## Slide 33: Vertical Multithreading
Cycle-by-cycle interleaving of second thread removes vertical waste

## Slide 34: Ideal Multithreading for Superscalar
Interleave multiple threads to multiple issue slots with no restrictions

## Slide 35: Simultaneous Multithreading
Add multiple contexts and fetch engines to wide out-of-order superscalar processor
  [Tullsen, Eggers, Levy, UW, 1995]
OOO instruction window already has most of the circuitry required to schedule from multiple threads
Any single thread can utilize whole machine

## Slide 36: Comparison of Issue Capabilities Courtesy of Susan Eggers

## Slide 37: From Superscalar to SMT
SMT is an out-of-order superscalar extended with hardware to support multiple executing threads

## Slide 38: From Superscalar to SMT
Small items
  per-thread program counters
  per-thread return address stacks
  per-thread bookkeeping for instruction retirement, trap & instruction dispatch queue flush
  thread identifiers, e.g., with BTB & TLB entries

## Slide 39: Simultaneous Multithreaded Processor

## Slide 40: SMT Design Issues
Which thread to fetch from next?
  Don’t want to clog instruction window with thread with many stalls  try to fetch from thread that has fewest insts in window
Locks
  Virtual CPU spinning on lock executes many instructions but gets nowhere  add ISA support to lower priority of thread spinning on lock

## Slide 41: Intel Pentium-4 Xeon Processor
Hyperthreading == SMT
Dual physical processors, each 2-way SMT
Logical processors share nearly all resources of the physical processor
  Caches, execution units, branch predictors
Die area overhead of hyperthreading ~5 %
When one logical processor is stalled, the other can make progress
  No logical processor can use all entries in queues when two threads are active
A processor running only one active software thread to run at the same speed with or without hyperthreading
“Death by 1000 cuts”

## Slide 42: And things to think about: Wider in the front…
P6: (% instructions dispatched that do not commit)