## Slide 1: Instruction scheduling
Based on slides by Ilhyun Kim and Mikko Lipasti

## Slide 2: Schedule of things to do
HW5 posted.
  Due on 4/23 (last day of class) @10pm – 24 hours late with only 5% off.
MS3 Today
Project is due on Saturday 4/20 at 9pm.
  Last synth job can still be running, but don’t rely on it.
  No code changes after this.
Oral and written reports are due on Tuesday 4/23.
  Brief directions for both posted shortly.
  Final written report is due at 9pm on Piazza
  Oral reports are during the day.
  Will watch at least 2 other talks.
    Can go to all if you wish.

## Slide 3: Lecture (and review) schedule
4/11: (today) Instruction scheduling
4/16: (Tuesday) No class (work on projects)
4/18: (Thursday) Exam Q&A in class
4/23: (Tuesday) Project presentations
4/24: (Wednesday) Exam Q&A (what time?)
4/26: (Friday) Final exam 10:30-12:30

## Slide 4: Today
Instruction scheduling overview
  Scheduling atomicity
  Speculative scheduling
  Scheduling recovery
Other neat ideas…
Reading list

## Slide 5: Register Dataflow
Scheduling review

## Slide 6: Instruction scheduling
A process of mapping a series of instructions into execution resources
  Decides when and where an instruction is executed
Data dependence graph
1
2
3
4
5
6
FU0
FU1
n
n+1
n+2
n+3
1
2
3
5
4
6
Mapped to two FUs
Instruction scheduling review

## Slide 7: Instruction scheduling
A set of wakeup and select operations
  Wakeup
    Broadcasts the tags of parent instructions selected
    Dependent instruction gets matching tags, determines if source operands are ready
    Resolves true data dependences
  Select
    Picks instructions to issue among a pool of ready instructions
    Resolves resource conflicts
      Issue bandwidth
      Limited number of functional units / memory ports
Instruction scheduling review

## Slide 8: Scheduling loop
Basic wakeup and select operations
=
=
=
=
OR
OR
readyL
tagL
readyR
tagR
=
=
=
=
OR
OR
readyL
tagL
readyR
tagR
tag W
tag 1
…
…
…
ready - request
request n
grant n
grant 0
request 0
grant 1
request 1
……
selected
issue
to FU
broadcast the tag of the selected instructions
Select logic
Wakeup logic
scheduling
loop
Instruction scheduling review

## Slide 9: Wakeup and Select
FU0
FU1
n
n+1
n+2
n+3
1
2
3
5
4
6
Select 1
Wakeup 2,3,4
Wakeup / select
Select 2, 3
Wakeup 5, 6
Select 4, 5
Wakeup 6
Select 6
Ready inst
to issue
1
2, 3, 4
4, 5
6
1
2
3
4
5
6
Instruction scheduling review

## Slide 10: Scheduling Atomicity
If we want to pipeline selection logic, we will latch the selection decision (it becomes a pipeline stage)
  So we can’t wake up the next guy until the cycle after we are selected.
n
n+1
n+2
n+3
n+4
select 1
wakeup 2, 3
select 2, 3
wakeup 4
select 4
select 1
wakeup 2, 3
Select 2, 3
wakeup 4
Select 4
Atomic scheduling
Non-Atomic
2-cycle scheduling
cycle
1
4
1
2
3
4
2
3
Scheduling Atomicity

## Slide 11: Implication of scheduling atomicity
Pipelining is a standard way to improve clock frequency
Hard to pipeline instruction scheduling logic without losing ILP
  ~10% IPC loss in 2-cycle scheduling
  ~19% IPC loss in 3-cycle scheduling
A major obstacle to building high-frequency microprocessors
Scheduling Atomicity

## Slide 12: Scheduler Designs
Data-Capture Scheduler
  Keep the most recent register value in reservation stations
  Data forwarding and wakeup are combined to some extent
    Early tag broadcast decouples this to some extent of course.
Register
File
Data-captured
scheduling window
(reservation station)
Functional Units
Forwarding
and wakeup
Register update
Scheduling Atomicity

## Slide 13: Scheduler Designs
Non-Data-Capture Scheduler
  Keep the most recent register value in RF (physical registers)
  Data forwarding and wakeup are cleanly decoupled
Register
File
Non-data-capture
scheduling
window
Functional Units
Update & Forwarding
wakeup
Scheduling Atomicity

## Slide 14: Mapping to pipeline stages
AMD K7 (data-capture)
Pentium 4 (non-data-capture)
Data
Data
Data /
wakeup
wakeup
Scheduling Atomicity

## Slide 15: Scheduling atomicity & non-data-capture scheduler
Fetch
Decode
Sched
/Exe
Writeback
Commit
Atomic Sched/Exe
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
Commit
wakeup/
select
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
Commit
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
Commit
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
Commit
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
Commit
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
Commit
Wakeup
/Select
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
Commit
Wakeup
/Select
Multi-cycle scheduling loop
Scheduling atomicity is not maintained
  Separated by extra pipeline stages (Disp, RF)
  Unable to issue dependent instructions consecutively
 solution: speculative scheduling
Scheduling Atomicity

## Slide 16: Speculative Scheduling
Speculatively wakeup dependent instructions even before the parent instruction starts execution
  Keep the scheduling loop within a single clock cycle
But, nobody knows what will happen in the future
Source of uncertainty in instruction scheduling: loads
  Cache hit / miss
  Store-to-load aliasing
   eventually affects timing decisions
Scheduler assumes that all types of instructions have pre-determined fixed latencies
  Load instructions are assumed to have a common case (over 90% in general) $DL1 hit latency
  If incorrect, subsequent (dependent) instructions are replayed
Speculative Scheduling

## Slide 17: Speculative Scheduling
Overview
Spec wakeup
/select
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
/Recover
Commit
Speculatively issued instructions
Re-schedule
when latency mispredicted
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
/Recover
Commit
Speculatively issued instructions
Re-schedule
when latency mispredicted
Spec wakeup
/select
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
/Recover
Commit
Speculatively issued instructions
Re-schedule
when latency mispredicted
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
/Recover
Commit
Speculatively issued instructions
Re-schedule
when latency mispredicted
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
/Recover
Commit
Speculatively issued instructions
Re-schedule
when latency mispredicted
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
/Recover
Commit
Speculatively issued instructions
Re-schedule
when latency mispredicted
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
/Recover
Commit
Speculatively issued instructions
Re-schedule
when latency mispredicted
Latency Changed!!
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
/Recover
Commit
Re-schedule
when latency mispredicted
Invalid input value
Speculatively issued instructions
Fetch
Decode
Schedule
Dispatch
RF
Exe
Writeback
/Recover
Commit
Speculatively issued instructions
Unlike the original Tomasulo’s algorithm
  Instructions are scheduled BEFORE actual execution occurs
  Assumes instructions have pre-determined fixed latencies
    ALU operations: fixed latency
    Load operations: assumes $DL1 latency (common case)
Speculative Scheduling
Notes: This is a very generic out-of-order pipeline that is based on original Tomasulo’s algorithm. In the algorithm, it assumes that ‘as soon as’ the result value becomes available, it wakes up dependent instructions and issues them atomically so that back-to-back execution is possible. However, today’s microprocessors have deeper pipeline to get the higher clock speed and throughput and the distance between writeback stage and the issue stage gets longer. So if we execute two dependent instructions in this pipeline based on the original scheme, we cannot do back-to-back execution and we’ll lose lots of ILP.
So, instead of waking up instructions from writeback stage, there’s a feed back loop where issued instructions speculatively wake up dependent instructions based on the instruction latency. So the previous instruction is issued. it speculatively wakes up dependent instruction, and finally they can execute in back-to-back cycles. If, for example, the first instruction is a load and we found that a cache miss occurred, which means this instruction do not have the correct memory value and it needs more cycles to get the value from memory, so the instruction and the dependent instruction are put again into the scheduler and waiting for the next issue slot.
Unlike the atomic wakeup and select scheduling, speculative scheduling assumes a fixed latency of instruction and schedules dependent instructions based on that.
And also, since resource uses are determined at scheduled time, for instance, even though we found that this load does not have to access the cache in the execution stage, it is impossible to deallocate that scheduled port and use it for other load instructions.

## Slide 18: Scheduling replay
Speculation needs verification / recovery
  There’s no free lunch
If the actual load latency is longer (i.e. cache miss) than what was speculated
  Best solution (disregarding complexity): replay data-dependent instructions issued under load shadow
verification flow
Fetch
Decode
Rename
Queue
Sched
Disp
Disp
RF
RF
Exe
Retire
/ WB
Commit
Rename
instruction flow
Cache miss
detected
Speculative Scheduling—recovery

## Slide 19: Wavefront propagation
Speculative execution wavefront
  speculative image of execution (from scheduler’s perspective)
Both wavefront propagates along dependence edges at the same rate (1 level / cycle)
  the real wavefront runs behind the speculative wavefront
The load resolution loop delay complicates the recovery process
  scheduling miss is notified a couple of clock cycles later after issue
verification flow
Fetch
Decode
Rename
Queue
Sched
Disp
Disp
RF
RF
Exe
Retire
/ WB
Commit
Rename
speculative execution
wavefront
real execution
wavefront
instruction flow
dependence
linking
Data
linking
Speculative Scheduling—recovery

## Slide 20: Issues in scheduling replay
Cannot stop speculative wavefront propagation
  Both wavefronts propagate at the same rate
  Dependent instructions are unnecessarily issued under load misses
checker
Sched
/ Issue
Exe
cache miss
signal
cycle n
cycle n+1
cycle n+2
cycle n+3
Speculative Scheduling—recovery

## Slide 21: Requirements of scheduling replay
Conditions for ideal scheduling replay
  All mis-scheduled dependent instructions are invalidated instantly
  Independent instructions are unaffected
Multiple levels of dependence tracking are needed
  e.g. Am I dependent on the current cache miss?
  Longer load resolution loop delay  tracking more levels
Propagation of recovery status should be faster than speculative wavefront propagation
Recovery should be performed on the transitive closure of dependent instructions
load
miss

## Slide 22: Scheduling replay schemes
Alpha 21264: Non-selective replay
  Replays all dependent and independent instructions issued under load shadow
  Analogous to squashing recovery in branch misprediction
  Simple but high performance penalty
    Independent instructions are unnecessarily replayed
Sched
Disp
RF
Exe
Retire
Invalidate & replay ALL instructions in the load shadow
LD
ADD
OR
AND
BR
LD
ADD
OR
AND
BR
LD
ADD
OR
AND
BR
miss
resolved
LD
ADD
OR
AND
BR
LD
ADD
OR
Cache
miss
AND
BR
Speculative Scheduling—recovery

## Slide 23: Position-based selective replay
Ideal selective recovery
  replay dependent instructions only
Dependence tracking is managed in a matrix form
  Column: load issue slot, row: pipeline stages
merge
matices
ADD
0 0
0 0
0 0
0 1
OR
0 0
0 0
0 0
0 1
SLL
0 0
0 0
0 0
0 1
AND
0 0
0 0
1 0
0 1
XOR
0 0
0 0
1 0
0 0
LD
LD
ADD
OR
XOR
AND
SLL
Integer pipeline
Mem pipeline
(width 2)
Sched
Disp
RF
Exe
Retire
ADD
0 0
0 0
0 1
0 0
OR
0 0
0 0
0 1
0 0
XOR
0 0
1 0
0 0
0 0
LD
LD
OR
AND
SLL
ADD
XOR
SLL
0 0
0 0
0 1
0 0
AND
0 0
1 0
0 1
0 0
tag / dep info
broadcast
kill bus broadcast
killed
killed
killed
killed
Cycle n
Cycle n+1
Sched
Disp
RF
Exe
Retire
1 0
0 1
0 0
1 0
bit merge
& shift
invalidate if bits match
in the last row
tagR
ReadyR
ReadyL
tagL
=
=
Kill bus
tag bus
dependence info bus
Cache miss
Detected
Speculative Scheduling—recovery

## Slide 24: We could also do something more radical
Greatly simplify scheduling in some way.
Misc. “Neat ideas”

## Slide 25: Another scheduling idea: Grandparents
Schedule based on grandparents
J. Stark, M.D. Brown, and Y.N. Patt. “On pipelining dynamic instruction scheduling logic,” ISCA 2000
Misc. “Neat ideas”

## Slide 26: Low-complexity scheduling techniques
FIFO (Palacharla, Jouppi, Smith, 1996)
  Replaces conventional scheduling logic with multiple FIFOs
    Steering logic puts instructions into different FIFOs considering dependences
    A FIFO contains a chain of dependent instructions
    Only the head instructions are considered for issue
Misc. “Neat ideas”

## Slide 27: FIFO (cont’d)
Scheduling example
Misc. “Neat ideas”

## Slide 28: FIFO (cont’d)
Performance
Comparable performance to the conventional scheduling
Reduced scheduling logic complexity
Many related papers on clustered microarchitecture
Can in-order clusters provide high performance?
Misc. “Neat ideas”

## Slide 29: Key Challenge: MLP (Memory-Level Parallelism)
Tolerate/overlap memory latency
  Once first miss is encountered, find another one
Naïve solution
  Implement a very large ROB, LSQ
  Power/area/delay make this infeasible
Build virtual instruction window
  How to do this?
Misc. “Neat ideas”

## Slide 30: Check point
Key notion is we need to be able to recover when we get a mis-speculation (or exception or other nuke situation)
  How about just storing a check point every X instructions (say 100).
    If there is a nuke, back up to check point and move forward with either
      Knowledge of issue (predict correctly this time) OR
      Carefully (in-order?).
    Don’t let stores write to memory until get to next check point.
Misc. “Neat ideas”

## Slide 31: Sources and Further Reading
I. Kim and M. Lipasti, “Understanding Scheduling Replay Schemes,” in Proceedings of the 10th International Symposium on High-performance Computer Architecture (HPCA-10), February 2004.
Srikanth Srinivasan, Ravi Rajwar, Haitham Akkary, Amit Gandhi, and Mike Upton, “Continual Flow Pipelines”, in Proceedings of ASPLOS 2004, October 2004.
Ahmed S. Al-Zawawi, Vimal K. Reddy, Eric Rotenberg, Haitham H. Akkary, “Transparent Control Independence,” in Proceedings of ISCA-34, 2007.
T. Shaw, M. Martin, A. Roth, “NoSQ: Store-Load Communication without a Store Queue, ” in Proceedings of the 39th Annual IEEE/ACM International Symposium on Microarchitecture, 2006.
Andrew Hilton, Santosh Nagarakatte, Amir Roth, "iCFP: Tolerating All-Level Cache Misses in In-Order Processors," Proceedings of HPCA 2009.
J. Stark, M.D. Brown, and Y.N. Patt. “On pipelining dynamic instruction scheduling logic,” ISCA 2000