## Slide 3
module compute_next_state(
input wire [2:0] state,
output reg [2:0] next_state);
always @* begin
next_state = state_reset;
case (state)
state_reset: begin
next_state = _____________;
end
state_pour: begin
next_state = _____________;
end
state_mix: begin
next_state = _____________;
end
state_bake: begin
next_state = _____________;
end
state_end: begin
next_state = _____________;
end
endcase
end
endmodule

## Slide 4
parameter state_reset = 3'h0;
parameter state_pour = 3'h1;
parameter state_mix = 3'h2;
parameter state_bake = 3'h3;
parameter state_end = 3'h4;
module state_register(
input wire clock,
input wire reset,
input wire [2:0] data_in,
output reg [2:0] data_out);
always @(posedge clock) begin
if (reset == 1'b1) begin
data_out <= state_reset;
end else begin
data_out <= data_in;
end
end
endmodule

## Slide 5
module top(
input wire reset,
input wire clock);
wire [2:0] next_state;
wire [2:0] state;
state_register u1 (clock, reset, next_state, state);
compute_next_state u2 (state, next_state);
endmodule

## Slide 6
module compute_next_state(
input wire [2:0] state,
input wire smoke,
output reg [2:0] next_state);
always @* begin
next_state = state_reset;
case (state)
state_reset: begin
next_state = state_pour;
end
state_pour: begin
next_state = state_mix;
end
state_mix: begin
next_state = state_bake;
end
Continued on next page

## Slide 7
state_bake: begin
if (smoke == 1’b0) begin
next_state = state_bake;
end else begin
next_state = state_end;
end
state_end: begin
next_state = state_end;
end
endcase
end
endmodule

## Slide 8
always @* begin
next_state = state_reset;
case (state)
state_reset: begin
pourer = 1'b0;
mixer = 1'b0;
oven = 1'b0;
next_state = state_pour;
end
state_pour: begin
pourer = 1'b1;
mixer = 1'b0;
oven = 1'b0;
next_state = state_mix;
end
state_mix: begin
pourer = 1'b0;
mixer = 1'b1;
oven = 1'b0;
next_state = state_bake;
end
state_bake: begin
pourer = 1'b0;
mixer = 1'b0;
oven = 1'b1;
if (smoke == 1'b0) begin
next_state = state_bake;
end else begin
next_state = state_end;
end
end
state_end: begin
pourer = 1'b0;
mixer = 1'b0;
oven = 1'b0;
next_state = state_end;
end
endcase
end

## Slide 9
always @* begin
pourer = 1'b0;
mixer = 1'b0;
oven = 1'b0;
next_state = state_reset;
case (state)
state_reset: begin
next_state = state_pour;
end
state_pour: begin
pourer = 1'b1;
next_state = state_mix;
end
state_mix: begin
mixer = 1'b1;
next_state = state_bake;
end
state_bake: begin
oven = 1'b1;
if (smoke == 1'b0) begin
next_state = state_bake;
end else begin
next_state = state_end;
end
end
state_end: begin
next_state = state_end;
end
endcase
end

## Slide 10
always @* begin
address_write = 1'b0;
mem_write = 1'b0;
next_state = state_reset;
case (state)
state_reset: begin
next_state = state_decide;
end
state_decide: begin
if (start == 1'b0) begin
next_state = state_decide;
end else if (type == 1'b0) begin
next_state = state_read1;
end else begin
next_state = state_write1;
end
end

## Slide 11
state_read1: begin
// write memory address register
address_write = 1'b1;
next_state = state_decide;
end
state_write1: begin
// write memory address register
address_write = 1'b1;
next_state = state_write2;
end
state_write2: begin
// write memory
mem_write = 1'b1;
next_state = state_decide;
end
endcase
end

## Slide 12
element
max
i
greater_out
memory
address
data
equal16_out
greater
equal16
plus1

## Slide 13
loop if (i==16) goto end
read1 memory_address = i
read2 element = mem[i]
compare if (element > max) goto write_max, else goto increment
write_max max = element
increment i = i+1; goto loop
end goto end

## Slide 14
state | greater_ out | equal16_ out | next_ state | element_ write | element_ drive | max_ write | i_ write | i_ drive | plus1_ drive | mem_ drive | addr_ write
reset |  |  | loop |  |  |  |  |  |  |  | 
loop |  | 1 | end |  |  |  |  |  |  |  | 
loop |  | 0 | read1 |  |  |  |  |  |  |  | 
read1 |  |  | read2 |  |  |  |  | 1 |  |  | 1
read2 |  |  | compare | 1 |  |  |  |  |  | 1 | 
compare | 1 |  | write_max |  |  |  |  |  |  |  | 
compare | 0 |  | increment |  |  |  |  |  |  |  | 
write_max |  |  | increment |  | 1 | 1 |  |  |  |  | 
increment |  |  | loop |  |  |  | 1 |  | 1 |  | 
end |  |  | end |  |  |  |  |  |  |  | 

## Slide 15
always @* begin
element_write = 1'b0;
element_drive = 1'b0;
max_write = 1'b0;
i_write = 1'b0;
i_drive = 1'b0;
plus1_drive = 1'b0;
memory_write = 1'b0;
memory_drive = 1'b0;
address_write = 1'b0;
next_state = state_reset;
case (state)
state_reset: begin
next_state = state_loop;
end
state_loop: begin
// if i is 16, then we're done
if (equal16_out == 1'b1) begin
next_state = state_end;
end else begin
next_state = state_read1;
end
end

## Slide 16
state_read1: begin
// transfer i to memory address
i_drive = 1'b1;
address_write = 1'b1;
next_state = state_read2;
end
state_read2: begin
// read memory[i]
memory_drive = 1'b1;
element_write = 1'b1;
next_state = state_compare;
end
state_compare: begin
// is memory[i] more than the current max?
if (greater_out == 1'b1) begin
next_state = state_write_max;
end else begin
next_state = state_increment;
end
end

## Slide 17
state_write_max: begin
// update max
element_drive = 1'b1;
max_write = 1'b1;
next_state = state_increment;
end
state_increment: begin
// increment i
plus1_drive = 1'b1;
i_write = 1'b1;
next_state = state_loop;
end
state_end: begin
next_state = state_end;
end
endcase
end

## Slide 18: top.v (partial)
register u3 (clock, reset, element_write, bus, element_out);
register u4 (clock, reset, max_write, bus, max_out);
register u5 (clock, reset, i_write, bus, i_out);
greater u6 (element_out, max_out, greater_out);
equal16 u7 (i_out, equal16_out);
plus1 u8 (i_out, plus1_out);
ram u9 (bus, ~address_write, clock, bus, memory_write, memory_out);
tristate u10 (element_out, bus, element_drive);
tristate u11 (plus1_out, bus, plus1_drive);
tristate u12 (i_out, bus, i_drive);
tristate u13 (memory_out, bus, memory_drive);
// display max on HEX2, HEX3
hexdigit u16 (max_out[3:0], HEX2);
hexdigit u17 (max_out[7:4], HEX3);
control u18 (clock, reset, greater_out, equal16_out, element_write, element_drive, max_write, i_write, i_drive, plus1_drive, memory_write, memory_drive, address_write);

## Slide 19: greater.v
module greater(
input wire [7:0] in1,
input wire [7:0] in2,
output reg out);
always @* begin
if (in1 > in2) begin
out = 1'b1;
end else begin
out = 1'b0;
end
end
endmodule