## Slide 1
state | READ | WRITE | next_state | mem_write | address_write
state_decide | 1 |  | state_read1 | 0 | 0
state_decide | 0 | 1 | state_write1 | 0 | 0
state_decide | 0 | 0 | state_decide | 0 | 0
state_read1 |  |  | state_decide | 0 | 1
state_write1 |  |  | state_write2 | 0 | 1
state_write2 |  |  | state_decide | 1 | 0

## Slide 2
always @* begin
case (state)
state_decide: begin
address_write = 1'b0;
mem_write = 1'b0;
if (READ == 1'b1) begin
next_state = state_read1;
end else if (WRITE == 1'b1) begin
next_state = state_write1;
end else begin
next_state = state_decide;
end
end

## Slide 3
state_read1: begin
address_write = 1'b1;
mem_write = 1'b0;
next_state = state_decide;
end
state_write1: begin
address_write = 1'b1;
mem_write = 1'b0;
next_state = state_write2;
end
state_write2: begin
address_write = 1'b0;
mem_write = 1'b1;
next_state = state_decide;
end
endcase
end

## Slide 4
parameter state_decide = 2’h0;
parameter state_read1 = 2’h1;
parameter state_write1 = 2’h2;
parameter state_write2 = 2’h3;
always @(posedge clock) begin
if (reset == 1'b1) begin
state <= state_decide;
end else begin
state <= next_state;
end
end

## Slide 5
element
max
i
greater_out
memory
address
data
equal16_out
greater
equal16
plus1

## Slide 6
loop if (i==16) goto end
read1 memory_address = i
read2 element = mem[i]
compare if (element > max) goto write_max, else goto increment
write_max max = element
increment i = i+1; goto loop
end goto end

## Slide 7
state |  |  |  |  |  |  |  |  |  |  | 

## Slide 8
state |  |  |  |  |  |  |  |  |  |  | 

## Slide 9
always @* begin
element_write = 1'b0;
element_drive = 1'b0;
max_write = 1'b0;
i_write = 1'b0;
i_drive = 1'b0;
plus1_drive = 1'b0;
memory_write = 1'b0;
memory_drive = 1'b0;
address_write = 1'b0;
next_state = state_reset;
case (state)
state_reset: begin
next_state = state_loop;
end
state_loop: begin
// if i is 16, then we're done
if (equal16_out == 1'b1) begin
next_state = state_end;
end else begin
next_state = state_read1;
end
end

## Slide 10
state_read1: begin
// transfer i to memory address
i_drive = 1'b1;
address_write = 1'b1;
next_state = state_read2;
end
state_read2: begin
// read memory[i]
memory_drive = 1'b1;
element_write = 1'b1;
next_state = state_compare;
end
state_compare: begin
// is memory[i] more than the current max?
if (greater_out == 1'b1) begin
next_state = state_write_max;
end else begin
next_state = state_increment;
end
end

## Slide 11
state_write_max: begin
// update max
element_drive = 1'b1;
max_write = 1'b1;
next_state = state_increment;
end
state_increment: begin
// increment i
plus1_drive = 1'b1;
i_write = 1'b1;
next_state = state_loop;
end
state_end: begin
next_state = state_end;
end
endcase
end

## Slide 12: top.v (partial)
register u3 (clock, reset, element_write, bus, element_out);
register u4 (clock, reset, max_write, bus, max_out);
register u5 (clock, reset, i_write, bus, i_out);
greater u6 (element_out, max_out, greater_out);
equal16 u7 (i_out, equal16_out);
plus1 u8 (i_out, plus1_out);
ram u9 (bus, ~address_write, clock, bus, memory_write, memory_out);
tristate u10 (element_out, bus, element_drive);
tristate u11 (plus1_out, bus, plus1_drive);
tristate u12 (i_out, bus, i_drive);
tristate u13 (memory_out, bus, memory_drive);
// display max on HEX2, HEX3
hexdigit u16 (max_out[3:0], HEX2);
hexdigit u17 (max_out[7:4], HEX3);
control u18 (clock, reset, greater_out, equal16_out, element_write, element_drive, max_write, i_write, i_drive, plus1_drive, memory_write, memory_drive, address_write);

## Slide 13: greater.v
module greater(
input wire [7:0] in1,
input wire [7:0] in2,
output reg out);
always @* begin
if (in1 > in2) begin
out = 1'b1;
end else begin
out = 1'b0;
end
end
endmodule