Modbus-IDA Conformance Test Group

Issues in Achieving Sister Conformance Test Laboratory Consistency

# Revision Control

| Date | Version | Name | Edits |
| --- | --- | --- | --- |
| 14 August 2004 | 0.1 | Parrott | Initial Outline |
| 22 August | 0.2 | Moyne | Formalization of document, review and expansion; Additions in Blue |

# Introduction:

As the Modbus protocol and Modbus-IDA conformance test laboratory policies mature, a need has been identified to establish a sister conformance test laboratory in China.  It is critical that the test policies in these two laboratories be aligned such that the following requirement be met:

Requirement R-1:  All sister laboratories in an international network will always produce the same results and recommendations for any Modbus Device Under Test (DUT).

This documents provides a listing of issues that must be addressed in order to meet requirement R-1.  It is suggested that these issues be reformatted into a checklist that will aid in laboratory commissioning.

# Issues:

## Devices

- All Modbus Devices Used in Testing (amount and type)

  - Same firmware release

  - Conformance tested (plus extra testing?)

  - Documentation of device, firmware, software and conformance test results

  - Coordination of any upgrades to device (HW, FW, SW or conformance testing

## Networks

- Network architecture

  - Cabling, Switch/Hub, Bridge, Repeaters setup documented and “consistent”

  - Consistency in any “long” network segments

  - Standard delay and loading tests should yield consistent results

## Hardware

- Same bridge devices if possible

- Same specifications of any other hardware (power supplies, O-scopes, etc.)

## Interoperability Network

- Documentation of hardware as defined above; networks do not have to be exactly the same with respect to conformant devices.

- Should consist of 100% conformance tested devices.

  - If not possible, then board should have the exact same layout of non-conformant devices.

## Computers

- Same OS and similar configurations and speeds if possible.

- Full documentation of computer configurations.

## Software

- Same version of test software (protocol and interoperability), documented, with revision control.

- Full documentation of computer configurations.

## Testing Procedures

- Standardization of documented test procedures (protocol test specification is sufficient?) with revision control.

- Clear definition of “test engineer liberties”, i.e., test engineer investigation procedures translation to test result.

- Clear definition of any iron-man testing (lengths, etc.).

- Clear definition of test order in procedure.

## Infrastructure

- Consistency in the following:

  - Test procedures

  - Device submission and preparation procedures

  - Results documentation procedure

  - Results reporting procedures

  - Database infrastructure for client and results tracking, etc.

  - Privacy policies

- Web sites should have same content (though in different languages), especially with respect to the above infrastructure topics.

- Policies established for consistent upgrade of HW and SW.

## Ramp-up

- Establish check-list for above issues

- On-site commissioning

  - Check-list execution

  - Side-by side testing for consistency evaluation

  - Separate testing and consistency verification on good device and bad device

- Older established lab to pre-verify new lab results for first few device tests

## Consistency Maintenance

- Policy established for (perhaps yearly) confirmation of consistency (check-list plus ramp-up type of (re) verification mechanisms).