## Slide 1
*
EECS 373
Design of Microprocessor-Based Systems
Nathan Heidt
Jonathan Bendes
Paul Doerr
University of Michigan
Quadcopter systems
November 27, 2012

## Slide 2: Outline
*
Why do we care?
What is a quadcopter
How does it work
Quadcopter systems
Choosing a quadcopter's parts
Looking Forward

## Slide 3: Why do we care?
*

## Slide 4: Why do we care?
*

## Slide 5: Why do we care?
*

## Slide 6: What is a quadcopter
"A quadrotor, also called a quadrotor helicopter or quadcopter, is a multicopter that is lifted and propelled by four rotors."
- Wikipedia
Similar to a standard single rotor helicopter
Very stable design
Simpler control from standard helicopter
Good for radio and autonomous control

## Slide 7: What is a quadcopter

## Slide 8: What is a quadcopter

## Slide 9: Quadcopter Sub-Systems
Motors
Sensors
Propellors
Airframe
Controllers

## Slide 10: Quadcopter Construction
Arm - Part that holds the motors
Center plate - main support: holds arms, batteries, and controllers
Landing Skid - attached to the arms, cushions landings

## Slide 11: How does it work - basic physics
  Adjacent Rotors spin opposite directions to maintain constant heading
  4 points of lift allow for control of roll, pitch, yaw, and height
  Enables quadrotors to maneuver in 3 dimensions
  Simple physics allows for simple flight controller
  Increased stability allows for higher level
robotics (Autonomy)

## Slide 12: How does it work - control systems
Closed-loop controllers - use feedback data from IMU to control each rotor
PID controller - uses the error between current position data and desired position to drive outputs
    P - proportional
    I - integral
    D - derivative
  Nonlinear controllers - more complex, could lead to more precise control
radhesh.wordpress.com

## Slide 13: How does it work - PID Gone Wrong

## Slide 14: How does it work - Sensors
IMU - combination gyro/accelerometer
  Collects data for 6 degrees of freedom
  9 DOF IMUs add 3 degree magnetometer
Camera
  Useful for radio control, analyzing
environment
LIDAR
  Uses laser to find distance to closest obstacles
  Expensive, invaluable for autonomous control
  Use SLAM to map surroundings

## Slide 15: How does it work – SLAM

## Slide 16: How does it work - Level Flight Waypoint Following

## Slide 17: Choosing quadcopter parts - body of quadcopter
*
Choose between two configurations x and +
take into account payloads
  i.e. batteries, sensors, control systems, etc
Choose a proper size for the application
  larger size means bigger motors are necessary
  smaller means more maneuverable but unable to carry as much
Materials
  wood is cheap but not as durable as other materials
  carbon fibre is strong and incredibly light but expensive
  Aluminum is durable and cheap but can be heavier than other materials
Notes: 1. push {r7, lr} => pushes the {register list} onto the stack
2. mov.w r3, #40 ; 0x28 =>
*

## Slide 18: Choosing quadcopter parts - body of quadcopter cont.
*
Choosing the right balance of parts is important to manage three essential elements
  cost, weight, and durability
Each element has a tradeoff
  The higher the price, often the lighter and more durable
A large quadcopter is going to be heavier and will require larger motors
  This in turn requires larger or better batteries
Heavier quadrotors tend to run for shorter amounts of time on standard systems
The primary things to consider are the size and weight of the payload as well as the budget allocated to the project
Notes: 1. push {r7, lr} => pushes the {register list} onto the stack
2. mov.w r3, #40 ; 0x28 =>
*

## Slide 19: Choosing quadcopter parts - motors and ESC
*
Typically brushless motors
ESC depends on motor ratings i.e. kV and max current
Motors must have sufficient thrust to lift the quadrotor
  kV = RPM/V at no load
  Total max thrust should be double the weight
ESC current supply rating must be higher than that of the motor
  typically given by: ESC = 1.2-1.5 x max amp rating of motor
Notes: 1. push {r7, lr} => pushes the {register list} onto the stack
2. mov.w r3, #40 ; 0x28 =>
*

## Slide 20: Choosing quadcopter parts - Sensors
*
IMU's are a large consideration for stability
Important factors include refresh rate and degrees of freedom (DOF)
6DOF vs 9DOF
  6DOF contains an accelerometer and a gyrometer
  9DOF has the addition of a magnetometer
Large range of quality (i.e. mems to fiber-optic gyro)
The added magnetometer is beneficial for navigation
  Noise becomes an issue
Notes: 1. push {r7, lr} => pushes the {register list} onto the stack
2. mov.w r3, #40 ; 0x28 =>
*

## Slide 21: Choosing quadcopter parts - Additional Sensors
*
Ultrasonic sensors (obstacles and height feedback)
Downwards facing cameras for hovering stability
GPS for navigation
Radio for control
Notes: 1. push {r7, lr} => pushes the {register list} onto the stack
2. mov.w r3, #40 ; 0x28 =>
*

## Slide 22: Choosing a quadcopter
*
There are several pre made quadcopters and kits available
  many are well designed and priced
Considerations to make between buying a pre made and building a custom quadcopter include:
  customizeability
  budget
  intended use
When buying a pre made quadcopter or a kit look at the specifications
Notes: 1. push {r7, lr} => pushes the {register list} onto the stack
2. mov.w r3, #40 ; 0x28 =>
*

## Slide 23: Looking forward
*
Quadcopters are a very popular robotics platform
There are hundreds of designs to choose from and more to create
There is a range of prices they can be purchased for
  low end models can be less than 200$
Many practical applications
Straightforward design and control
Notes: 1. push {r7, lr} => pushes the {register list} onto the stack
2. mov.w r3, #40 ; 0x28 =>
*

## Slide 24
*
Questions?
Comments?
Discussion?

## Slide 25
Sources
http://www.towerhobbies.com/products/heli-max/hmxe0835/hmxe0835_550.jpg
http://thequadcopterguy.blogspot.com/p/choosing-your-parts.html
http://en.wikipedia.org/wiki/Quadrotor
http://radhesh.wordpress.com
http://upload.wikimedia.org/wikipedia/commons/thumb/f/fa/6DOF_en.jpg/330px-6DOF_en.jpg
http://static.geekbeat.tv/wp-content/uploads/2012/02/ardrone2.0.png
http://www.rcmodelpart.com/images/v/201209/13470012980.jpg
http://www.hobbytronics.co.uk/image/data/sparkfun/imu_fusion_imu3000.jpg
http://www.kvh.com/~/media/Images/KVH/Product/Gyros%20IMUs/TG6000%20IMU/prod_tg6000.ashx?bc=white
http://www.parallax.com/Portals/0/Images/Prod/2/280/28015-M.jpg
http://zedomax.com/image/200611/parallax_gps.gif