## Slide 1
EECS 373
Design of Microprocessor-Based Systems
Student Presentations
Tianhua Zheng and Jason Shintani
Motor control
November 27th, 2012

## Slide 2: Announcements
Today is a good day!
Motors are awesome!

## Slide 3: Outline
Minute quiz
Announcements
Special purpose motors (servos, steppers, actuators)
H-bridge
CEMF

## Slide 4: Servo Motors
A motor that has an on-board electric circuit for controlling the direction of rotation, as well as the position, of the output shaft.
Typical rotation range: 90 degrees or 180 degrees
Typical price range: $10 to 10’s of $1,000.
Notes: http://embedded-lab.com/blog/?p=4653
http://www.lirtex.com/robotics/servo-motors-information-and-control/

## Slide 5: Servo Motor Control
Closed loop control
  Measure the exact position of the motor head
  Fix the gaps from the desired position by controlling the motor
Control signal: PWM
  Operate between 4.8V and 6V
  Generally @ 50Hz

## Slide 6: Example PWM for servo
The position of the motor is not determined by duty cycle but the high time. Typically 1.5ms high corresponds to the neutral position.

## Slide 7: Usage of Servo Motors
Used in a wide variety of application
  Robotic arms
  Toy-cars, air-planes and helicopters
  Industrial machinery
Easy to control
  Only need PWM signal
Low energy consumption
  Works in closed loop
Small Size
  As small as several inches squared

## Slide 8: Torque vs. cost
Chart: 
| 53.25 | 44.05 | 41.01 | 103.82 | 159.82 | 122.26 | 119.49 | 183.23 | 193.27
Cost of Torque - Servo Motor | 0.02 | 0.02 | 0.02 | 1.5 | 7.4 | 9.8 | 19.6 | 58.8 | 68.8

## Slide 9: Stepper Motor
A brushless DC electric motor that divides a full rotation into a number of equal steps
Offers precise rotation control and relatively high rotational speed
  Generally can turn in 0.9 to 1.8 degree in each direction
Unipolar and Bipolar, or Hybrid
  Difference in the way the electromagnets are connected
  Different control methods

## Slide 10: Stepper Motor Control
“Single-Step” controlling method
“Double-Step” controlling method
“Half-Step” stepping method

## Slide 11: Stepper Motor Control
Need controller to generate waveform to drive the stepper motor
Discrete Transitions

## Slide 12: Usage of Stepper Motor
Used in a wide variety of application in industry
  Computer Peripherals
  Business Machines
And also in everyday life
  BBQ grill
  Stage intelligent light systems
  Power windows and power seats
High positioning accuracy, large torque, reliability.

## Slide 13: Torque vs. cost
Chart: 
| 45.33 | 45.33 | 46.14 | 46.14 | 46.14 | 51.81 | 51.81 | 51.81 | 51.81 | 57.54 | 57.54 | 75.97 | 80.02 | 84.07 | 88.93 | 97.03
Cost of Torque | 160 | 170 | 260 | 270 | 270 | 330 | 330 | 340 | 340 | 480 | 480 | 580 | 820 | 900 | 1200 | 1550

## Slide 14: Outline
Minute quiz
Announcements
Special purpose motors (servos, steppers, actuators)
H-bridge
CEMF

## Slide 15: H-bridge
A set of four switches, mechanical or solid-state, with series pairs in parallel.
Used to provide direction control for DC motors.
Often found in IC packages.
DC brushed motors

## Slide 16: H-bridge speed control
Control signal: PWM
  Unlike servos, H-bridges use PWM to regulate power supplied to the motor.
  This can be correlated to speed if the mechanical load is know or thru closed-loop feedback from a quadrature encoder.
  50,000Hz – 60,000Hz
PWM generation
  The PWM signal is generated by switching one of the two switches that have current flowing.
  For example, if the motor from the previous slide was running right, 1001, PWM’ing S1 would limit the current to the motor.

## Slide 17: 1001 - Forward

## Slide 18: 0110 - Reverse

## Slide 19: 1100, 0011, 1111 – Shoot thru

## Slide 20: H-bridge components and application
A motor controller that supports power (speed) control is made of four MOSFET’s or BJT’s.
  Typically, N-Channel MOSFET’s are chosen because of their low source to drain resistance.
  Solid-state switches are chosen because they allow for higher switching frequencies and wear less on each individual throw (no sparks).
Mechanical switches are much cheaper but do not allow for effective power (speed) control.

## Slide 21: H-bridge application

## Slide 22: Non H-bridge applications
Servos
Stepper motors
Non-reversible configurations
AC motors
DC brushless motors

## Slide 23: Outline
Minute quiz
Announcements
Special purpose motors (servos, steppers, actuators)
H-bridge
CEMF

## Slide 24: Counter-electromotive force (CEMF)
When dealing with high-current DC motors CEMF must be considered.
  CEMF is a product of Faraday’s Law of Induction and Lenz’s Law.
  The CEMF is created by the spinning armatures.
  The CEMF is how motors are also generators.
Why is this important?
  Because large motors will generate large CEMF induced currents.
    If the H-bridge goes into a breaking state care must be taken to properly divert and dissipate the current.
CEMF can also be used to sense speed and load.

## Slide 25: 0101 - Break

## Slide 26: 0110 1100 - Possible break circuit

## Slide 27: Thank You!

## Slide 28: Servo Motor VS. Stepper Motor

## Slide 29: DC brushless motor
Notes: Note the CEMF