## Slide 1: DynaMOS: Dynamic Schedule Migration for Heterogeneous Cores
Shruti Padmanabha, Andrew Lukefahr, Reetuparna Das, Scott Mahlke
Micro-48, Waikiki, Hawaii
December 14, 2015
University of Michigan
Electrical Engineering and Computer Science

## Slide 2
Program
Order
Dependency
Graph
1
2
3
4
5
6
1
2
3
4
5
6
1
2
3
5
6
4
1
2
3
4
5
6
2-wide
In-order (InO) Execution
2-wide
Out-of-order
(OoO) Execution
Reordering instructions  2x performance!
Reordering hardware  6x power!
Notes: OoO achieves optimal schedules for its resources
At the cost of power-hungry hardware
- ROB, RAT, Issue logic

## Slide 3: Redundancy on OoO
Code repeats!
Create optimal reordered schedule!
OoO
Core
Redundantly
  90% probability of creating similar schedules for 70% of traces!
Program
Traces

## Slide 4: Objective
Expose and eliminate wasteful work on the expensive OoO hardware
Without significantly hurting performance

## Slide 5: Background: Heterogeneity In Hardware
Many hardware designs of varying capabilities on the same chip
  OoOs, In-orders, Accelerators, FPGAs…
Most efficient hardware chosen for application
ARM’s big.LITTLE, Nvidia’s Tegra-3, Intel Xeon+FPGA, AMD Fusion…

## Slide 6: Background: Fine-grained Heterogeneous Architectures
*Composite Cores: Pushing Heterogeneity into a Core, Lukefahr et al, Micro 2012
OoO
Backend
InO
Backend
RF
RF
Shared Frontend
L2$
L1$
Minimize transfer overhead
Allow application migration at the granularity of 100s of instructions
Controller

## Slide 7: DynaMOS: Dynamic Schedule Migration for Heterogeneous Cores
InO
Backend
Program
Traces
OoO
Backend
Trace
$
Memoize!
Achieve near OoO performance with near InO hardware!

## Slide 8: Motivation - Oracle
Chart: % Execution on InO
| astar | bzip2 | gcc | gobmk | h264ref | hmmer | libquantum | mcf | omnetpp | perlbench | sjeng | xalancbmk | cactusADM | calculix | gromacs | milc | namd | wrf | leslie3d | bwaves | povray | dealII | GemsFDTD | gamess | tonto | zeusmp | average
No Memoization | 0.5411 | 0.2025 | 0.4998 | 0.6073 | 0.2227 | 0.1197 | 0.177 | 0.4785 | 0.6304 | 0.4702 | 0.612 | 0.4169 | 0.194 | 0.3661 | 0.2079 | 0.2669 | 0.2608 | 0.3026 | 0.218 | 0.4017 | 0.2241 | 0.3272 | 0.2791 | 0.1535 | 0.2349 | 0.2231 | 0.30002
With Memoization | 0.6408 | 0.9017 | 0.9454 | 1 | 0.7787 | 0.5959 | 0.6961 | 0.7434 | 0.9802 | 0.9629 | 0.9707 | 0.8643 | 0.8691 | 0.78 | 0.8109 | 0.6976 | 0.9336 | 0.7193 | 0.6368 | 0.9192 | 0.845 | 0.7501 | 0.9592 | 0.553 | 0.8389 | 0.8226 | 0.80568
Performance loss capped at 5%
  Benchmarks with unpredictable control/data flow are not memoizable
  Memoization works for regular benchmarks with predictable control/data flow
  DynaMOS can potentially execute 80% of the application on an InO core, to achieve 95% of an OoO core’s performance

## Slide 9: DynaMOS: Challenges
InO
Backend
OoO
Backend
Trace
$
L1
I$
Trace generation & Selection
Detect profitable traces to memoize – Intelligent trace-based predictor
1
1
Determine a trace boundary
Find repeatability in schedules
Determine profitability of memoizing a trace

## Slide 10: DynaMOS: Challenges
InO
Backend
OoO
Backend
Trace
$
L1
I$
Trace generation & Selection
OinO HW
Guarantee correct execution of reordered schedule on InO – OinO mode
Detect profitable traces to memoize – Intelligent trace-based predictor
1
2
1
2

## Slide 11: Designing the OinO Mode
Correctness Factor | OoO | OinO
Memory disambiguation detection | Load Store Queue | Specialized LSQ
False register dependencies | Register renaming | 2 – level renaming
Divergence from predicted behavior or interrupts | Reorder buffer and Register Alias Table | Atomic commit
2
Fetch
Decode
Back-end
LSQ
PRF
InO Core
Trace Commit
Trace complete?
*Modifications for OinO mode are shaded in blue
a
b

## Slide 12: Handling False Dependencies
a
Seq # | Original Assembly
1(HEAD) | ldr r2, [r2]
2 | add r5, r2, #4
3 | ldr r2, [r3]
Memoized Trace on OinO
ldr r2.1, [r2.0]
ldr r2.2, [r3.0]
add r5.1, r2.1, #4
True Dependency (RAW)!
False Dependency (WAW)!
OoO reorders independent instructions
Seq # | After Reordering on OoO
1(HEAD) | ldr r2, [r2]
3 | ldr r2, [r3]
2 | add r5, r2, #4
Level 1:
Intra trace dependencies
Done on the OoO
PR 2
2.0
2.1
2.2
2.3
Physical Register File
Access indexed physical location
Constraint:
Only 4 PR per Arch Register!
Overhead:
Bigger PRF on InO!

## Slide 13: Handling False Dependencies
a
IT | Memoized Trace on OinO
 | ldr r2.1, [r2.0]
I | ldr r2.2, [r3.0]
 | add r5.1, r2.1, #4
Level 2:
Inter trace dependencies
Done by the OinO
PR 2
2.0
2.1
2.2
2.3
Physical Register File
 | ldr r2.1, [r2.0]
II | ldr r2.2, [r3.0]
 | add r5.1, r2.1, #4
Committed Offset Ptr
Rotating
PR 2
2.2
2.3
2.0
2.1

## Slide 14
Handling memory disambiguation
Seq # | Prog Order (Mem)
0 | Str 1
1 | Ld 1
2 | Str 2
3 | Ld 2
4 | Ld 3
Memoized Trace (Mem)
Ld 3
Str 2
Ld 1
Ld 2
Str 1
Seq #
4
2
1
3
0
Load/Store Queue |  |  |  | 
4 | 3 | 2 | 1 | 0
(iv) Allocate OinO LSQ entries in
Seq # Order
(iii) Trace Memoized In Tr$
(ii) Encode Mem Position With Trace
(v) Check Younger Mem Ops for Aliasing
(i) Trace Selected by OoO
Str 2
Ld 3
b
Overhead:
LSQ structure and Seq# table per trace

## Slide 15: Evaluation Methodology
Architectural Feature | Parameters
Big Core | 3 wide O3 @ 2GHz 12 stage pipeline 128 ROB Entries 128 entry PRF, 32 entry LSQ
Little Core | 3 wide InOrder @ 2GHz 8 stage pipeline 128 entry PRF, 32 entry LSQ
Memory System | 32 KB L1 i/d cache, 2 cycle access 4KB Trace cache, 1 cycle access 1MB L2 cache, 15 cycle access 1GB Main Mem, 80 cycle access
Simulator | Gem5
Energy Model | McPAT
Benchmarks | SPEC 2k6, compiled for ARM ISA Simulated for a total of 108 simpoints of 300M instructions each
  Overheads:
  Hardware overheads induce 8% increase in the power of InO
  4kB Trace $ adds 10% to the leakage energy

## Slide 16
Utilization of Little
Bar 2 = DynaMOS
(With Memoization)
Bar 1 = Composite Core
(No Memoization)
Chart: % Execution On InO
| average | astar | bzip2 |
%Big | 0.86914 | 0.62486 | 0.85282 | 0.83536 | 0.8587 | 0.22404
%InO mode | 0.13074 | 0.097672 | 0.14718 | 0.14398 | 0.1413 | 0.12843
%OinO mode | 0 | 0.27747 | 0 | 0.020667 | 0 | 0.64753
  Worst-case DynaMOS performance ~ Composite Cores
  Little executes both low-performance traces and traces with high memoizability
Performance loss capped at 5%
%OoO
%InO
%OinO

## Slide 17
Energy Savings
Chart: 
| astar | bzip2 | gcc | gobmk | h264ref | hmmer | libquantum | mcf | omnetpp | perlbench | sjeng | xalancbmk | bwaves | cactusADM | calculix | dealII | gamess | GemsFDTD | gromacs | leslie3d | milc | namd | povray | tonto | wrf | zeusmp | average
DynaMOS | 0.21424 | 0.42247 | 0.30812 | 0.32828 | 0.25472 | 0.2998 | 0.35325 | 0.23791 | 0.53319 | 0.38225 | 0.28199 | 0.29901 | 0.31092 | 0.16456 | 0.34709 | 0.32311 | 0.23408 | 0.37907 | 0.4693 | 0.21687 | 0.30363 | 0.35402 | 0.2817 | 0.44479 | 0.35693 | 0.39473 | 0.31614

## Slide 18: Additional Results in the Paper
Sensitivity studies to different microarchitecture configurations of OoO and InO
  Equal widths in both cores allows the simplest memoization, leading to best results
Comparison studies to Loop Caches and Execution Caches
  Switching over the InO core saves the most energy
Sensitivity studies to the size of the Trace Cache and various other constraints imposed in OinO

## Slide 19: Summary
Out-of-order cores create similar schedules for repeating code
  Wasteful use of expensive resources
DynaMOS: Exploit fine-grained heterogeneity to allow sharing of OoO schedules with InO cores
  Allows 32% energy savings over only an OoO core with a 5% performance loss
More details and comparison to related work in the paper

## Slide 20
DynaMOS: Dynamic Schedule Migration for Heterogeneous Cores
Shruti Padmanabha, Andrew Lukefahr, Reetuparna Das, Scott Mahlke
Micro-48, Waikiki, Hawaii
University of Michigan
Electrical Engineering and Computer Science
MAHALO!
QUESTIONS?