## Slide 1: EECS 270 Fall 2020
Lecture 11 More on minimal sum-of-products
Kmaps

## Slide 2: Informal algorithm
What we are going to do is circle groups of “1s” that are rectangles where each side is a power of 2 in length.
  We never circle a rectangle that is part of a larger legal rectangle.
  We only circle enough rectangles so that every 1 is circled.
  Recall a square is special case of a rectangle.

## Slide 3
K-map “rules”
  Only circle adjacent cells (remember edges are adjacent!)
  Only circle groups that are powers of 2 (1, 2, 4, 8, …)
  Only circle 1-cells

## Slide 6: Terminology (1/3)
Notice that we are finding sum-of-products solutions.
Recall that a minterm is a product term that includes all of the functions variables exactly once.
The on-set of a function is the set of minterms that define when the function should evaluate to 1 (the minterms that have a 1 in the truth table.)
  The off-set is the set of minterms that evaluate to zero.
An implicant of a function is a product term that evaluates to 1 only in places that function evaluates to 1.
  The on-set of an implicant of a function is a subset of the on-set of the function.
  Graphically, in a K-map an implicant is: ________________

## Slide 7: Terminology (2/3)
An implicant covers those minterms that appears in its on-set.
  What is the on-set of the function F(a,b)=a? ____________________
  What minterms does that function cover? ______________________
Removing a variable from a term is known as expanding the term. This is the same as expanding the size of a circle on a K-map

## Slide 8: Terminology (3/3)

## Slide 9: Covering
g
= input combinations
for which g outputs 1
Space of all 2n input
combinations (minterms)
f
= input combinations
for which f outputs 1
f covers g
if f=1 whenever g=1
f ≥ g

## Slide 10: Implicants
g
= input combinations
for which g outputs 1
h
f
= input combinations
for which f outputs 1
If g is a product term & g≤f,
Then g is an implicant of f.
Space of all 2n input
combinations (minterms)
= input combinations
for which h outputs 1

## Slide 11: Prime Implicants
Removing a literal from any product term (any implicant) makes it cover twice as many minterms.
  Removing a literal “grows” the term
  ex. 3 variables: ab’c covers 1 minterm ab’ ac each cover 2 minterms b’c
f
ab’c
ab’
ac
b’c
Any way of removing a literal
makes ab’c no longer imply f.
So ab’c is a prime implicant of f.
ab’c is an implicant of f.

## Slide 12
Implicant: Any product term that implies a function F (i.e., if, for some input combination, product term P = 1, then F = 1 for the same input combination)
Prime Implicant: An implicant such that if one literal is removed, the resulting product term no longer implies F
Essential Prime Implicant: A prime implicant that covers a minterm that is not covered by any other prime implicants
Theorem: The minimal SOP of a function is a sum of prime implicants and includes all essential prime implicants
These are only a few of the implicants of this function…

## Slide 13: More formal algorithm
Identify all prime implicants
Identify all essential ones.
Circle all essential prime implicants
Cover the remaining minterms using a minimal number of remaining prime implicants.
  Notice that there may be more than one solution.
  Also notice that the last step is a bit vague

## Slide 14: Examples

## Slide 15: More examples

## Slide 16: What’s left?
Don’t cares
5+ variable
Product-of-sums
Programmable techniques
Lots of practice.
More context. Remember this is only for 2-level logic…