Quiz 5 – EECS 270, Spring '05

Name: ________________________________________________ unique name: ________________

Honor code:

I have not given or received aid on this quiz, nor have I observed anyone else doing so:

Sign here:_____________________________________

This quiz is graded out of 100 points and is worth about 4% of your class grade.  You will have 20 minutes for this quiz.  Closed everything including calculators! To receive partial credit, work must be shown.

- Using a D-flip-flop and standard gates, draw a T-flip-flop. [15]

- Define the following terms [15]

  - Set-up time

  - Hold time

  - Volatile memory

- Convert the following [20]

  - 25MHz frequency to _________________ ns

  - 10KHz frequency to _________________ ms

  - 20ms period to _________________ Hz

  - 0.5 ns period to _________________ MHz

  - 2 μs period to ___________________ MHz

- Using only nMOS and pMOS transistors, implement the following logic function:
 A*B+C.  You will lose 5 points if your design uses more than 8 transistors.  You may assume you have A, B, C, !A, !B, and !C as inputs to your circuit.  [30]

- Using the symbols “1” for Vcc, 0 for Ground, HiZ for HiZ and “Smoke” for directly connecting Vcc to Ground, write a truth table for the following transistor circuit. [20]

| A | B | C | OUT |
| --- | --- | --- | --- |
| 0 | 0 | 0 |  |
| 0 | 0 | 1 |  |
| 0 | 1 | 0 |  |
| 0 | 1 | 1 |  |
| 1 | 0 | 0 |  |
| 1 | 0 | 1 |  |
| 1 | 1 | 0 |  |
| 1 | 1 | 1 |  |

# Text boxes

A

A

C

B

OUT

B

C