Quiz 1 – Spring 2013 – EECS 270

Name: ____________________________________  uname: _________________

This quiz is graded out of 100 points.  Please remember you can drop your lowest quiz score.  You will have 15 minutes for the quiz.  It is closed book and closed notes. Show your work and circle your answer!  The last problem is quite hard and worth fewer points…

- Convert the following to canonical sum-of-products using any method. [30]

F=(A+B+C)*!(A+D) [30 points]

- Fill-in-the-blank [25 points, -5 for each wrong or blank answer, minimum 0]

  - The 5-bit 2’s complement number representation of -5 is_____________.

  - 10001, when treated as a 5-bit signed-magnitude number, has a decimal 

representation of __________.

  - ___________ gates and ___________ gates are each logically complete.

  - The range of representation for a 6-bit unsigned number is from 

_________  to __________.

- Using only the devices listed below, design a circuit which takes two 3-bit signed numbers (X[2:0] and Y[2:0]) and outputs the smaller of the two, named OUT[2:0]. (If the inputs have the same value, you can output either). 

In your design you may use the following devices (as well as freely using “0” and “1” as a inputs as desired)

- AND, OR, and XOR gates (any number of inputs)

- Inverters

- 1-bit 2 to 1 MUX

- 3-bit unsigned comparator (has an “equal” and “greater than” output)

- 3-bit 2 to 1 MUX

- 8 to 3 priority encoder

You must clearly label any device you use (other than gates and inverters) and your design should be clear enough that someone else could understand how everything was to be connected.  Your grade will be based in part upon the efficiency of your design. [30]

- Design a device that takes in a 4-bit 2’s complement number and outputs a 5-bit 2’s complement number that is twice the value.  You may use standard gates, but are to use as few gates as possible. [15]