## Slide 1: EECS 470
Further review: Pipeline Hazards and More
Lecture 2 – Winter 2024
Slides developed in part by Profs. Austin, Brehob, Falsafi, Hill, Hoe, Lipasti, Martin, Roth, Shen, Smith, Sohi, Tyson, Vijaykumar, and Wenisch of Carnegie Mellon University, Purdue University, University of Michigan, University of Pennsylvania, and University of Wisconsin.

## Slide 2: Announcements
HW1 due 1/18 @10pm (2 days)
  Use office hours, this isn’t trivial.
  Some review, some stuff to learn on your own.
Programming assignment 1 due 1/23 (7 days)
  Hand-in electronically by 10pm
Should be reading
  C.1-C.3 (review)
  3.1, 3.4-3.5 (new material)
Get on 470’s Piazza site (link on website)
Bureaucracy &
Scheduling

## Slide 3: Today
Touch on performance
Cover a bit on ISAs
Pickup where we left off on pipelining
Bureaucracy &
Scheduling

## Slide 4: Performance – Key Points
Amdahl’s law
  Soverall = 1 / ( (1-f) + f/S )
Iron law
Averaging Techniques
Arithmetic
Time
Harmonic
Rates
Performance

## Slide 5: Speedup
While speedup is generally is used to explain the impact of parallel computation, we can also use it to discuss any performance improvement.
  Keep in mind that if execution time stays the same, speedup is 1.
    Speedup
  A speedup of 2.0 means that it takes half as long to do something.
  So 0.5 “speedup” actually means it takes twice as long to do something.
    Be careful when reading papers, folks sometimes use it incorrectly
    Sometimes they use %
Performance

## Slide 6
Instruction Set Architecture
ISA

## Slide 7: Instruction Set Architecture
“Instruction set architecture (ISA) is the structure of a computer that a machine language programmer (or a compiler) must understand to write a correct (timing independent) program for that machine”
IBM introducing 360 in 1964
- IBM 360 is a family of binary-compatible machines with distinct microarchitectures and technologies, ranging from Model 30 (8-bit datapath, up to 64KB memory) to Model 70 (64-bit datapath, 512KB memory) and later Model 360/91 (the Tomasulo).
- IBM 360 replaced 4 concurrent, but incompatible lines of IBM architectures developed over the previous 10 years
ISA

## Slide 8: ISA: A contract between HW and SW
ISA (instruction set architecture)
  A well-defined hardware/software interface
  The “contract” between software and hardware
    Functional definition of operations, modes, and storage locations supported by hardware
    Precise description of how to invoke, and access them
  No guarantees regarding
    How operations are implemented
    Which operations are fast and which are slow and when
    Which operations take more power and which take less
ISA

## Slide 9: Components of an ISA
Programmer-visible states
  Program counter, general purpose registers, memory, control registers
Programmer-visible behaviors (state transitions)
  What to do, when to do it
A binary encoding
  ISAs last 25+ years (because of SW cost)…
  …be careful what goes in
if imem[pc]==“add rd, rs, rt”
then
pc  pc+1
gpr[rd]=gpr[rs]+grp[rt]
Example “register-transfer-level” description of an instruction
ISA

## Slide 10: RISC vs CISC
Recall “Iron” law:
  (instructions/program) * (cycles/instruction) * (seconds/cycle)
CISC (Complex Instruction Set Computing)
  Improve “instructions/program” with “complex” instructions
  Easy for assembly-level programmers, good code density
RISC (Reduced Instruction Set Computing)
  Improve “cycles/instruction” with many single-cycle instructions
  Increases “instruction/program”, but hopefully not as much
    Help from smart compiler
  Perhaps improve clock cycle time (seconds/cycle)
    via aggressive implementation allowed by simpler instructions
ISA

## Slide 11: What Makes a Good ISA?
Programmability
  Easy to express programs efficiently?
Implementability
  Easy to design high-performance implementations?
  More recently
    Easy to design low-power implementations?
    Easy to design high-reliability implementations?
    Easy to design low-cost implementations?
Compatibility
  Easy to maintain programmability (implementability) as languages and programs (technology) evolves?
  x86 (IA32) generations: 8086, 286, 386, 486, Pentium, PentiumII, PentiumIII, Pentium4,…
ISA

## Slide 12: Typical Instructions (Opcodes)
What operations are necessary? {sub, ld & st, conditional br.}
  What is the minimum complete ISA for a von Neuman machine?
Too little or too simple  not expressive enough
  difficult to program (by hand)
  programs tend to be bigger
Too much or too complex  most of it won’t be used
  too much “baggage” for implementation.
  difficult choices during compiler optimization
ISA

## Slide 13: Basic Pipelining
Basic Pipelining

## Slide 14: Before there was pipelining…
Basic datapath: fetch, decode, execute
Single-cycle control: hardwired
    Low CPI (1)
    Long clock period (to accommodate slowest instruction)
Multi-cycle control: micro-programmed
    Short clock period
    High CPI
Can we have both low CPI and short clock period?
    Not if datapath executes only one instruction at a time
    No good way to make a single instruction go faster
insn0.fetch, dec, exec
Single-cycle
Multi-cycle
insn1.fetch, dec, exec
insn0.dec
insn0.fetch
insn1.dec
insn1.fetch
insn0.exec
insn1.exec
Basic Pipelining

## Slide 15: Pipelining
Important performance technique
  Improves throughput at the expense of latency
    Why does latency go up?
Begin with multi-cycle design
  When instruction advances from stage 1 to 2…
  … allow next instruction to enter stage 1
  Each instruction still passes through all stages
  But instructions enter and leave at a much faster rate
Automotive assembly line analogy
insn0.dec
insn0.fetch
insn1.dec
insn1.fetch
Multi-cycle
Pipelined
insn0.exec
insn1.exec
insn0.dec
insn0.fetch
insn1.dec
insn1.fetch
insn0.exec
insn1.exec
Basic Pipelining

## Slide 16: Pipeline Illustrated:
Basic Pipelining

## Slide 17: 370 Processor Pipeline Review
I-cache
Reg
File
PC
+1
D-cache
ALU
Fetch
Decode
Memory
(Write-back)
Tpipeline = Tbase / 5
Execute
Basic Pipelining

## Slide 18: Basic Pipelining
Data hazards
  What are they?
  How do you detect them?
  How do you deal with them?
Micro-architectural changes
  Pipeline depth
  Pipeline width
Forwarding ISA (minor point)
Control hazards (time allowing)
Basic Pipelining

## Slide 19
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
Bits 0-2
Bits 16-18
op
dest
offset
valB
valA
PC+1
PC+1
target
ALU
result
op
dest
valB
op
dest
ALU
result
mdata
eq?
instruction
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
Bits 22-24
data
dest
Fetch Decode Execute Memory WB
Basic Pipelining

## Slide 20
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
op
dest
offset
valB
valA
PC+1
PC+1
target
ALU
result
op
dest
valB
op
dest
ALU
result
mdata
eq?
instruction
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
dest
Fetch Decode Execute Memory WB
Basic Pipelining

## Slide 21
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
op
offset
valB
valA
PC+1
PC+1
target
ALU
result
op
valB
op
ALU
result
mdata
eq?
instruction
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
fwd
fwd
fwd
data
Fetch Decode Execute Memory WB
Basic Pipelining

## Slide 22: Pipeline function for ADD
Fetch: read instruction from memory
Decode: read source operands from reg
Execute: calculate sum
Memory: Pass results to next stage
Writeback: write sum into register file
Basic Pipelining

## Slide 23: Data Hazards
add 1 2 3
nand 3 4 5
time
fetch decode execute memory writeback
fetch decode execute memory writeback
add
nand
If not careful, you will read the wrong value of R3
Pipelining &
Data Hazards

## Slide 24: Three approaches to handling data hazards
Avoidance
  Make sure there are no hazards in the code
Detect and Stall
  If hazards exist, stall the processor until they go away.
Detect and Forward
  If hazards exist, fix up the pipeline to get the correct value (if possible)
Pipelining &
Data Hazards

## Slide 25: Handling data hazards: avoid all hazards
Assume the programmer (or the compiler) knows about the processor implementation.
  Make sure no hazards exist.
    Put noops between any dependent instructions.
add 1 2 3
noop
noop
nand 3 4 5
write R3 in cycle 5
read R3 in cycle 6
Pipelining &
Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 26: Problems with this solution
Old programs (legacy code) may not run correctly on new implementations
  Longer pipelines need more noops
Programs get larger as noops are included
  Especially a problem for machines that try to execute more than one instruction every cycle
  Intel EPIC: Often 25% - 40% of instructions are noops
Program execution is slower
  CPI is one, but some I’s are noops
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 27: Handling data hazards: detect and stall
Detection:
  Compare regA with previous DestRegs
    3 bit operand fields
  Compare regB with previous DestRegs
    3 bit operand fields
Stall:
  Keep current instructions in fetch and decode
  Pass a noop to execute
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 28
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
op
offset
valB
valA
PC+1
PC+1
target
ALU
result
op
valB
op
ALU
result
mdata
eq?
add 1 2 3
7
10
14
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
End of Cycle 1
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 29
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
add
3
7
14
PC+1
PC+1
target
ALU
result
op
valB
op
ALU
result
mdata
eq?
nand 3 4 5
7
10
14
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
3
End of Cycle 2
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 30
Hazard detection
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
add
3
7
14
PC+1
PC+1
target
ALU
result
op
valB
op
ALU
result
mdata
eq?
nand 3 4 5
7
10
14
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
3
3
First half of cycle 3
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 31
REG
file
IF/
ID
ID/
EX
3
compare
Hazard
detected
regA
regB
compare
compare
compare
3
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 32
3
Hazard
detected
regA
regB
compare
0 1 1
0 1 1
0 0 0
1
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 33: Handling data hazards: detect and stall the pipeline until ready
Detection:
  Compare regA with previous DestReg
    3 bit operand fields
  Compare regB with previous DestReg
    3 bit operand fields
Stall:
  Keep current instructions in fetch and decode
  Pass a noop to execute
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 34
Hazard
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
add
7
14
1
2
target
ALU
result
valB
ALU
result
mdata
eq?
nand 3 4 5
7
10
11
14
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
3
3
en
en
First half of cycle 3
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 35: Handling data hazards: detect and stall the pipeline until ready
Detection:
  Compare regA with previous DestReg
    3 bit operand fields
  Compare regB with previous DestReg
    3 bit operand fields
Stall:
  Keep current instructions in fetch and decode
  Pass a noop to execute
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 36
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
2
21
add
ALU
result
mdata
nand 3 4 5
7
10
11
14
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
3
End of cycle 3
noop
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 37
Hazard
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
noop
2
21
add
ALU
result
mdata
nand 3 4 5
7
10
11
14
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
3
3
en
en
First half of cycle 4
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 38
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
noop
2
noop
add
21
nand 3 4 5
7
10
11
14
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
3
End of cycle 4
noop
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 39
No Hazard
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
noop
2
noop
add
21
nand 3 4 5
7
10
11
14
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
3
3
First half of cycle 5
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 40
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
nand
11
21
2
3
noop
noop
add 3 7 7
7
21
11
77
14
1
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
5
data
End of cycle 5
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 41: No more hazard: stalling
add 1 2 3
nand 3 4 5
time
fetch decode execute memory writeback
fetch decode decode decode execute
add
nand
We are careful to get the right value of R3
hazard
hazard
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 42: Problems with detect and stall
CPI increases every time a hazard is detected!
Is that necessary? Not always!
  Re-route the result of the add to the nand
    nand no longer needs to read R3 from reg file
    It can get the data later (when it is ready)
    This lets us complete the decode this cycle
      But we need more control to remember that the data that we aren’t getting from the reg file at this time will be found elsewhere in the pipeline at a later cycle.
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 43: Handling data hazards: detect and forward
Detection: same as detect and stall
  Except that all 4 hazards are treated differently
    i.e., you can’t logical-OR the 4 hazard signals
Forward:
  New datapaths to route computed data to where it is needed
  New Mux and control to pick the right data
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 44: Detect and Forward Example
  add 1 2 3 // r3 = r1 + r2
  nand 3 4 5 // r5 = r3 NAND r4
  add 6 3 7 // r7 = r3 + r6
  lw 3 6 10 // r6 = MEM[r3+10]
  sw 6 2 12 // MEM[r6+12]=r2
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 45
Hazard
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
add
7
14
1
2
nand 3 4 5
7
10
11
77
14
1
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
3
fwd
fwd
fwd
3
First half of cycle 3
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 46
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
nand
11
10
2
3
21
add
add 6 3 7
7
10
11
77
14
1
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
5
data
H1
3
End of cycle 3
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 47
New Hazard
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
nand
11
10
2
3
21
add
add 6 3 7
7
10
11
77
14
1
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
5
data
3
M
U
X
H1
3
First half of cycle 4
21
11
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 48
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
add
10
1
3
4
-2
nand
add
21
lw 3 6 10
7
10
11
77
14
1
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
7
5
3
data
M
U
X
H2
H1
End of cycle 4
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 49
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
add
10
1
3
4
-2
nand
add
21
lw 3 6 10
7
10
11
77
14
1
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
7
5
3
data
M
U
X
H2
H1
First half of cycle 5
3
No Hazard
21
1
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 50
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
lw
10
21
4
5
22
add
nand
-2
sw 6 2 12
7
21
11
77
14
1
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
7
5
data
M
U
X
H2
H1
6
End of cycle 5
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 51
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
lw
10
21
4
5
22
add
nand
-2
sw 6 2 12
7
21
11
77
14
1
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
6
7
5
data
M
U
X
H2
H1
First half of cycle 6
Hazard
6
en
en
L
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 52
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
5
31
lw
add
22
sw 6 2 12
7
21
11
-2
14
1
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
6
7
data
M
U
X
H2
End of cycle 6
noop
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 53
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
noop
5
31
lw
add
22
sw 6 2 12
7
21
11
-2
14
1
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
6
7
data
M
U
X
H2
First half of cycle 7
Hazard
6
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 54
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
sw
12
7
1
5
noop
lw
99
7
21
11
-2
14
1
0
22
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
6
data
M
U
X
H3
End of cycle 7
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 55
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
sw
12
7
1
5
noop
lw
99
7
21
11
-2
14
1
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
6
data
M
U
X
H3
First half of cycle 8
99
12
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 56
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
M
U
X
111
sw
7
noop
7
21
11
-2
14
99
0
8
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
data
M
U
X
H3
End of cycle 8
Pipelining & Data Hazards
  Avoidance
  Detect and Stall
  Detect and Forward

## Slide 57: Pipeline function for BEQ
Fetch: read instruction from memory
Decode: read source operands from reg
Execute: calculate target address and test for equality
Memory: Send target to PC if test is equal
Writeback: Nothing left to do
Pipelining & Control Hazards

## Slide 58: Control Hazards
beq 1 1 10
sub 3 4 5
F
D
E
M
W
F
D
E
M
W
t0
t1
t2
t3
t4
t5
beq
sub
squash
Pipelining & Control Hazards

## Slide 59: Handling Control Hazards
Avoidance (static)
  No branches?
  Convert branches to predication
    Control dependence becomes data dependence
Detect and Stall (dynamic)
  Stop fetch until branch resolves
Speculate and squash (dynamic)
  Keep going past branch, throw away instructions if wrong
Pipelining & Control Hazards

## Slide 60: Avoidance Via Predication
if (a == b) {
x++;
y = n / d;
}
sub t1  a, b
jnz t1, PC+2
add x  x, #1
div y  n, d
sub t1  a, b
add(!t1) x  x, #1
div(!t1) y  n, d
sub t1  a, b
add t2  x, #1
div t3  n, d
cmov(!t1) x  t2
cmov(!t1) y  t3
Pipelining & Control Hazards
  Avoidance
  Detect and Stall
  Speculate and Squash

## Slide 61: Handling Control Hazards: Detect & Stall
Detection
  In decode, check if opcode is branch or jump
Stall
  Hold next instruction in Fetch
  Pass noop to Decode
Pipelining & Control Hazards
  Avoidance
  Detect and Stall
  Speculate and Squash

## Slide 62
PC
Inst
mem
REG
file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
sign
ext
Control
bnz r1
Pipelining & Control Hazards
  Avoidance
  Detect and Stall
  Speculate and Squash

## Slide 63: Control Hazards
beq 1 1 10
sub 3 4 5
time
fetch decode execute memory writeback
fetch fetch fetch
beq
sub
fetch
or
fetch
Target:
Pipelining & Control Hazards
  Avoidance
  Detect and Stall
  Speculate and Squash

## Slide 64: Problems with Detect & Stall
CPI increases on every branch
Are these stalls necessary? Not always!
  Branch is only taken half the time
  Assume branch is NOT taken
    Keep fetching, treat branch as noop
    If wrong, make sure bad instructions don’t complete
Pipelining & Control Hazards
  Avoidance
  Detect and Stall
  Speculate and Squash

## Slide 65: Handling Control Hazards: Speculate & Squash
Speculate “Not-Taken”
  Assume branch is not taken
Squash
  Overwrite opcodes in Fetch, Decode, Execute with noop
  Pass target to Fetch
Pipelining & Control Hazards
  Avoidance
  Detect and Stall
  Speculate and Squash

## Slide 66
PC
REG
file
M
U
X
A
L
U
M
U
X
1
Data
memory
+
+
M
U
X
IF/
ID
ID/
EX
EX/
Mem
Mem/
WB
sign
ext
Control
equal
M
U
X
beq
sub
add
nand
add
sub
beq
beq
Inst
mem
noop
noop
noop
Pipelining & Control Hazards
  Avoidance
  Detect and Stall
  Speculate and Squash

## Slide 67: Problems with Speculate & Squash
Always assumes branch is not taken
Can we do better? Yes.
  Predict branch direction and target!
  Why possible? Program behavior repeats.
  More on branch prediction to come...
Pipelining & Control Hazards
  Avoidance
  Detect and Stall
  Speculate and Squash

## Slide 68: Branch Delay Slot (MIPS, SPARC)
F
D
E
M
W
F
F
D
E
M
t0
t1
t2
t3
t4
t5
W
next:
target:
i: beq 1, 2, tgt
j: add 3, 4, 5
What can we put here?
branch:
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
delay:
target:
branch:
Squash
- Instruction in delay slot executes even on taken branch
Pipelining & Control Hazards
Branch Delay Slot

## Slide 69: Improving pipeline performance
Add more stages
Widen pipeline
Improving pipeline
performance

## Slide 70: Adding pipeline stages
Pipeline frontend
  Fetch, Decode
Pipeline middle
  Execute
Pipeline backend
  Memory, Writeback
Improving pipeline
performance

## Slide 71: Adding stages to fetch, decode
Delays hazard detection
No change in forwarding paths
No performance penalty with respect to data hazards
Improving pipeline
performance

## Slide 72: Adding stages to execute
Check for structural hazards
  ALU not pipelined
  Multiple ALU ops completing at same time
Data hazards may cause delays
  If multicycle op hasn't computed data before the dependent instruction is ready to execute
Performance penalty for each stall
Improving pipeline
performance

## Slide 73: Adding stages to memory, writeback
Instructions ready to execute may need to wait longer for multi-cycle memory stage
Adds more pipeline registers
  Thus more source registers to forward
    More complex hazard detection
    Wider muxes
    More control bits to manage muxes
Improving pipeline
performance

## Slide 74: Wider pipelines
fetch
decode
execute
mem
WB
fetch
decode
execute
mem
WB
More complex hazard detection
    2X pipeline registers to forward from
    2X more instructions to check
    2X more destinations (muxes)
    Need to worry about dependent
instructions in the same stage
Improving pipeline
performance

## Slide 75: Making forwarding explicit
add r1  r2, EX/Mem ALU result
  Include direct mux controls into the ISA
  Hazard detection is now a compiler task
  New micro-architecture leads to new ISA
    Is this why this approach always seems to fail? (e.g., simple VLIW, Motorola 88k)
  Can reduce some resources
    Eliminates complex conflict checkers