## Slide 1: EECS 470
Finish Tomasulo
Branches: Address prediction and recovery Lecture 5 – Winter 2024
Slides developed in part by Profs. Austin, Brehob, Falsafi, Hill, Hoe, Lipasti, Martin, Roth, Shen, Smith, Sohi, Tyson, Vijaykumar, and Wenisch of Carnegie Mellon University, Purdue University, University of Michigan, University of Pennsylvania, and University of Wisconsin.

## Slide 2: Announcements:
Programming assignment #2
  Due Tuesday 1/30
HW #2
  Due Friday 2/22
Reading
  Book: 3.1, 3.3-3.6, 3.8
  Combining Branch Predictors, S. McFarling, WRL Technical Note TN-36, June 1993.
    On the website.

## Slide 3: Last time:
Started in on Tomasulo’s algorithm.

## Slide 4: Today
Some deep thoughts on Tomasulo’s
Branch prediction consists of
  Branch taken predictor
  Address predictor
  Mispredict recovery.
Also interrupts become relevant
  “Recovery” is fairly similar…

## Slide 5: But first… Brehob’s Verilog rules*
Always blocks
  In always_comb blocks, use blocking assignments.
  In always_ff blocks, use non-blocking assignments.
    Do not mix blocking and non-blocking assignments in the same always block.
  Do not make assignments to the same variable in more than one always block.
  Make sure that all paths through a combinational always block assign all variables.
  Sync. resets.
Generic:
  Correctly use logical and bitwise operators.
  Avoid extra text that confuses
    X=A?1’b1:1’b0; //big ick.
    if(X==1’b1) //ick but sometimes okay.
* Most of these are style/clarity issues. Some are required. In the real world there are good reasons to break nearly all of these. But in 470, please follow them. When we grade for style we’ll be looking at these issues (among other things!)

## Slide 6: Simple Tomasulo Data Structures
RS:
  Status information
    R: Destination Register
    op: Operand (add, etc.)
  Tags
    T1, T2: source operand tags
  Values
    V1, V2: source operand values
value
V1
V2
FU
T
T2
T1
T
op
==
==
==
==
Map Table
Reservation Stations
CDB.V
CDB.T
Fetched
insns
Regfile
R
T
==
==
==
==
Map table (also RAT: Register Alias Table)
  Maps registers to tags
Regfile (also ARF: Architected Register File)
  Holds value of register if no value in RS

## Slide 7: Tomasulo Data Structures (Timing Free Example)
Map Table | 
Reg | T
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | R | op | T1 | T2 | V1 | V2
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
CDB | 
T | V
ARF | 
Reg | V
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Instruction
r0=r1*r2
r1=r2*r3
r2=r4+1
r1=r1+r1

## Slide 8: Tomasulo Data Structures (Timing Free Example #2)
Map Table | 
Reg | Tag
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Reservation Stations |  |  |  |  |  |  |  | 
T | FU | busy | op | R | T1 | T2 | V1 | V2
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
CDB | 
T | V
ARF | 
Reg | V
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Instruction
r0=r1*r2
r1=r0*r3
r0=r4+1
r1=r1+r0

## Slide 9: Note:
Tuesday’s slides had a detailed example with timing.
  Just for reference, some of you may find it useful.

## Slide 10: Can We Add Superscalar?
Dynamic scheduling and multiple issue are orthogonal
  E.g., Pentium4: dynamically scheduled 5-way superscalar
  Two dimensions
    N: superscalar width (number of parallel operations)
    W: window size (number of reservation stations)
What do we need for an N-by-W Tomasulo?
  RS: N tag/value w-ports (D), N value r-ports (S), 2N tag CAMs (W)
  Select logic: WN priority encoder (S)
  MT: 2N r-ports (D), N w-ports (D)
  RF: 2N r-ports (D), N w-ports (W)
  CDB: N (W)
  Which are the expensive pieces?

## Slide 11: Superscalar Select Logic
Superscalar select logic: WN priority encoder
  Somewhat complicated (N2 logW)
  Can simplify using different RS designs
Split design
  Divide RS into N banks: 1 per FU?
  Implement N separate W/N1 encoders
  Simpler: N * logW/N
  Less scheduling flexibility
FIFO design [Palacharla+]
  Can issue only head of each RS bank
  Simpler: no select logic at all
  Less scheduling flexibility (but surprisingly not that bad)

## Slide 12: Dynamic Scheduling Summary
Dynamic scheduling: out-of-order execution
  Higher pipeline/FU utilization, improved performance
  Easier and more effective in hardware than software
    More storage locations than architectural registers
    Dynamic handling of cache misses
Instruction buffer: multiple F/D latches
  Implements large scheduling scope + “passing” functionality
  Split decode into in-order dispatch and out-of-order issue
    Stall vs. wait
Dynamic scheduling algorithms
  Scoreboard: no register renaming, limited out-of-order
  Tomasulo: copy-based register renaming, full out-of-order

## Slide 13: Are we done?
When can Tomasulo go wrong?
  Branches
    What if a branch finishes after older instructions (things behind the branch) finish?
  Exceptions!!
    No way to figure out relative order of instructions in RS

## Slide 14: And… a bit of terminology
Issue can be thought of as a two-stage process: “wakeup” and “select”.
  When the RS figures out it has it’s data and is ready to run it is said to have “woken up” and the process of doing so is called wakeup
    But there may be a structural hazard—no EX unit available for a given RS
      When?
  Thus, in addition to be woken up, and RS needs to be selected before it can go to the execute unit (EX stage).
    This process is called select

## Slide 15: Questions
What are we “renaming” to?
Why are branches a challenge?
  What are my options on how to handle them?
What are some other names for the map table?
Could you explain when to update the RAT again?
  Why?

## Slide 16: Branch mispredict
In this original version of Tomasulo’s algorithm, branches are a big problem.
  Unless we don’t speculate past branches, we allow instructions to speculatively modify architectural state.
    That’s a really bad idea—we have no recovery mechanism.
    Think about the 5-state pipeline.
  Tomasulo’s answer was to not let instructions be dispatched until all branches in front of them have resolved.
    Branches are about ~15% (1 in 7 or so) of all instructions.
      That really limits us.
Let’s first discuss how to predict.

## Slide 17: Parts of the predictor
Direction Predictor
  For conditional branches
    Predicts whether the branch will be taken
  Examples:
    Always taken; backwards taken
Address Predictor
  Predicts the target address (use if predicted taken)
  Examples:
    BTB; Return Address Stack; Precomputed Branch
Recovery logic

## Slide 18: Example gzip:
gzip: loop branch A@ 0x1200098d8
Executed: 1359575 times
Taken: 1359565 times
Not-taken: 10 times
% time taken: 99% - 100%
Easy to predict (direction and address)

## Slide 19: Example gzip:
gzip: if branch B@ 0x12000fa04
Executed: 151409 times
Taken: 71480 times
Not-taken: 79929 times
% time taken: ~49%
Easy to predict? (maybe not/ maybe dynamically)

## Slide 20: Example: gzip
0
100
Direction prediction: always taken
Accuracy: ~73 %
A
B

## Slide 21: Branch Backwards
Most backward branches are heavily TAKEN
Forward branches slightly more likely to be NOT-TAKEN

## Slide 22: Using history
1-bit history (direction predictor)
  Remember the last direction for a branch
branchPC
NT
T
How big is the table?

## Slide 23: Using history
2-bit history (direction predictor)
branchPC
SN
NT
T
ST
How big is the Table?

## Slide 24: Using History Patterns
~80 percent of branches are either heavily TAKEN or heavily NOT-TAKEN
For the other 20%, we need to look a patterns of reference to see if they are predictable using a more complex predictor
Example: gcc has a branch that flips each time
T(1) NT(0) 10101010101010101010101010101010101010

## Slide 25: Local history
branchPC
NT
T
10101010
Pattern History
Table
Branch History
Table
What is the prediction
for this BHT 10101010?
When do I update the tables?

## Slide 26: Local history
branchPC
NT
T
01010101
Pattern History
Table
Branch History
Table
On the next execution of this
branch instruction, the branch
history table is 01010101,
pointing to a different pattern
What is the accuracy of a flip/flop branch 0101010101010…?

## Slide 27: Global history
01110101
Pattern History
Table
Branch History
Register
if (aa == 2)
aa = 0;
if (bb == 2)
bb = 0;
if (aa != bb) { …
How can branches interfere with each other?

## Slide 28: Gshare predictor
Ref: Combining Branch Predictors
branchPC
01110101
Pattern History
Table
Branch History
Register
xor
Must read!

## Slide 29: Hybrid predictors
Local predictor
(e.g. 2-bit)
Global/gshare predictor
(much more state)
Prediction
1
Prediction
2
Selection table
(2-bit state machine)
How do you select which predictor to use?
How do you update the various predictor/selector?
Prediction

## Slide 30: Overriding Predictors
Big predictors are slow, but more accurate
Use a single cycle predictor in fetch
Start the multi-cycle predictor
  When it completes, compare it to the fast prediction.
    If same, do nothing
    If different, assume the slow predictor is right and flush pipline.
Advantage: reduced branch penalty for those branches mispredicted by the fast predictor and correctly predicted by the slow predictor

## Slide 31: “Trivial” example: Tournament Branch Predictor
Local
  8-entry 3-bit local history table indexed by PC
  8-entry 2-bit up/down counter indexed by local history
Global
  8-entry 2-bit up/down counter indexed by global history
Tournament
  8-entry 2-bit up/down counter indexed by PC

## Slide 32
Tournament selector 00=local, 11=global | 
ADR[4:2] | Pred. state
0 | 00
1 | 01
2 | 00
3 | 10
4 | 11
5 | 00
6 | 11
7 | 10
Local predictor 1st level table (BHT) 0=NT, 1=T | 
ADR[4:2] | History
0 | 001
1 | 101
2 | 100
3 | 110
4 | 110
5 | 001
6 | 111
7 | 101
Local predictor 2nd level table (PHT) 00=NT, 11=T | 
History | Pred. state
0 | 00
1 | 11
2 | 10
3 | 00
4 | 01
5 | 01
6 | 11
7 | 11
Global predictor table 00=NT, 11=T | 
History | Pred. state
0 | 11
1 | 10
2 | 00
3 | 00
4 | 00
5 | 11
6 | 11
7 | 00
Branch
History
Register

## Slide 33
Tournament selector 00=local, 11=global | 
ADR[4:2] | Pred. state
0 | 00
1 | 01
2 | 00
3 | 10
4 | 11
5 | 00
6 | 11
7 | 10
Local predictor 1st level table (BHT) 0=NT, 1=T | 
ADR[4:2] | History
0 | 001
1 | 101
2 | 100
3 | 110
4 | 110
5 | 001
6 | 111
7 | 101
Local predictor 2nd level table (PHT) 00=NT, 11=T | 
History | Pred. state
0 | 00
1 | 11
2 | 10
3 | 00
4 | 01
5 | 01
6 | 11
7 | 11
Global predictor table 00=NT, 11=T | 
History | Pred. state
0 | 11
1 | 10
2 | 00
3 | 00
4 | 00
5 | 11
6 | 11
7 | 00
r1=2, r2=6, r3=10, r4=12, r5=4
Address of joe =0x100 and each instruction is 4 bytes.
Branch History Register = 110
joe: add r1 r2 r3
beq r3 r4 next
bgt r2 r3 skip // if r2>r3 branch
lw r6 4(r5)
add r6 r8 r8
skip: add r5 r2 r2
bne r4 r5 joe
next: noop

## Slide 34: General speculation
Control speculation
  “I think this branch will go to address 90004”
Data speculation
  “I’ll guess the result of the load will be zero”
Memory conflict speculation
  “I don’t think this load conflicts with any proceeding store.”
Error speculation
  “I don’t think there were any errors in this calculation”

## Slide 35: Speculation in general
Need to be 100% sure on final correctness!
  So need a recovery mechanism
  Must make forward progress!
Want to speed up overall performance
  So recovery cost should be low or expected rate of occurrence should be low.
  There can be a real trade-off on accuracy, cost of recovery, and speedup when correct.
Should keep the worst case in mind…

## Slide 36
Address
Prediction

## Slide 37: BTB (Chapter3.5)
Branch Target Buffer
  Addresses predictor
  Lots of variations
Keep the target of “likely taken” branches in a buffer
  With each branch, associate the expected target.

## Slide 38
Branch PC | Target address
0x05360AF0 | 0x05360000
… | …
… | …
… | …
… | …
… | …
BTB indexed by current PC
  If entry is in BTB fetch target address next
Generally set associative (too slow as FA)
Often qualified by branch taken predictor

## Slide 39: So…
BTB lets you predict target address during the fetch of the branch!
If BTB gets a miss, pretty much stuck with not-taken as a prediction
  So limits prediction accuracy.
Can use BTB as a predictor.
  If it is there, predict taken.
Replacement is an issue
  LRU seems reasonable, but only really want branches that are taken at least a fair amount.

## Slide 40
Branch
Recovery

## Slide 41: Pipeline recovery is pretty simple
Squash and restart fetch with right address
  Just have to be sure that nothing has “committed” its state yet.
In our 5-stage pipe, state is only committed during MEM (for stores) and WB (for registers)

## Slide 42: Tomasulo’s
Recovery seems really hard
  What if instructions after the branch finish after we find that the branch was wrong?
    This could happen. Imagine
      R1=MEM[R2+0]
      BEQ R1, R3 DONE  Predicted not taken
      R4=R5+R6
  So we have to not speculate on branches or not let anything pass a branch
    Which is really the same thing.
    Branches become serializing instructions.
      Note that can be executing some things before and after the branch once branch resolves.

## Slide 43: What we need is:
Some way to not commit instructions until all branches before it are committed.
  Just like in the pipeline, something could have finished execution, but not updated anything “real” yet.

## Slide 44
Interrupt!!!

## Slide 45: Interrupts
These have a similar problem.
  If we can execute out-of-order a “slower” instruction might not generate an interrupt until an instruction in front of it has finished.
This sounds like the end of out-of-order execution
  I mean, if we can’t finish out-of-order, isn’t this pointless?

## Slide 46: Exceptions and Interrupts
Exception Type | Sync/Async | Maskable? | Restartable?
I/O request | Async | Yes | Yes
System call | Sync | No | Yes
Breakpoint | Sync | Yes | Yes
Overflow | Sync | Yes | Yes
Page fault | Sync | No | Yes
Misaligned access | Sync | No | Yes
Memory Protect | Sync | No | Yes
Machine Check | Async/Sync | No | No
Power failure | Async | No | No

## Slide 47: Precise Interrupts
Implementation approaches
  Don’t
    E.g., Cray-1
  Buffer speculative results
    E.g., P4, Alpha 21264
    History buffer
    Future file/Reorder buffer
Instructions
Completely
Finished
No Instruction
Has Executed
At All
PC
Precise State
Speculative State

## Slide 48: Precise Interrupts via the Reorder Buffer
MEM
@ Alloc
  Allocate result storage at Tail
@ Sched
  Get inputs (ROB T-to-H then ARF)
  Wait until all inputs ready
@ WB
  Write results/fault to ROB
  Indicate result is ready
@ CT
  Wait until inst @ Head is done
  If fault, initiate handler
  Else, write results to ARF
  Deallocate entry from ROB
IF
ID
Alloc
Sched
EX
ROB
CT
Head
Tail
PC
Dst regID
Dst value
Except?
Reorder Buffer (ROB)
  Circular queue of spec state
  May contain multiple definitions of same register
In-order
In-order
Any order
ARF

## Slide 49: Reorder Buffer Example
Code Sequence
f1 = f2 / f3
r3 = r2 + r3
r4 = r3 – r2
Initial Conditions
- reorder buffer empty
- f2 = 3.0
- f3 = 2.0
- r2 = 6
- r3 = 5
ROB
Time
H
T
regID: f1
result: ?
Except: ?
H
T
regID: f1
result: ?
Except: ?
regID: r3
result: ?
Except: ?
H
T
regID: f1
result: ?
Except: ?
regID: r3
result: 11
Except: N
regID: r4
result: ?
Except: ?
r3
regID: r8
result: 2
Except: n
regID: r8
result: 2
Except: n
regID: r8
result: 2
Except: n

## Slide 50: Reorder Buffer Example
Code Sequence
f1 = f2 / f3
r3 = r2 + r3
r4 = r3 – r2
Initial Conditions
- reorder buffer empty
- f2 = 3.0
- f3 = 2.0
- r2 = 6
- r3 = 5
ROB
Time
H
T
regID: f1
result: ?
Except: ?
regID: r3
result: 11
Except: n
regID: r4
result: 5
Except: n
H
T
regID: f1
result: ?
Except: y
regID: r3
result: 11
Except: n
regID: r4
result: 5
Except: n
regID: r8
result: 2
Except: n
regID: r8
result: 2
Except: n
H
T
regID: f1
result: ?
Except: y
regID: r3
result: 11
Except: n
regID: r4
result: 5
Except: n

## Slide 51: Reorder Buffer Example
Code Sequence
f1 = f2 / f3
r3 = r2 + r3
r4 = r3 – r2
Initial Conditions
- reorder buffer empty
- f2 = 3.0
- f3 = 2.0
- r2 = 6
- r3 = 5
ROB
Time
H
T
H
T
first inst
of fault
handler

## Slide 52: There is more complexity here
Rename table needs to be cleared
  Everything is in the ARF
  Really do need to finish everything which was before the faulting instruction in program order.
What about branches?
  Would need to drain everything before the branch.
    Why not just squash everything that follows it?

## Slide 53: And while we’re at it…
Does the ROB replace the RS?
  Is this a good thing? Bad thing?

## Slide 54: ROB
ROB
  ROB is an in-order queue where instructions are placed.
  Instructions complete (retire) in-order
  Instructions still execute out-of-order
  Still use RS
    Instructions are issued to RS and ROB at the same time
    Rename is to ROB entry, not RS.
    When execute done instruction leaves RS
  Only when all instructions in before it in program order are done does the instruction retire.

## Slide 55: Review Questions
Could we make this work without a RS?
  If so, why do we use it?
Why is it important to retire in order?
Why must branches wait until retirement before they announce their mispredict?
  Any other ways to do this?

## Slide 56: Can We Add Superscalar?
Dynamic scheduling and multiple issue are orthogonal
  E.g., Pentium4: dynamically scheduled 5-way superscalar
  Two dimensions
    N: superscalar width (number of parallel operations)
    W: (number of reservation stations)
What do we need for an N-by-W Tomasulo?
  RS: N tag/value w-ports (D), N value r-ports (S), 2N tag CAMs (W)
  Select logic: WN priority encoder (S)
  MT: 2N read-ports (D), N write-ports (D)
  RF: 2N read-ports (D), N write-ports (W)
  CDB: N (W)
  Which are the expensive pieces?

## Slide 57: Superscalar Select Logic
Superscalar select logic: WN priority encoder
  Somewhat complicated (N2 logW)
  Can simplify using different RS designs
Split design
  Divide RS into N banks: 1 per FU?
  Implement N separate W/N1 encoders
  Simpler: N * logW/N
  Less scheduling flexibility
FIFO design [Palacharla+]
  Can issue only head of each RS bank
  Simpler: no select logic at all
  Less scheduling flexibility (but surprisingly not that bad)