## Slide 1: EECS 470
Adding a RoB
Lecture 7 – Winter 2024
Slides developed in part by Profs. Austin, Brehob, Falsafi, Hill, Hoe, Lipasti, Martin, Roth, Shen, Smith, Sohi, Tyson, Vijaykumar, and Wenisch of Carnegie Mellon University, Purdue University, University of Michigan, University of Pennsylvania, and University of Wisconsin.

## Slide 2: Last time:
Covered branch predictors
  Direction
    Bimodal, local history, global, gshare, tournament
  Address
    BTB
    RAS (briefly)

## Slide 3: Warning: Crazy times coming
HW2 due on Friday 2/2 (tomorrow!)
Will do group formation and project materials on Tuesday 2/6.
Group formation will be done in class on Thursday 2/8
P3 is due on Sunday 2/9
  It’s a lot of work (20 hours?)
Proposal is due on Tuesday 2/13
  It’s not a lot of work (1 hour?) to do the write-up, but you’ll need to meet with your group and discuss things.
    Don’t worry too much about getting this right. You’ll be allowed to change (we’ll meet the following Friday). Just a line in the sand. Will discuss on 2/6.
HW3 is due on Wednesday 2/14. No late homework. Answers posted right after it’s due!
Midterm is on Thursday 2/15 in the evening
  Review session over that weekend (date/time TBA)
  Q&A in class 2/15
  Best way to study is look at old exams (posted on-line later this week)
20 minute proposal meetings on Friday 2/16 rather than lab

## Slide 5: General speculation
Control speculation
  “I think this branch will go to address 90004”
Data speculation
  “I’ll guess the result of the load will be zero”
Memory conflict speculation
  “I don’t think this load conflicts with any proceeding store.”
Error speculation
  “I don’t think there were any errors in this calculation”

## Slide 6: Speculation in general
Need to be 100% sure on final correctness!
  So need a recovery mechanism
  Must make forward progress!
Want to speed up overall performance
  So recovery cost should be low or expected rate of occurrence should be low.
  There can be a real trade-off on accuracy, cost of recovery, and speedup when correct.
Should keep the worst case in mind…

## Slide 7: Precise Interrupts and branches via the Reorder Buffer
MEM
@ Alloc
  Allocate result storage at Tail
@ Sched
  Get inputs (ROB T-to-H then ARF)
  Wait until all inputs ready
@ WB
  Write results/fault to ROB
  Indicate result is ready
@ CT
  Wait until inst @ Head is done
  If fault, initiate handler
  Else, write results to ARF
  Deallocate entry from ROB
IF
ID
Alloc
Sched
EX
ROB
CT
Head
Tail
PC
Dst regID
Dst value
Except?
Reorder Buffer (ROB)
  Circular queue of spec state
  May contain multiple definitions of same register
In-order
In-order
Any order
ARF

## Slide 8: Reorder Buffer Example
Code Sequence
f1 = f2 / f3
r3 = r2 + r3
r4 = r3 – r2
Initial Conditions
- reorder buffer empty
- f2 = 3.0
- f3 = 2.0
- r2 = 6
- r3 = 5
ROB
Time
H
T
regID: f1
result: ?
Except: ?
H
T
regID: f1
result: ?
Except: ?
regID: r3
result: ?
Except: ?
H
T
regID: f1
result: ?
Except: ?
regID: r3
result: 11
Except: N
regID: r4
result: ?
Except: ?
r3
regID: r8
result: 2
Except: n
regID: r8
result: 2
Except: n
regID: r8
result: 2
Except: n

## Slide 9: Reorder Buffer Example
Code Sequence
f1 = f2 / f3
r3 = r2 + r3
r4 = r3 – r2
Initial Conditions
- reorder buffer empty
- f2 = 3.0
- f3 = 2.0
- r2 = 6
- r3 = 5
ROB
Time
H
T
regID: f1
result: ?
Except: ?
regID: r3
result: 11
Except: n
regID: r4
result: 5
Except: n
H
T
regID: f1
result: ?
Except: y
regID: r3
result: 11
Except: n
regID: r4
result: 5
Except: n
regID: r8
result: 2
Except: n
regID: r8
result: 2
Except: n
H
T
regID: f1
result: ?
Except: y
regID: r3
result: 11
Except: n
regID: r4
result: 5
Except: n

## Slide 10: Reorder Buffer Example
Code Sequence
f1 = f2 / f3
r3 = r2 + r3
r4 = r3 – r2
Initial Conditions
- reorder buffer empty
- f2 = 3.0
- f3 = 2.0
- r2 = 6
- r3 = 5
ROB
Time
H
T
H
T
first inst
of fault
handler

## Slide 11: There is more complexity here
Rename table needs to be cleared
  Everything is in the ARF
  Really do need to finish everything which was before the faulting instruction in program order.
What about branches?
  Would need to drain everything before the branch.
    Why not just squash everything that follows it?

## Slide 12: And while we’re at it…
Does the ROB replace the RS?
  Is this a good thing? Bad thing?

## Slide 13: ROB
ROB
  ROB is an in-order queue where instructions are placed.
  Instructions complete (retire) in-order
  Instructions still execute out-of-order
  Still use RS
    Instructions are issued to RS and ROB at the same time
    Rename is to ROB entry, not RS.
    When execute done instruction leaves RS
  Only when all instructions in before it in program order are done does the instruction retire.

## Slide 14: Adding a Reorder Buffer

## Slide 15: Tomasulo Data Structures (Timing Free Example, “P6 scheme”)
Map Table | 
Reg | Tag
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Reservation Stations (RS) |  |  |  |  |  |  |  | 
T | FU | busy | op | RoB | T1 | T2 | V1 | V2
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
CDB | 
T | V
ARF | 
Reg | V
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
Instruction
r0=r1*r2
r1=r2*r3
Branch if r1=0
r0=r1+r1
r2=r2+1
Reorder Buffer (RoB) |  |  |  |  |  |  | 
RoB Number | 0 | 1 | 2 | 3 | 4 | 5 | 6
Dest. Reg. |  |  |  |  |  |  | 
Value |  |  |  |  |  |  | 

## Slide 16: Review Questions
Could we make this work without the RS?
  If so, why do we do that?
Why is it important to retire in order?
Why must branches wait until retirement before they announce their mispredict?
  Any other ways to do this?

## Slide 17: More review questions
What is the purpose of the RoB?
Why do we have both a RoB and a RS?
  Yes, that was pretty much on the last page…
Misprediction
  When to we resolve a mis-prediction?
  What happens to the main structures (RS, RoB, ARF, Rename Table) when we mispredict?
What is the whole purpose of OoO execution?

## Slide 18: And yet more review questions!
What is the purpose of the RoB?
Why do we have both a RoB and a RS?
Misprediction
  When to we resolve a mis-prediction?
  What happens to the main structures (RS, RoB, ARF, Rename Table) when we mispredict?
What is the whole purpose of OoO execution?

## Slide 19: When an instruction is dispatched how does it impact each major structure?
Rename table?
ARF?
RoB?
RS?

## Slide 20: When an instruction completes execution how does it impact each major structure?
Rename table?
ARF?
RoB?
RS?

## Slide 21: When an instruction retires how does it impact each major structure?
Rename table?
ARF?
RoB?
RS?

## Slide 22: Topic change
Why on earth are we doing this?
  Why do we think it helps?
Homework 2 problems 5 and 6 made the argument.
  Only need to obey true data dependencies.
    Huge speedup potential.

## Slide 23: Optimizing CPU Performance
Golden Rule: tCPU = Ninst*CPI*tCLK
Given this, what are our options
  Reduce the number of instructions executed
  Reduce the cycles to execute an instruction
  Reduce the clock period
Our first focus: Reducing CPI
  Approach: Instruction Level Parallelism (ILP)

## Slide 24: Why ILP?
Vs.
Requirements
  Parallelism
  Large window
  Limited control deps
  Eliminate “false” deps
  Find run-time deps

## Slide 25: How Much ILP is There? (Chapter 3.10)

## Slide 26: How Large Must the “Window” Be?

## Slide 27: ALU Operation GOOD, Branch BAD
Expected Number of Branches
Between Mispredicts
E(X) ~ 1/(1-p)
E.g., p = 95%, E(X) ~ 20 brs, 100-ish insts

## Slide 28: How Accurate are Branch Predictors?

## Slide 29: Impact of Physical Storage Limitations
Each instruction “in flight” must have storage for its result
  Really worse than this because of mispeculation…

## Slide 30: Registers GOOD, Memory BAD
Benefits of registers
  Well described deps
  Fast access
  Finite resource
Memory loses these benefits for flexibility
  *p = …
  *q = …
  … = *p
?

## Slide 31: “Bottom Line” for an Ambitious Design