## Slide 1: EECS 470 Final touches on Out-of-Order execution
Review
Tclk
Superscalar
Looking back
Looking forward
Lecture 10 – Winter 2024
Slides developed in part by Profs. Austin, Brehob, Falsafi, Hill, Hoe, Lipasti, Martin, Roth, Shen, Smith, Sohi, Tyson, Vijaykumar, and Wenisch of Carnegie Mellon University, Purdue University, University of Michigan, University of Pennsylvania, and University of Wisconsin.

## Slide 2: Times and Dates and Places
Exam Q&A
  Today 6-8 pm 1200 EECS
In class on Thursday similar Q&A.
One from yesterday should be in the lecture recordings by the end of the day.
Midterm Thursday 7-9pm
  DOW 1010 and 1014
  Assignments posted shortly
If you have a conflict or other issue, be sure we are aware of it.

## Slide 3
A: R1=MEM[R2+0]
B: R2=R1/R3
C: R3=R2+R0
D: Branch (R1==0)
E: R3=R1+R3
F: R3=R3+R0
G: R3=R3+19
H: R1=R7+R6
AR | Target
0 | 
1 | 
2 | 
3 | 
RRAT
AR | Target
0 | 4
1 | 2
2 | 7
3 | 1
RAT
RoB
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
3 | 2 | 44 | 55 | 3 | 66 | 7 | 11 | 8 | 20
PRF

## Slide 4: Alternative option (v0.9?)
Use “back pointers” instead of RRAT.
  Record, in the ROB, which value in the RAT you overwrote.
    On commit, free that value (it will be the same as the one you would have overwritten in the RAT!)
    On mispredict, “undo” each step in reverse order (from tail to head).
  This gives same functionality as RRAT.
    Slower to handle mispredict that is at the head of the RoB.

## Slide 5: R10K discussion
What do the RAT entries point to?
What do the RRAT entries point to?
When do we write a value to the PRF?
When do we write a value to the RRAT?
What happens on a mispredict?

## Slide 6: What happens on… (R10K)
Dispatch
Execute Complete?
Commit?
Commit of a mispredicted branch?

## Slide 7: Terminology and background
Branch RAT (BRAT)
  “Branch Stack” used by MIPSR10K paper
Retirement RAT (RRAT)
  Retirement Map table
  Architected Map table

## Slide 8: Other little details
We’ve largely ignored timing in this class.
  Focus on algorithm, not implementation.
However, there are some timing issues to worry about.
  (btw, there are timing slides on the website. Don’t take them as “truth” for your project, merely one implementation).
  One issue is “ships passing in the night”
    When a dispatching instruction is dependent on data on the CDB in the same cycle.
    Add a MUX… (where?)

## Slide 9
Optimizing CPU Performance
Golden Rule: tCPU = Ninst*CPI*tCLK
Given this, what are our options
  Reduce the number of instructions executed
  Reduce the cycles to execute an instruction
  Reduce the clock period
Our first focus: Reducing CPI
  Approach: Instruction Level Parallelism (ILP)

## Slide 10
Tclock (again)

## Slide 11: tCLK (again)
Recall: tCPU = Ninst*CPI*tCLK
What defines tCLK?
  Critical path latency (= logic + wire latency)
  Latch latency
  Clock skew
  Clock period design margins
In current and future generation designs
  Wire latency becoming dominant latency of critical path
  Due to growing side-wall capacitance
  Brings a spatial dimension to architecture optimization
    E.g., How long are the wires that will connect these two devices?

## Slide 12: Wire delay vs gate delay
From https://www.sciencedirect.com/science/article/pii/B9780128009796000044

## Slide 13: Determining the Latency of a Wire
scale
shrinks
grows
Further reading: https://asic-soc.blogspot.com/2008/10/net-delay.html

## Slide 15: But reality is worse…. (Fringe)
For Intel 0.25u process
W~=0.64
T~=0.48
H is around 0.9.
www.ee.bgu.ac.il/~Orly_lab/courses/Intro_Course/Slides/Lecture02-2-Wire.ppt

## Slide 16: And reducing the number of instructions executed…
Sorry, wrong class.
  Compilers can help with this (a lot in some cases)
  So can ISA design, but making instructions too complex hurts ILP and tCLK
    Not clear there is a lot of room here for improvement.
So on the whole reducing # of instructions doesn’t look to be viable.
  So ILP would seem to be “where it’s at”

## Slide 17
Optimizing CPU Performance
Golden Rule: tCPU = Ninst*CPI*tCLK
Given this, what are our options
  Reduce the number of instructions executed
  Reduce the cycles to execute an instruction
  Reduce the clock period
Our first focus: Reducing CPI
  Approach: Instruction Level Parallelism (ILP)

## Slide 18
Superscalar
Out-of-Order

## Slide 19: SuperScalar OoO
Out-of-order and superscalar make for a nice combination
  The whole point of OoO is to find something to do.
    Superscalar provides the resources to do it.
Out-of-order scales pretty nicely
  Dependencies resolved at rename
  True dependencies dealt with already by rename and the general OoO model.
So we’ve already done a lot of the work.

## Slide 20: But more to go
To be superscalar one needs to be able to complete more than 1 instruction per cycle in a sustained way.
  This means fetch, rename, issue, execute, CDB broadcast and retire must all be able to do 2 instructions at once.
  It is mostly a matter of scale.

## Slide 21: Fetch
Performing more than one fetch seems straightforward.
  Just grab PC and PC+4
  It can be complicated by hardware restrictions
    Say the two instructions span a cacheline
  Branches also cause problems
    What if PC+4 is wrong?
  But as long as you can usually/often fetch two life is good.
    And we can add tricks to handle these problems
      Trace cache, multi-branch predictor, Icache annotations

## Slide 22: Decode
Just have two of them.
  For x86 or other CISC this might be unreasonable
    Trace cache or otherwise caching decoded instructions might help here.

## Slide 23: Rename
One change is we need more ports to the RAT.
Other (bigger) issue is making sure dependencies inside of the group are dealt with.
    R1=…
    …=R1
  How do we handle this?
    Basically similar to “register forwarding” inside of the register file

## Slide 24: RAT
Write
Read
AW1
AW2
AR1a
AR1b
AR2a
AR2b
PW1
PW2
PR1a
PR1b
PR2a
PR2b
Situation: Two instructions (1 and 2) come in to the RAT. RAT renames two source
registers per instruction (ARXa and ARXb) and allocates new PRF for two destination
locations.

## Slide 25: Dispatch
Need to be able to send more than one instruction to the RoB and RS per cycle
  Just more ports in RS and RoB.
  A bit more complexity with “Ships passing in the Night”.
  Read ports in PRF (R10K)
    Read ports in ARF/ROB (P6)

## Slide 26: Wake-up/select
We’ve already been allowing more than one instruction to go to an exec unit per cycle.
  No real change here.

## Slide 27: Execute complete/CDB
As two instructions need to be able to complete per cycle need more than one CDB.
  In general everyone has to listen to everyone
  Could try to partition CDBs but this is tricky.
  Makes RS’s bigger and probably slower.
RoB needs yet more ports.

## Slide 28: Commit
In R10K this isn’t a big deal.
  But need to realize that more than one instruction at the head of the RoB is done (more ports) and must be able to complete them (maybe more ports)
  In P6, you’ve got to do more copies.
    Multiple read ports (RoB); multiple write ports (ARF)

## Slide 29
LSQ

## Slide 30: LSQ issues
Load/Store queue
  It is pretty tricky to get right.
    Send to LSQ at issue
    Does this replace the RS?
      Maybe…
  Probably a Store (circular) queue and a load buffer
    Loads need to note which stores they care about
      Ones that were there when the load issued
      Need to not get caught by “wrap around” of the store queue
    Loads need to check for what exactly?

## Slide 31: So what to do?
You have a lot of options on load launch
  Conservative
    Launch loads at the head of the LSQ (bad)
  Moderate
    Launch loads at when no conflicting/unknown stores exist in front of you (ok)
  Aggressive
    Launch loads ASAP, but fix if wrong.
    Lots of potential issues.
      Imagine you launched a load then solve it by forwarding. What happens when the load returns?
And store forwarding might be tricky.
  Can you identify the situation when you can forward?
    If so, can you write verilog code for that?

## Slide 32: Non-LSQ options
Just launch loads from the RoB when they hit the head (easy/poor)
As above, but prefetch the data into the cache ASAP.
  This might actually work well. Probably need non-direct-mapped cache though.
Use RoB to track when load has no conflicting/unknown stores in front of it.
  Seems annoying, might be easy. Still poorish performance.
More on memory
disambiguation later

## Slide 33
Misc other stuff

## Slide 34: More details
RS
  We’ve been doing generic RSs
  Could also dedicate groups of RSs to a single execution unit (or group of similar execution units).
    May make the RSs simpler
    Will result in needing more total RSs to get the same performance
    Everyone needs to listen to the CDB
    For the project, means you have a bunch of similar code. Often a bad idea when fixing bugs.

## Slide 35: Reading the register file on the way to EX
The idea is to not read the PRF or RoB or CDB for the value, only for the fact that the value is available.
    Grab the value on your way to the EX unit.
  Advantages
    No CDB broadcast of values
    Don’t need to look in the PRF/ARF/RoB for values on issue.
  Disadvantages
    Already slow Wake-up/select/dispatch now slower
      (But as we may be pipelining this anyways, not too bad).

## Slide 36: Back-to-Back dependent instructions
What has to happen to get them to go back to back?
  Why is this hard?
  How is it solved in the real world?

## Slide 37
Looking back
(and foward)

## Slide 38: Looking back
Keep the big picture in mind
  OoO is about finding ILP.
      If you don’t need ILP don’t bother
    Why might you not need ILP?
      Application doesn’t need it
      TLP instead.
  In many ways this is about finding work to do while high-latency instructions run
    If you fix the memory problem, it isn’t clear that OoO makes any sense.

## Slide 39: Looking back
Renaming is distinct from OoO
  You can rename without OoO
    (Not obviously useful!)
  You can have OoO without renaming
    In fact the first OoO processor, CDC 6600 used scoreboarding which had no renaming but is out-of-order.

## Slide 40: Static vs. Dynamic reordering
Some reordering is better done statically
  Have a global view
      (infinite window)
  Have access to the original source
    May tell you about intent or even behavior.
      Array behavior may make load/store conflicts easy to identify.
  Regular code structures may lend themselves to optimal ordering
    Software pipelining
Just a one-time compile cost.
  Saves power and hardware cost if reordering done in software!

## Slide 41: Static vs. Dynamic
Some things are better done dynamically
  Have live data
    Worst case vs. actual case
      Load/Store ordering possible to get right without being paranoid about the worst case.
    Program behavior may change based on data set
      Branch prediction in particular
  Can speculate
    Static specifies program behavior. Much harder to speculate in the complier.

## Slide 42: Looking forward
There is a LOT more to architecture than out-of-order execution
  Memory
    If OoO is mostly about reordering around high-latency loads memory sounds important
  Power
    Modern processors are eating huge amounts of power and we can’t cool them. So what can an architect do?
  Multi-processors
    One way to get performance is to have many processors working on a task.
  Static reordering
    As noted, saves power over dynamic & might be able to use both together to get a nice impact.