## Slide 1: EECS 470
Cache overview
4 Hierarchy questions
More on Locality
Lecture 11 & 12: Caches – Winter 2024
Slides developed in part by Profs. Austin, Brehob, Falsafi, Hill, Hoe, Lipasti, Martin, Roth, Shen, Smith, Sohi, Tyson, Vijaykumar, and Wenisch of Carnegie Mellon University, Purdue University, University of Michigan, University of Pennsylvania, and University of Wisconsin.

## Slide 2: Class project
Project restrictions
  The I-cache and D-cache size is limited to the size it has in what we gave you.
  Can’t have more CDBs then degree of super scalarness.
  Must use our multiplier (P2)
Milestone 1:
    It is due on Tues 3/5
    Should have high-level design done ASAP.
    Module you hand in should be:
      Self testing, well written.
    Be aware of sample (single) RS on the website.

## Slide 3
Memory pyramid
Disk (Many GB)
Memory (128MB – fewGB)
L2 Cache (½-32MB)
L1 Cache
(several KB)
Reg
100s bytes
Cache Design 101
1 cycle access (early in pipeline)
1-4 cycle access
6-15 cycle access
100-500 cycle access
Millions cycle access!

## Slide 4
Cache1
1 a : a hiding place especially for concealing and preserving provisions or implements b : a secure place of storage
3 : a computer memory with very short access time used for storage of frequently used instructions or data -- called also cache memory
1From Merriam-Webster on-line
Cache overview

## Slide 5: Locality of Reference
Principle of Locality:
  Programs tend to reuse data and instructions near those they have used recently.
  Temporal locality: recently referenced items are likely to be referenced in the near future.
  Spatial locality: items with nearby addresses tend to be referenced close together in time.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
*v = sum;
Locality in Example:
  Data
    Reference array elements in succession (spatial)
  Instructions
    Reference instructions in sequence (spatial)
    Cycle through loop repeatedly (temporal)

## Slide 6: Caching: The Basic Idea
Main Memory
  Stores words
    A–Z in example
Cache
  Stores subset of the words
    4 in example
  Organized in lines
    Multiple words
    To exploit spatial locality
Access
  Word must be in cache for processor to access
Big, Slow Memory
A
B
C
•
•
•
Y
Z
Small,
Fast Cache
A
B
G
H
Processor

## Slide 7
Direct-mapped cache
29
123
150
162
18
33
19
210
00000
00010
00100
00110
01000
01010
01100
01110
10000
10010
10100
10110
11000
11010
11100
11110
Cache
V d tag data
Memory
78
120
71
173
21
28
200
225
0
0
0
0
Address
01101
218
44
141
28
33
181
119
66
23
10
16
214
98
129
42
74
Block Offset (1-bit)
Line Index (2-bit)
Tag (2-bit)
Compulsory Miss: first reference to memory block
Capacity Miss: Working set doesn’t fit in cache
Conflict Miss: Working set maps to same cache line
3-C’s
Cache overview

## Slide 8
2-way set associative cache
29
123
150
162
18
33
19
210
00000
00010
00100
00110
01000
01010
01100
01110
10000
10010
10100
10110
11000
11010
11100
11110
Cache
V d tag data
Memory
78
120
71
173
21
28
200
225
0
0
0
0
Address
01101
218
44
141
28
33
181
119
66
23
10
16
214
98
129
42
74
Block Offset (unchanged)
1-bit Set Index
Larger (3-bit) Tag
Impact on the 3C’s?
Cache overview

## Slide 9: Parameters
Total cache size
  (block size  # sets  associativity)
Associativity (Number of “ways”)
Block size (bytes per block)
Number of sets
Cache overview

## Slide 10
Performance Measures
  Miss rate
    % of memory refereces which are not found in the cache.
    A related measure is #misses per 1000 instructions
  Average memory access time
    MR*TMiss + (1-MR)* THit
      THit & TMiss --Access time for a hit or miss
But what do we want to measure?
  Impact on program execution time.
What are some flaws of using
  Miss Rate?
  Ave. Memory Access Time?
  Program execution time?
  Misses per 1000 instructions?
Cache overview

## Slide 11
Effects of Varying Cache Parameters
Total cache size?
  Positives:
    Should decrease miss rate
  Negatives:
    May increase hit time
    Increased area requirements
    Increased power (mainly static)
      Interesting paper:
        Krisztián Flautner, Nam Sung Kim, Steve Martin, David Blaauw, Trevor N. Mudge: Drowsy Caches: Simple Techniques for Reducing Leakage Power. ISCA 2002: 148-157
Cache overview

## Slide 12
Effects of Varying Cache Parameters
Bigger block size?
  Positives:
    Exploit spatial locality ; reduce compulsory misses
    Reduce tag overhead (bits)
    Reduce transfer overhead (address, burst data mode)
  Negatives:
    Fewer blocks for given size; increase conflict misses
    Increase miss transfer time (multi-cycle transfers)
    Wasted bandwidth for non-spatial data
Cache overview

## Slide 13
Effects of Varying Cache Parameters
Increasing associativity
  Positives:
    Reduces conflict misses
    Low-assoc cache can have pathological behavior (very high miss)
  Negatives:
    Increased hit time
    More hardware requirements (comparators, muxes, bigger tags)
    Minimal improvements past 4- or 8- way.
Cache overview

## Slide 14
Effects of Varying Cache Parameters
Replacement Strategy: (for associative caches)
  LRU: intuitive; difficult to implement with high assoc; worst case performance can occur (N+1 element array)
  Random: Pseudo-random easy to implement; performance close to LRU for high associativity
  Optimal: replace block that has next reference farthest in the future; hard to implement (need to see the future) 
Cache overview

## Slide 15
Effects of Varying Cache Parameters
Write Policy: How to deal with write misses?
  Write-through / no-allocate
    Total traffic? Read misses  block size + writes
    Common for L1 caches back by L2 (esp. on-chip)
  Write-back / write-allocate
    Needs a dirty bit to determine whether cache data differs
    Total traffic? (read misses + write misses)  block size + dirty-block-evictions  block size
    Common for L2 caches (memory bandwidth limited)
  Variation: Write validate
    Write-allocate without fetch-on-write
    Needs sub-block cache with valid bits for each word/byte

## Slide 16: 4 Hierarchy questions
Where can a block be placed?
How do you find a block (and know you’ve found it)?
Which block should be replaced on a miss?
What happens on a write?
Cache overview

## Slide 17: So from here…
We need to think in terms of both the hierarchy questions as well as performance.
  We often will use Average Access Time as a predictor of the impact on execution time. But we will try to keep in mind they may not be the same thing!
Even all these questions don’t get at everything!
Cache overview

## Slide 18: Set Associative as a change from Direct Mapped
Impact of being more associative?
  MR? TMiss? THit?
Hierarchy questions:
  Where can a block be placed?
  How do you find a block (and know you’ve found it)?
  Which block should be replaced on a miss?
  What happens on a write?
4 Hierarchy questions

## Slide 19: Hash cache
Idea:
  Grab some bits from the tag and use them, as well as the old index bits, to select a set.
  Simplest version would be if N sets, grab the 2N lowest order bits after the offset and XOR them in groups of 2.
Impact:
  Impact of being more associative?
    MR? TMiss? THit?
  Hierarchy questions:
    Where can a block be placed?
    How do you find a block (and know you’ve found it)?
    Which block should be replaced on a miss?
    What happens on a write?
4 Hierarchy questions

## Slide 20: Skew cache
Idea:
  As hash cache but a different and independent hashing function is used for each way.
Impact:
  Impact of being more associative?
    MR? TMiss? THit?
  Hierarchy questions:
    Where can a block be placed?
    How do you find a block (and know you’ve found it)?
    Which block should be replaced on a miss?
    What happens on a write?
4 Hierarchy questions

## Slide 21: Victim cache
Idea:
  A small fully-associative cache (4-8 lines typically) that is accessed in parallel with the main cache. This victim cache is managed as if it were an L2 cache (even though it is as fast as the main L1 cache).
Impact:
  Impact of being more associative?
    MR? TMiss? THit?
  Hierarchy questions:
    Where can a block be placed?
    How do you find a block (and know you’ve found it)?
    Which block should be replaced on a miss?
    What happens on a write?
4 Hierarchy questions

## Slide 22: What’s hard about implementing caches?

## Slide 23: So…
What’s hard about caches?
  And in particular, for the project?
There are a lot of implementation details that get tricky
  LRU is tricky to do above 2 way
  Critical word first
    less important for the project, but a real issue.
  Making a non-blocking cache is tricky
  Writes are tricky
  Dealing with load/store dependencies
  Multi-processor issues
Difficult things with caches

## Slide 24: Critical Word First
Idea:
  For caches where the line size is greater than the word size, send the word which causes the miss first
Why?
  As always, the processor is what matters.
  We are getting extra data (cache line) into the cache to handle future requests
  But we want to get the current request handled as quickly as possible.
What’s hard?
  Memory system needs to support this.
  We need to take an action while the data is still arriving.
Difficult things with caches: Critical Word First

## Slide 25: LRU is difficult
We want to keep track of the exact order things have been used in the set.
  So if I have 4 things, I want to know the MRU, the next MRU, etc.
I could maintain a stack-like structure
  But that’s a lot of data movement.
I could maintain a counter for each line
  But that’s a lot of work and area (why area?)
No good way to track LRU?
  Something smart?
Difficult things with caches: LRU

## Slide 26: Pseudo-LRU replacement
# of bits needed to maintain order among N items?
So for N=16 we need: ____ bits.
Any better ideas?
45
Difficult things with caches: LRU

## Slide 27: Psuedo LRU
Way 0 | Way 1 | Way 2 | Way 3
General theme:
On a hit or replacement, switch all the bits to point away
from you.
Replace the one pointed to.
0
0
0
1
1
1
Difficult things with caches: LRU

## Slide 28: Handling Multiple Outstanding Accesses
Question: If the processor can generate multiple cache accesses, can the later accesses be handled while a previous miss is outstanding?
Goal: Enable cache access when there is a pending miss
Goal: Enable multiple misses in parallel
  Memory-level parallelism (MLP)
Solution: Non-blocking or lockup-free caches
  Kroft, “Lockup-Free Instruction Fetch/Prefetch Cache Organization," ISCA 1981.
This section from Dr. Onur Mutlu
Difficult things with caches: Non-blocking caches
Notes: Onur Mutlu

## Slide 29: Handling Multiple Outstanding Accesses
Idea: Keep track of the status/data of misses that are being handled in Miss Status Handling Registers (MSHRs)
  A cache access checks MSHRs to see if a miss to the same block is already pending.
    If pending, a new request is not generated
    If pending and the needed data available, data forwarded to later load
  Requires buffering of outstanding miss requests
Difficult things with caches: Non-blocking caches

## Slide 30: Miss Status Handling Register
Also called “miss buffer”
Keeps track of
  Outstanding cache misses
  Pending load/store accesses that refer to the missing cache block
Fields of a single MSHR entry
  Valid bit
  Cache block address (to match incoming accesses)
  Control/status bits (prefetch, issued to memory, which subblocks have arrived, etc)
  Data for each subblock
  For each pending load/store
    Valid, type, data size, byte in block, destination register or store buffer entry address
Difficult things with caches: Non-blocking caches

## Slide 31: MSHR Operation
On a cache miss:
  Search MSHRs for a pending access to the same block
    Found: Allocate a load/store entry in the same MSHR entry
    Not found: Allocate a new MSHR
    No free entry: stall
When a subblock returns from the next level in memory
  Check which loads/stores waiting for it
    Forward data to the load/store unit
    De-allocate load/store entry in the MSHR entry
  Write subblock in cache or MSHR
  If last subblock, de-allaocate MSHR (after writing the block in cache)
Difficult things with caches: Non-blocking caches

## Slide 32: Non-Blocking Cache Implementation
When to access the MSHRs?
  In parallel with the cache?
  After cache access is complete?
MSHRs need not be on the critical path of hit requests
  Which one below is the common case?
    Cache miss, MSHR hit
    Cache hit
Difficult things with caches: Non-blocking caches

## Slide 33: Miss Status Handling Register Entry
Difficult things with caches: Non-blocking caches

## Slide 34: So…
What’s hard about caches?
  And in particular, for the project?
There are a lot of implementation details that get tricky
  LRU is tricky to do above 2 way
  Critical word first
    less important for the project, but a real issue.
  Making a non-blocking cache is tricky
  Writes are tricky
  Dealing with load/store dependencies
  Multi-processor issues
Difficult things with caches

## Slide 35: 3C’s model
Break cache misses into three categories
  Compulsory miss
  Capacity miss
  Conflict miss
Compulsory
  The block in question had never been accessed before.
Capacity
  A fully-associative cache of the same size would also have missed this access given the same reference stream.
Conflict
  That fully-associative cache would have gotten a hit.

## Slide 36: 3C’s example
Consider the “stream” of blocks 0, 1, 2, 0, 2, 1
  Given a direct-mapped cache with 2 lines, which would hit, which would miss?
  Classify each type of miss.

## Slide 37: 3C’s – sum-up.
What’s the point?
  Well, if you can figure out what kind of misses you are getting, you might be able to figure out how to solve the problem.
    How would you “solve” each type?
What are the problems?

## Slide 38: Reference stream
A memory reference stream is an n-tuple of addresses which corresponds to n ordered memory accesses.
  A program which accesses memory locations 4, 8 and then 4 again would be represented as (4,8,4).

## Slide 39: Locality of reference
The reason small caches get such a good hit-rate is that the memory reference steam is not random.
  A given reference tends to be to an address that was used recently. This is called temporal locality.
  Or it may be to an address that is near another address that was used recently. This is called spatial locality.
Therefore, keeping recently accessed blocks in the cache can result in a remarkable number of hits.
  But there is no known way to quantify the amount of locality in the reference stream.

## Slide 40: Stack distance – A measure of locality
Consider the reference stream
(0, 8, 4, 4, 12, 16, 32, 4)
If the cache line size is 8 bytes, the block reference stream is
(0, 1, 0, 0, 1, 2, 4, 0)
Now define the stack distance of a reference to be the number of unique block addresses between the current reference and the previous reference to the same block number. In this case
(, , 1, 0, 1, , , 3)

## Slide 41: Stack distance – A measure of locality (2)
Memory reference stream | 0 | 8 | 4 | 4 | 12 | 16 | 32 | 4
Block reference stream | 0 | 1 | 0 | 0 | 1 | 2 | 4 | 0
Stack distance |  |  | 1 | 0 | 1 |  |  | 3
Number non-infinite accesses
Cumulative stack distance

## Slide 42: Stack distances of the SPEC benchmarks – cumulative
Notes: Can see that SPECint has more locality than SPECfp

## Slide 43: Stack distances of selected SPECfp benchmarks

## Slide 44: Why is this interesting?
It is possible to distinguish locality from conflict.
  Pure miss-rate data of set-associative caches depends upon both the locality of the reference stream and the conflict in that stream.
It is possible to make qualitative statements about locality
  For example, SPECint has a higher degree of locality than SPECfp.

## Slide 45: Fully-associative caches
A fully-associative LRU cache consisting of n lines will get a hit on any memory reference access with a stack distance of n-1 or less.
  Fully associative caches of size n store the last n uniquely accessed blocks.
  This means the locality curves are simply a graph of the hit rate on a fully associative cache of size n-1.

## Slide 46: Direct-mapped caches
Consider a direct-mapped cache of n cache lines and the block reference stream (x, y, x).
  The second reference to x will be a hit unless y is mapped to the same cache line as x.
  If x and y are independent, the odds x being a hit is (n-1)/n
In general if there are m unique accesses between the two references to x, the odds of a hit are:

## Slide 47: Expected hit rate at a given stack distance for a 128-line cache
Notes: Similar things can be done for set-associative caches
Area under each curve=128
Simply moving the area around.

## Slide 48: Verification – direct mapped 128-entry cache
SPECfp
SPECint

## Slide 49: Why is this interesting?
It is possible to see exactly why more associative caches do better than less associative caches
  It also becomes possible to see when they do worse.
  The area under the curve is always equal to the number of cache lines.
It provides an expectation of performance.
  If things are worse, there must be excessive conflict.
  If things are better, it is likely due to spatial locality.

## Slide 50: The 3C’s model
The 3’Cs model describes misses as conflict, capacity or compulsory by comparing a direct-mapped cache to a fully-associative cache.
  Those accesses in the gray area are conflict misses.
  The in the green area are capacity misses.
  The blue area is where both caches get a hit.
  The yellow area is ignored by the 3C’s model. Perhaps a “conflict hit”?
The 3C’s model is much more limited.
  It cannot distinguish between expected conflict and excessive conflict.

## Slide 51
64-line DM
64-line FA
128-line FA
128-line DM

## Slide 52: The filtering of locality (1/2) gcc after a 64KB direct-mapped cache

## Slide 53: The filtering of locality (2/2)
Notice that there fewer references at the lowest stack distances than at the highest.
  Yet it is at the lowest stack distances where highly-associative caches concentrate their power.
  The locality seen by the L2 cache is fundamentally different than that seen by the L1 cache
    A large enough cache can make this effect go away…

## Slide 54: Measuring non-random conflict (1/2)
Combining the cache and locality models makes it possible to predict a hit rate.
  On these reference streams the cache tends to do better than predicted.
    Although some benchmarks, like mgrid, see significantly worse performance.
Benchmark | Average predicted hit rate | Average actual hit rate
SPECint | 90.81% | 91.38%
SPECfp | 83.19% | 83.84%

## Slide 55: Measuring non-random conflict (2/2)
A more advanced technique, using a hash-cache, allows us to roughly quantify the amount of excessive conflict and scant conflict.
  This can be useful when deciding if a hash cache is appropriate.
  It is also useful to provide feedback to the compiler about its data-layout choices.
Other compilers (gcc for example) tend to have a higher degree of excessive conflict.
  So this technique may also be able to tell us something about compliers.

## Slide 56: Understanding non-standard caches 128-line direct-mapped component and a 6-line victim component

## Slide 57: Some review
Consider the access pattern A, B, C, A. Assume the three accesses are all independently randomly placed with uniform probability
  In a direct-mapped cache with 8 lines, what is the probability of a miss?
  A two-way associative cache with 4 lines?
  A victim cache of 1 one backing up a direct-mapped cache of 4 lines?
  A skew cache with 8 lines?
What is bogus about the above assumptions?

## Slide 58: VIPT caches
(Done on board)