## Slide 1: EECS 470 Power and Architecture
Many slides taken from Prof. David Brooks, Harvard University and modified by Mark Brehob . A couple of slides are also taken from Prof. Wenisch. Any errors are almost certainly Mark’s.
Thanks to both!
Introduction

## Slide 2: Outline
Why is power a problem?
What uses power in a chip?
Relationship between power and performance.
How can we reduce power?
Introduction

## Slide 3: Why is power a problem in a μP?
Power used by the μP, vs. system power
Dissipating Heat
  Melting (very bad)
  Packaging (to cool  $)
  Heat leads to poorer performance.
Providing Energy
  Battery
  Cost of electricity
Introduction

## Slide 4: Why worry about power dissipation?
Environment
Thermal issues: affect cooling, packaging, reliability, timing
Battery
life
Why is power a problem?

## Slide 5: Where does the juice go in laptops?
Left, Microsoft, 2009.
Top Right, Samavat, 2011
Bottom Right, Kumar, Kumar, Taruna 2020

## Slide 6: Servers and data centers?
Chart: 
Need whole-system
approaches to save energy
K.M.U. Ahmed et al.: A Review of Data Centers Energy Consumption And Reliability Modeling

## Slide 7: More data center
Power usage effectiveness (PUE)
A PUE of 2.0 means that for every 2W of power supplied to the data center, only 1W is consumed by computing equipment. Values of around 2.9 are pretty common
Data Centers are about 1.5% of global electricity use as of 2023
https://www.scientificamerican.com/ article/the-ai-boom-could-use-a-shocking-amount-of-electricity

## Slide 8: A Paradigm Shift In Computing
Chart: 
| 1971 | 1972 | 1974 | 1978 | 1982 | 1985 | 1989 | 1993 | 1996 | 1998 | 2000 | 2001 | 2002 | 2004 | 2007 | 2008
Transistors (100,000's) | 0.023 | 0.025 | 0.045 | 0.29 | 1.34 | 2.75 | 12 | 31 | 75 | 95 | 420 | 250 | 2200 | 5920 | 9000 | 20000
Power (W) | 2 | 9 | 12 | 20 | 52 | 78 | 85 | 85 | 100 | 100 | 100
Performance (GOPS) | 0.006 | 0.117 | 0.481 | 0.993 | 3.016 | 5.46 | 7.65 | 11.05 | 16 | 20.49 | 26
Efficiency (GOPS/W) | 0.003 | 0.013 | 0.040083 | 0.04965 | 0.058 | 0.07 | 0.09 | 0.13 | 0.16 | 0.2049 | 0.26
Era of High Performance Computing Era of Energy-Efficient Computing
c. 2000
Limits on heat extraction
Limits on energy-efficiency of operations
Stagnates performance growth
IEEE Computer—April 2001
T. Mudge
Notes: ----Data points generated from the following processors
VAX-11/780
VAX-11/785
VAX 8700
Sun-4/260
MIPS M/120
MIPS M2000
IBM RS6000/540
HP PA-RISC, 0.05 GHz
Alpha 21064, 0.2 GHz
PowerPC 604, 0.1 GHz
Alpha 21064A, 0.3 GHz
Alpha 21164, 0.3 GHz
Alpha 21164, 0.5 GHz
Alpha 21164, 0.6 GHz
Alpha 21264, 0.6 GHz
Alpha 21264A, 0.7 GHz
Intel Pentium III, 1.0 GHz
AMD Athlon, 1.6 GHz
Intel Pentium 4, 3.0 GHz
AMD Opteron, 2.2 GHz
Intel Xeon, 3.6 GHz
64-bit Intel Xeon, 3.6 GHz

## Slide 9: Spot Heat Issues in Microprocessors
Why is power a problem?

## Slide 10: Why is cooling so costly? (1)
Server density increasing
Integration, disaggregation reduce hardware costs
Need for high-BW interconnect
Data center floor space costs up to $15,000 /m2
Heat flux up to
500W per ft2 floor space;
Racks draw 4 to 20kW each
Source: AHRAE 2006

## Slide 11: Why is cooling so costly? (2)
Source: C. Patel, HP Labs
Servers’ 3-year power & cooling costs nearing their purchase price
Heat density drives cooling cost
Cooling power grows super-linearly with thermal load
Heat Generated
Power to Remove
100W
250W
20kW
5W
1MW
1MW
2kW
20W

## Slide 12: Intel Itanium packaging
Complex and expensive (note heatpipe)
Source: H. Xie et al. “Packaging the Itanium Microprocessor”
Electronic Components and Technology Conference 2002
Why is power a problem?

## Slide 13: P4 packaging
Simpler, but still…
Source: Intel web site
From Tiwari, et al., DAC98
Why is power a problem?

## Slide 14: Power-Aware Computing Applications
Energy-Constrained Computing
Temperature/di-dt-Constrained

## Slide 15: Environment
Environment Protection Agency (EPA): computers consume 10% of commercial electricity consumption
  This incl. peripherals, possibly also manufacturing
  A DOE report suggested this percentage is much lower (3.0-3.5%)
  No consensus, but it’s still a lot
  Total cost of electricity for gaming computers estimated at $10 Billion/year.
    http://newscenter.lbl.gov/2015/08/31/gaming-computers-offer-huge-untapped-energy-savings-potential/
Data center growth was cited as a contribution to the 2000/2001 California Energy Crisis
Equivalent power (with only 30% efficiency) for AC
Lap burn
Fan noise
Why is power a problem?

## Slide 16: Power-Aware Needed across all computing platforms
Mobile/portable (cell phones, laptops, PDA)
  Battery life is critical
Desktops/Set-Top (PCs and game machines)
  Packaging cost is critical
Servers (Mainframes and compute-farms)
  Packaging limits
  Volumetric (performance density)
Why is power a problem?

## Slide 17: How CMOS Transistors Work
What uses power in a chip?

## Slide 18: MOS Transistors are Switches
What uses power in a chip?

## Slide 19: Static CMOS
What uses power in a chip?

## Slide 20: Basic Logic Gates
What uses power in a chip?

## Slide 21: CMOS Water Analogy
Electron: water molecule
Charge: weight of water
Voltage: height
Current: flow rate
Capacitance: container cross-section
(Think of power-plants that store energy in water towers)
What uses power in a chip?

## Slide 22: Liquid Inverter
Capacitance at input
  Gates of NMOS, PMOS
  Metal interconnect
Capacitance at output
  Fanout (# connections) to other gates
  Metal Interconnect
NMOS conducts when water level is above switching threshold
PMOS conducts below
No conduction after container full
Slide courtesy D. Brooks, Harvard

## Slide 23: Inverter Signal Propagation (1)
Slide courtesy D. Brooks, Harvard

## Slide 24: Inverter Signal Propagation (2)
Slide courtesy D. Brooks, Harvard

## Slide 25: Delay and Power Observations
Load capacitance increases delay
  High fanout (gates attached to output)
  Interconnection
Higher current can increase speed
  Increasing transistor width raises currents but also raises capacitance
Energy per switching event independent of current
  Depends on amount of charge moved, not rate
What uses power in a chip?

## Slide 26: Power: The Basics
Dynamic power vs. Static power
  Dynamic: “switching” power
  Static: “leakage” power
  Dynamic power dominates, but static power increasing in importance
Static power: steady, per-cycle energy cost
Dynamic power: capacitive and short-circuit
Capacitive power: charging/discharging at transitions from 01 and 10
Short-circuit power: power due to brief short-circuit current during transitions.
What uses power in a chip?

## Slide 27: Dynamic (Capacitive) Power Dissipation
Data dependent – a function of switching activity
What uses power in a chip?

## Slide 28: Capacitive Power dissipation
Power ~ ½ CV2Af
Capacitance:
Function of wire length, transistor size
Supply Voltage:
Has been dropping with successive fab generations
Clock frequency:
Increasing…
Activity factor:
How often, on average, do wires switch?
What uses power in a chip?

## Slide 29: Lowering Dynamic Power
Reducing Vdd has a quadratic effect
  Has a negative (~linear) effect on performance however
Lowering CL
  May improve performance as well
  Keep transistors small (keeps intrinsic capacitance (gate and diffusion) small)
Reduce switching activity
  A function of signal transition stats and clock rate
  Clock Gating idle units
  Impacted by logic and architecture decisions
What uses power in a chip?

## Slide 30: Static Power: Leakage Currents
Subthreshold currents grow exponentially with increases in temperature, decreases in threshold voltage
  But threshold voltage scaling is key to circuit performance!
Gate leakage primarily dependent on gate oxide thickness, biases
Both type of leakage heavily dependent on stacking and input pattern
What uses power in a chip?

## Slide 31: Lowering Static Power
Design-time Decisions
  Use fewer, smaller transistors -- stack when possible to minimize contacts with Vdd/Gnd
  Multithreshold process technology (multiple oxides too!)
    Use “high-Vt” slow transistors whenever possible
Dynamic Techniques
  Reverse-Body Bias (dynamically adjust threshold)
    Low-leakage sleep mode (maintain state), e.g. XScale
  Vdd-gating (Cut voltage/gnd connection to circuits)
    Zero-leakage sleep mode
    Lose state, overheads to enable/disable
What uses power in a chip?

## Slide 32: Power vs. Energy
Power consumption in Watts
  Determines battery life in hours
  Sets packaging limits
Energy efficiency in joules
  Rate at which energy is consumed over time
  Energy = power * delay (joules = watts * seconds)
  Lower energy number means less power to perform a computation at same frequency
What uses power in a chip?

## Slide 33: Power vs. Energy
What uses power in a chip?

## Slide 34: Power vs. Energy
Power-delay Product (PDP) = Pavg * t
  PDP is the average energy consumed per switching event
Energy-delay Product (EDP) = PDP * t
  Takes into account that one can trade increased delay for lower energy/operation
Energy-delay2 Product (EDDP) = EDP * t
  Why do we need so many formulas?!!?
  We want a voltage-invariant efficiency metric! Why?
  Power ~ ½ CV2Af, Performance ~ f (and V)
What uses power in a chip?

## Slide 35: E vs. EDP vs. ED2P
Power ~ CV2f ~ V3 (fixed microarch/design)
Performance ~ f ~ V (fixed microarch/design)
(For the nominal voltage range, f varies linearly with V)
Comparing processors that can only use freq/voltage scaling as the primary method of power control:
  (perf)3 / power, or MIPS3 / W is a fair metric to compare energy efficiencies.
  This is an ED2 P metric. We could also use: (CPI)3 * W for a given application
What uses power in a chip?

## Slide 36: E vs. EDP vs. ED2P
Currently have a processor design:
  80W, 1 BIPS, 1.5V, 1GHz
  Want to reduce power, willing to lose some performance
  Cache Optimization:
    IPC decreases by 10%, reduces power by 20% => Final Processor: 900 MIPS, 64W
    Relative E = MIPS/W (higher is better) = 14/12.5 = 1.125x
  Energy is better, but is this a “better” processor?
What uses power in a chip?

## Slide 37: Not necessarily
80W, 1 BIPS, 1.5V, 1GHz
  Cache Optimization:
    IPC decreases by 10%, reduces power by 20% => Final Processor: 900 MIPS, 64W
    Relative E = MIPS/W (higher is better) = 14/12.5 = 1.125x
    Relative EDP = MIPS2/W = 1.01x
    Relative ED2P = MIPS3/W = .911x
What if we just adjust frequency/voltage on processor?
  How to reduce power by 20%?
  P = CV2F = CV3 => Drop voltage by 7% (and also Freq) => .93*.93*.93 = .8x
  So for equal power (64W)
    Cache Optimization = 900MIPS
    Simple Voltage/Frequency Scaling = 930MIPS
What uses power in a chip?