## Slide 1: On Power and Multi-Processors
Finishing up power issues and how those issues have led us to multi-core processors.
Introduce multi-processor systems.

## Slide 2: Capacitive Power dissipation
Power ~ ½ CV2Af
Capacitance:
Function of wire length, transistor size
Supply Voltage:
Has been dropping with successive fab generations
Clock frequency:
Increasing…
Activity factor:
How often, on average, do wires switch?
What uses power in a chip?

## Slide 3: With more voltage you can get a higher frequency
Back to our water analogy:
  The higher voltage is a higher water tower so a higher water pressure.
  The “buckets” fill up faster
  The circuit is faster.
This is roughly a linear relationship over a fairly small dynamic range.

## Slide 4: And so…
Power ~ ½ CV2Af.
  We can scale frequency with voltage.
  We can claim that power ~proportional to f3.
Performance ~f.
  Doubling frequency doesn’t double performance (memory latency) but it’s close enough for our “~”
Say we have a processor that uses 100W and can do 1 billion operations per second (1GOP).
  Increasing performance to 1.1 GOPs with voltage/frequency scaling will need (1.1)3 *100W= 133W

## Slide 5: Can we do better?
Can’t we get speedup in other ways than frequency scaling?
  Of course. Bigger caches, increasing superscalar, etc.
  But most of these have a pretty high performance/power ratio also.
    Consider being more superscalar
      The cost for each “level” is more than the previous (why?)
      The benefit of each “level” is less than the previous (why?)
    Caches are similar.
      Doubling a cache size roughly halves its miss rate.
        That’s a doubling in cache power for fewer and fewer misses removed (and higher and higher latency!)

## Slide 6: Sample problem
Say I have a 200W budget and a single-core processor that can do 10 GOPs.
  What performance would I expect to get out of two cores using the same power budget?
  Four cores?
  Eight cores?
Does this really scale so nicely?
  Of course not, but it’s another dimension to extract performance from
    Thread-level!

## Slide 7: So…
Multiprocessors seem like a good place to improve performance with a more reasonable power cost.

## Slide 8: Why multi-processors?
Why multi-processors?
  Multi-processors have been around for a long time.
    Originally used to get best performance for certain highly-parallel tasks.
  We now use them to get solid performance per unit of energy.
    Basic theme: it’s much less energy to do two things slowly than one thing twice as fast.
So that’s it?
  Not so much.
    We need to make it possible/reasonable/easy to use.
    Nothing comes for free.
      If we take a task and break it up so it runs on a number of processors, there is going to be a price.

## Slide 9: Thread-Level Parallelism
Thread-level parallelism (TLP)
  Collection of asynchronous tasks: not started and stopped together
  Data shared loosely, dynamically
Example: database/web server (each query is a thread)
  accts is shared, can’t register allocate even if it were scalar
  id and amt are private variables, register allocated to r1, r2
struct acct_t { int bal; };
shared struct acct_t accts[MAX_ACCT];
int id,amt;
if (accts[id].bal >= amt)
{
accts[id].bal -= amt;
spew_cash();
}
0: addi r1,accts,r3
1: ld 0(r3),r4
2: blt r4,r2,6
3: sub r4,r2,r4
4: st r4,0(r3)
5: call spew_cash
6: ... ... ...

## Slide 10: Shared-Memory Multiprocessors
P1
P2
P3
P4
Memory System
Shared memory
  Multiple execution contexts sharing a single address space
    Multiple programs (MIMD)
    Or more frequently: multiple copies of one program (SPMD)
  Implicit (automatic) communication via loads and stores
Notes: Familiar for system (OS and DB) as well as application programmers
  Why? The same techniques that use concurrency to overlap disk and network latencies also work for parallel speedup on MPs. The exact same software can take advantage of MPs with only small changes

## Slide 11: What’s the other option?
Basically the only other option is “message passing”
  We communicate via explicit messages.
  So instead of just changing a variable, we’d need to call a function to pass a specific message.
Message passing systems are easy to build and pretty efficient.
  But harder to code.
Shared memory programming is basically the same as multi-threaded programming on one processors
  And (many) programmers already know how to do that.

## Slide 12: So Why Shared Memory?
Pluses
  For applications looks like multitasking uniprocessor
  For OS only evolutionary extensions required
  Easy to do communication without OS being involved
  Software can worry about correctness first then performance
Minuses
  Proper synchronization is complex
  Communication is implicit so harder to optimize
  Hardware designers must implement
Result
  Traditionally bus-based Symmetric Multiprocessors (SMPs), and now the CMPs are the most success parallel machines ever
  And the first with multi-billion-dollar markets

## Slide 13: Shared-Memory Multiprocessors
P1
P2
P3
P4
There are lots of ways to connect processors together
Interconnection Network
Cache
M1
Interface
Cache
M2
Interface
Cache
M3
Interface
Cache
M4
Interface
Notes: Familiar for system (OS and DB) as well as application programmers
  Why? The same techniques that use concurrency to overlap disk and network latencies also work for parallel speedup on MPs. The exact same software can take advantage of MPs with only small changes

## Slide 14: Paired vs. Separate Processor/Memory?
Separate processor/memory
  Uniform memory access (UMA): equal latency to all memory
  Simple software, doesn’t matter where you put data
  Lower peak performance
  Bus-based UMAs common: symmetric multi-processors (SMP)
Paired processor/memory
  Non-uniform memory access (NUMA): faster to local memory
  More complex software: where you put data matters
  Higher peak performance: assuming proper data placement
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
R
R
R
R

## Slide 15: Shared vs. Point-to-Point Networks
Shared network: e.g., bus (left)
  Low latency
  Low bandwidth: doesn’t scale beyond ~16 processors
  Shared property simplifies cache coherence protocols (later)
Point-to-point network: e.g., mesh or ring (right)
  Longer latency: may need multiple “hops” to communicate
  Higher bandwidth: scales to 1000s of processors
  Cache coherence protocols are complex
CPU($)
Mem
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
R
R
R
R

## Slide 16: Organizing Point-To-Point Networks
Network topology: organization of network
  Tradeoff performance (connectivity, latency, bandwidth)  cost
Router chips
  Networks that require separate router chips are indirect
  Networks that use processor/memory/router packages are direct
    Fewer components, “Glueless MP”
Point-to-point network examples
  Indirect tree (left)
  Direct mesh or ring (right)
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
CPU($)
Mem
R
R
R
R
R
R
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R

## Slide 17: Implementation #1: Snooping Bus MP
Two basic implementations
Bus-based systems
  Typically small: 2–8 (maybe 16) processors
  Typically processors split from memories (UMA)
    Sometimes multiple processors on single chip (CMP)
    Symmetric multiprocessors (SMPs)
    Common, I use one everyday
CPU($)
CPU($)
Mem
CPU($)
Mem
CPU($)

## Slide 18: Implementation #2: Scalable MP
General point-to-point network-based systems
  Typically processor/memory/router blocks (NUMA)
    Glueless MP: no need for additional “glue” chips
  Can be arbitrarily large: 1000’s of processors
    Massively parallel processors (MPPs)
  In reality only government (DoD) has MPPs…
    Companies have much smaller systems: 32–64 processors
    Scalable multi-processors
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R
CPU($)
Mem
R

## Slide 19: Issues for Shared Memory Systems
Two in particular
  Cache coherence
  Memory consistency model
Closely related to each other

## Slide 20: An Example Execution
Two $100 withdrawals from account #241 at two ATMs
  Each transaction maps to thread on different processor
  Track accts[241].bal (address is in r3)
Processor 0
0: addi r1,accts,r3
1: ld 0(r3),r4
2: blt r4,r2,6
3: sub r4,r2,r4
4: st r4,0(r3)
5: call spew_cash
Processor 1
0: addi r1,accts,r3
1: ld 0(r3),r4
2: blt r4,r2,6
3: sub r4,r2,r4
4: st r4,0(r3)
5: call spew_cash
CPU0
Mem
CPU1

## Slide 21: No-Cache, No-Problem
Scenario I: processors have no caches
  No problem
Processor 0
0: addi r1,accts,r3
1: ld 0(r3),r4
2: blt r4,r2,6
3: sub r4,r2,r4
4: st r4,0(r3)
5: call spew_cash
Processor 1
0: addi r1,accts,r3
1: ld 0(r3),r4
2: blt r4,r2,6
3: sub r4,r2,r4
4: st r4,0(r3)
5: call spew_cash
500
500
400
400
300

## Slide 22: Cache Incoherence
Scenario II: processors have write-back caches
  Potentially 3 copies of accts[241].bal: memory, p0$, p1$
  Can get incoherent (inconsistent)
Processor 0
0: addi r1,accts,r3
1: ld 0(r3),r4
2: blt r4,r2,6
3: sub r4,r2,r4
4: st r4,0(r3)
5: call spew_cash
Processor 1
0: addi r1,accts,r3
1: ld 0(r3),r4
2: blt r4,r2,6
3: sub r4,r2,r4
4: st r4,0(r3)
5: call spew_cash
500
V:500
500
D:400
500
D:400
500
V:500
D:400
500
D:400

## Slide 23: Hardware Cache Coherence
Coherence controller:
  Examines bus traffic (addresses and data)
  Executes coherence protocol
    What to do with local copy when you see different things happening on bus
CPU
D$ data
D$ tags
CC
bus

## Slide 24: Snooping Cache-Coherence Protocols
Bus provides serialization point
Each cache controller “snoops” all bus transactions
  take action to ensure coherence
    invalidate
    update
    supply value
  depends on state of the block and the protocol
Notes: 7

## Slide 25: Snooping Design Choices
Processor
ld/st
Snoop (observed bus transaction)
State
Tag
Data
. . .
Controller updates state of blocks in response to processor and snoop events and generates bus xactions
Often have duplicate cache tags
Snoopy protocol
  set of states
  state-transition diagram
  actions
Basic Choices
  write-through vs. write-back
  invalidate vs. update
Cache
Notes: 8

## Slide 26: The Simple Invalidate Snooping Protocol
Write-through, no-write-allocate cache
Actions: PrRd, PrWr, BusRd, BusWr
PrWr / BusWr
Valid
BusWr
Invalid
PrWr / BusWr
PrRd / BusRd
PrRd / --
Notes: 9

## Slide 27: Example time
Processor 1 |  | Processor 2 |  | Bus
Processor Transaction | Cache State | Processor Transaction | Cache State | 
Read A |  |  |  | 
Read A |  |  |  | 
 |  | Read A |  | 
Write A |  |  |  | 
 |  | Read A |  | 
 |  | Write A |  | 
Write A |  |  |  | 
Actions:
PrRd, PrWr,
BusRd, BusWr

## Slide 28: More Generally: MOESI
[Sweazey & Smith ISCA86]
M - Modified (dirty)
O - Owned (dirty but shared) WHY?
E - Exclusive (clean unshared) only copy, not dirty
S - Shared
I - Invalid
Variants
  MSI
  MESI
  MOSI
  MOESI
O
M
E
S
I
ownership
validity
exclusiveness

## Slide 29: MESI example
M - Modified (dirty)
E - Exclusive (clean unshared) only copy, not dirty
S - Shared
I - Invalid
Processor 1 |  | Processor 2 |  | Bus
Processor Transaction | Cache State | Processor Transaction | Cache State | 
Read A |  |  |  | 
Read A |  |  |  | 
 |  | Read A |  | 
Write A |  |  |  | 
 |  | Read A |  | 
 |  | Write A |  | 
Write A |  |  |  | 
Actions:
PrRd, PrWr,
BRL – Bus Read Line (BusRd)
BWL – Bus Write Line (BusWr)
BRIL – Bus Read and Invalidate
BIL – Bus Invalidate Line