## Slide 1: Instruction Set Architectures: History and Issues
Many slides taken from Dr. Srinivasan Parthasarathy. Some figures from our text.
Any errors are my own…

## Slide 2: Schedule of things to do
HW5 posted.
  Due on 4/23 (last day of class) @10pm – 24 hours late with only 5% off.
MS3 meeting out later today.
Project is due on Saturday 4/20 at 9pm.
  Last synth job can still be running, but don’t rely on it.
  No code changes after this.
Oral and written reports are due on Tuesday 4/23.
  Brief directions for both posted shortly.
  Final written report is due at 9pm on Piazza
  Oral reports are during the day.
  Will watch at least 2 other talks.
    Can go to all if you wish.

## Slide 3: Computer Architecture’s Changing Definition
1950s to 1960s:
  Computer Architecture Course =
    Computer Arithmetic
1970s to 1980s:
  Computer Architecture Course =
    Instruction Set Design (especially ISA appropriate for compilers)
1990s+
  Computer Architecture Course =
    Design of CPU (microarchitecture)
    Design of memory system & I/O system
    Multiprocessor/multi-thread issues
Intro

## Slide 4: Instruction Set Architecture: The interface between hardware and software
Instruction set architecture is the structure of a computer that a machine language programmer must understand to write a correct (timing independent) program for that machine.
The instruction set architecture is also the machine description that a hardware designer must understand to design a correct implementation of the computer.
Software
Hardware
Intro

## Slide 5: Interface Design
A good interface:
  Lasts through many implementations (portability, compatibility)
  Is used in many different ways (generality)
  Provides convenient functionality to higher levels
  Permits an efficient implementation at lower levels
Interface
imp 1
imp 2
imp 3
use
use
use
time
Intro

## Slide 6: Today’s outline
History of ISA design
Overview of ISA options
  Classification into 0,1,2,3 address machines
  Addressing modes
  Other issues
Sum-up.
Intro

## Slide 7: Evolution of Instruction Sets
Single Accumulator (EDSAC 1950)
Accumulator + Index Registers
(Manchester Mark I, IBM 700 series 1953)
Separation of Programming Model
from Implementation
High-level Language Based
Concept of a Family
(B5000 1963)
(IBM 360 1964)
General Purpose Register Machines
Complex Instruction Sets
Load/Store Architecture
RISC
(VAX, Intel 432 1977-80)
(CDC 6600, Cray 1 1963-76)
(Mips,Sparc,HP-PA,IBM RS6000,PowerPC . . .1987)
“EPIC”?
(IA-64. . .1999)
History

## Slide 8: Evolution of Instruction Sets
Major advances in computer architecture are typically associated with landmark instruction set designs
Design decisions must take into account:
  technology
  machine organization
  programming languages
  compiler technology
  operating systems
And they in turn influence these
History

## Slide 9: Today’s outline
History of ISA design
Overview of ISA options
  Classification into 0,1,2,3 address machines
  Addressing modes
  Other issues
Sum-up.

## Slide 10: What Are the Components of an ISA?
Sometimes known as The Programmer’s Model of the machine
Storage cells
  General and special purpose registers in the CPU
  Many general-purpose cells of same size in memory
  Storage associated with I/O devices
The machine instruction set
  The instruction set is the entire repertoire of machine operations
  Makes use of storage cells, formats, and results of the fetch/execute cycle
    e.g.., register transfers
Overview

## Slide 11: What Must an Instruction Specify?(I)
Which operation to perform add r0, r1, r3
  Ans: Op code: add, load, branch, etc.
Where to find the operands: add r0, r1, r3
  In CPU registers, memory cells, I/O locations, or part of instruction
Place to store result add r0, r1, r3
  Again CPU register or memory cell
Data Flow
Overview

## Slide 12: What Must an Instruction Specify?(II)
Location of next instruction add r0, r1, r3 br endloop
  Almost always memory cell pointed to by program counter—PC
Sometimes there is no operand, or no result, or no next instruction.
  Can you think of examples?
Overview

## Slide 13: Instructions Can Be Divided into 3 Classes (I)
Data movement instructions
  Move data from a memory location or register to another memory location or register without changing its form
  Load—source is memory and destination is register
  Store—source is register and destination is memory
Arithmetic and logic (ALU) instructions
  Change the form of one or more operands to produce a result stored in another location
  Add, Sub, Shift, etc.
Branch instructions (control flow instructions)
  Alter the normal flow of control from executing the next instruction in sequence
  Br Loc, Brz Loc2,—unconditional or conditional branches
Overview

## Slide 14: Classifying ISAs
Accumulator (before 1960):
1 address add A acc <- acc + mem[A]
Stack (1960s to 1970s):
0 address add tos <- tos + next
Memory-Memory (1970s to 1980s):
2 address add A, B mem[A] <- mem[A] + mem[B]
3 address add A, B, C mem[A] <- mem[B] + mem[C]
Register-Memory (1970s to present):
2 address add R1, A R1 <- R1 + mem[A]
load R1, A R1 <_ mem[A]
Register-Register (Load/Store) (1960s to present):
3 address add R1, R2, R3 R1 <- R2 + R3
load R1, R2 R1 <- mem[R2]
store R1, R2 mem[R1] <- R2
Overview: Classification

## Slide 15: Classifying ISAs
Overview: Classification

## Slide 16: Stack Architectures
Instruction set:
  add, sub, mult, div, . . .
  push A, pop A
Example: A*B - (A+C*B)
  push A
  push B
  mul
  push A
  push C
  push B
  mul
  add
  sub
A
B
A
A*B
A*B
A*B
A*B
A
A
C
A*B
A
A*B
A
C
B
B*C
A+B*C
result
Overview: Classification

## Slide 17: Stacks: Pros and Cons
Pros
  Good code density (implicit operand addressing top of stack)
  Low hardware requirements
  Easy to write a simpler compiler for stack architectures
Cons
  Stack becomes the bottleneck
  Little ability for parallelism or pipelining
  Data is not always at the top of stack when need, so additional instructions like SWAP are needed
  Difficult to write an optimizing compiler for stack architectures
  How about an OoO machine?
Overview: Classification

## Slide 18
Accumulator Architectures
Instruction set:
  add A, sub A, mult A, div A, . . .
  load A, store A
Example: A*B - (A+C*B)
  load B
  mul C
  add A
  store D
  load A
  mul B
  sub D
B
B*C
A+B*C
A
A+B*C
A*B
result
Overview: Classification

## Slide 19
Accumulators: Pros and Cons
Pros
  Very low hardware requirements
  Easy to design and understand
Cons
  Accumulator becomes the bottleneck
  Little ability for parallelism or pipelining
  High memory traffic
  How about an OoO machine?
Overview: Classification

## Slide 20
Memory-Memory Architectures
Instruction set:
  (3 operands) add A, B, C sub A, B, C mul A, B, C
Example: A*B - (A+C*B)
  3 operands
    mul D, A, B
    mul E, C, B
    add E, A, E
    sub E, D, E
Overview: Classification

## Slide 21
Memory-Memory: Pros and Cons
Pros
  Requires fewer instructions (especially if 3 operands)
  Easy to write compilers for (especially if 3 operands)
Cons
  Very high memory traffic (especially if 3 operands)
  Variable number of clocks per instruction (especially if 2 operands)
  With two operands, more data movements are required
  How about an OoO machine?
Overview: Classification

## Slide 22
Register-Memory Architectures
Instruction set:
  add R1, A sub R1, A mul R1, B
  load R1, A store R1, A
Example: A*B - (A+C*B)
  load R1, A
  mul R1, B /* A*B */
  store R1, D
  load R2, C
  mul R2, B /* C*B */
  add R2, A /* A + CB */
  sub R2, D /* AB - (A + C*B) */
Overview: Classification

## Slide 23
Memory-Register: Pros and Cons
Pros
  Some data can be accessed without loading first
  Instruction format easy to encode
  Good code density
Cons
  Operands are not equivalent (poor orthogonality)
  Variable number of clocks per instruction
  May limit number of registers
Overview: Classification

## Slide 24
Load-Store Architectures
Instruction set:
  add R1, R2, R3 sub R1, R2, R3 mul R1, R2, R3
  load R1, R4 store R1, R4
Example: A*B - (A+C*B)
  load R4, &A
  load R5, &B
  load R6, &C
  mul R7, R6, R5 /* C*B */
  add R8, R7, R4 /* A + C*B */
  mul R9, R4, R5 /* A*B */
  sub R10, R9, R8 /* A*B - (A+C*B) */
Overview: Classification

## Slide 25
Load-Store: Pros and Cons
Pros
  Simple, fixed length instruction encoding
  Instructions take similar number of cycles
  Relatively easy to pipeline
Cons
  Higher instruction count
  Not all instructions need three operands
  Dependent on good compiler
    Need to schedule registers well at the least.
Overview: Classification

## Slide 26: Comparing Code Density
Stack
push A
push B
mul
push A
push C
push B
mul
add
sub
Accum.
load B
mul C
add A
store D
load A
mul B
sub D
Reg-Mem
load R1, A
mul R1, B
store R1, D
load R2, C
mul R2, B
add R2, A
sub R2, D
Load/Store
load R4, &A
load R5, &B
load R6, &C
mul R7, R6, R5
add R8, R7, R4
mul R9, R4, R5
sub R10, R9, R8
If we need 5 bits to specify a register, 16 bits to specify a memory location and 8 bits to specify the opcode,
how many bits do we use for each scheme?
Overview: Classification

## Slide 27: Types of Addressing Modes (VAX)
1. Register direct Ri
2. Immediate (literal) #n
3. Displacement M[Ri + #n]
4. Register indirect M[Ri]
5. Indexed M[Ri + Rj]
6. Direct (absolute) M[#n]
7. Memory Indirect M[M[Ri] ]
8. Autoincrement M[Ri++]
9. Autodecrement M[Ri - -]
10. Scaled M[Ri + Rj*d + #n]
memory
reg. file
Overview: Addressing modes

## Slide 28: Summary of Use of Addressing Modes
Overview: Addressing modes

## Slide 29: Distribution of Displacement Values
Overview: Addressing modes

## Slide 30: Branch Distances (in terms of number of instructions)
Overview: Other issues

## Slide 31
Registers vs. Memory
Advantages of Registers
  Faster than cache (no addressing mode or tags)
  Deterministic (no misses)
  Can replicate (multiple read ports)
  Short identifier (typically 3 to 8 bits)
  Reduce memory traffic
Disadvantages of Registers
  Need to save and restore on procedure calls and context switch
  Can’t take the address of a register (for pointers)
  Fixed size (can’t store strings or structures efficiently)
  Generally limited in number
Overview: Other issues

## Slide 32
How about something other than registers and memory?
We have two namespaces.
  Why not 3?
What other name spaces might make sense?
Overview: Other issues

## Slide 33
Alignment Issues
If the architecture does not restrict memory accesses to be aligned then
  Software is simple
  Hardware must detect misalignment and make 2+ memory accesses
  Expensive detection logic is required
  All references can be made slower
Sometimes unrestricted alignment is required for backwards compatibility
If the architecture restricts memory accesses to be aligned then
  Software must guarantee alignment
  Hardware detects misalignment access and traps
  No extra time is spent when data is aligned
Since we want to make the common case fast, having restricted alignment is often a better choice, unless compatibility is an issue
Overview: Other issues

## Slide 34: Frequency of Immediate Operands
Overview: Other issues

## Slide 35: 80x86 Instruction Frequency (SPECint92, Fig. 2.16)
Overview: Other issues

## Slide 36: Today’s outline
History of ISA design
Overview of ISA options
  Classification into 0,1,2,3 address machines
  Addressing modes
  Other issues
Sum-up.

## Slide 37: Encoding an Instruction Set
What are the metrics of goodness?
  TProgram is always the main measure.
  But what goes into that?
    Number of instructions
    Time it takes to execute each instruction
      Complexity of instruction
        Decode
        Execute
      Size if code total (yes, that double counts number of instructions to some extent)
      Impact on parallelization
Sum-up

## Slide 38: Encoding an Instruction Set
Some impacts are pretty obvious
  If you need fewer bits for a given program, you can expect a higher Icache hit rate.
  If instructions aren’t regular (which field selects the input registers, variable instruction word lenght) you can expect a longer decode time.
Some aren’t
  Discuss how the ISA might make a superscalar out-of-order processor difficult to build.
Sum-up
Notes: Some issues:
Variable word length makes superscalar fetch harder.
Additional dependencies can make out-of-order very difficult.
Stack creates a bottleneck that might hurt both SS and OoO (though you might be able to rename your way out of it?)

## Slide 39: Encoding an Instruction Set
Consider a load/store machine that uses immediates
  5 bits for registers, 16 bits for immediates.
    What percent of a 32-bit ISA encoding does a 3 register argument instruction use?
    An instruction using two registers and an immediate?
  What would be the downside to using a 12-bit immediate? The upside?
Sum-up

## Slide 40: Encoding an Instruction Set
A desire to have as many registers and addressing modes as possible
The impact of size of register and addressing mode fields on the average instruction size and hence on the average program size
A desire to have instruction encode into lengths that will be easy to handle in the implementation
Sum-up