## Slide 1: Finish Licensing & Embedded Linux Lectures 6 and 7

## Slide 2: NOTE:
Be sure to register your RPi.
  See Piazza post @59 (pinned)
  Basically, bring your Pi to lab this week and register it or follow directions for doing it from home.

## Slide 3: Copyright, Copyleft, and Legal Issues

## Slide 4: The basic copyright options
No license:
  Without a license, the code is copyrighted by default. People can read the code, but they have no legal right to use it. To use the code, you must contact the author directly and ask permission.
Public domain:
  If your code is in the public domain, anyone may use your code for any purpose whatsoever. Nothing is in the public domain by default; you have to explicitly put your work in the public domain if you want it there. Otherwise, you must be dead a long time before your work reverts to the public domain.
Text from https://blog.codinghorror.com/pick-a-license-any-license/, also includes a (too) terse summary of the common software licenses.

## Slide 5: Linux (common usage of the word)
A POSIX-compliant and widely deployed desktop/server operating system licensed under the GPL
  POSIX
    Unix-like environment (shell, standard programs like awk etc.)
  Desktop OS
    Designed for users and servers
    Not designed for embedded systems
  GPL
    GNU Public License. May mean you need to make source code available to others.
      First “copyleft” license.
    Linux is licensed under GPL-2, not GPL-3.

## Slide 6: GPL in three slides (1/3)
A licensee of GPL v2-licensed software can:
  copy and distribute the program's unmodified source code
  modify the program's source code and distribute the modified source
  distribute compiled versions of the program, both modified and unmodified
Provided that:
  all distributed copies (modified or not) carry a copyright notice and exclusion of warranty
  all modified copies are distributed under the GPL v2
  all compiled versions of the program are accompanied by the relevant source code, or a viable offer to make the relevant source code available
Background: legal issues
Largely taken from http://www.oss-watch.ac.uk/resources/gpl.xml

## Slide 7: GPL in three slides (2/3)
Some points
  If you don’t redistribute the code, you don’t need to share the source.
  You can bundle software with GPL-ed software and not have to license the bundled software.
    “Mere aggregations” aren’t impacted.
  Loadable Kernel Modules are tricky though
    Often we need device drivers for our application (we’ll be writing them later)
    But they touch the Linux code in a non-trivial way.
      There is some debate about if a LKM is an aggregation or a modification of the original kernel.
      In general there are proprietary drivers out there and even open source groups that help support said drivers.
General theme:
  Be sure you understand the law before you use software licensed under the GPL on a proprietary project.
    Using gcc to compile or ddd to debug is fine, but when you are modifying the code of software licensed under the GPL you might be obligated to release your code.
Read (or at least scan): The Cathedral and the Bazaar before the midterm.
Background: legal issues

## Slide 8: GPL in three slides (3/3)
GPL v3
  Prevents using GPL on hardware that won’t run other code (“Tivoization”)
    Though only for consumer hardware (IBM has a business model here?)
  Addresses patents
    Can’t sue for (software?) patent on code you release.
Lesser GPL
  Mainly for libraries/APIs.
  Makes it clear can use libraries in proprietary code without having to release proprietary code.
Background: legal issues

## Slide 9: OK, one more
gcc is GPL v3
  But has a runtime exception.
  When you use GCC to compile a program, GCC may combine portions of certain GCC header files and runtime libraries with the compiled program. The purpose of this Exception is to allow compilation of non-GPL (including proprietary) programs to use, in this way, the header files and runtime libraries covered by this Exception.
Linux is GPL v2
  Fear of limiting DRM and private keys keeps them away from v3.
There is a short preamble:
  This copyright does *not* cover user programs that use kernel services by normal system calls - this is merely considered normal use of the kernel, and does *not* fall under the heading of "derived work".

## Slide 10: Another common License: Creative Commons
These are basically a free configurable license.
  Attribution (by)
    Must give author credit
  ShareAlike (sa)
    Like GPL, they must distribute any changes.
  NonCommercial (nc)
    Only for non-commercial
  NoDerivatives (nd)
    Can’t make changes.
Idea is, someone smart wrote the words to do what you probably want to do.
  You still hold ownership, so if they want a different license, they can come to you to negotiate.
Wikipedia is CC BY-SA
Creative Commons is generally a poor license for code but still used for that. See https://creativecommons.org/faq/
But quite useful for documentation and databases

## Slide 11: MIT license
Permission is hereby granted, free of charge, to any person obtaining a copy of this software and associated documentation files (the "Software"), to deal in the Software without restriction, including without limitation the rights to use, copy, modify, merge, publish, distribute, sublicense, and/or sell copies of the Software, and to permit persons to whom the Software is furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all copies or substantial portions of the Software.
(And then a disclaimer of liability)
Basically, just grants permission.
  Can add to a closed-source product, etc.
  More-or-less public domain with the disclaimer of liability being required in any place the code is used.

## Slide 12: Fair use
Fair use lets you use copyrighted works
  But in general there are guidelines for what you can use.
Four factors are:
  the purpose and character of your use
    Transformative or not (parody falls here).
  the nature of the copyrighted work
    Published/not published, factual works.
  the amount and substantiality of the portion taken
    The amount taken and the % taken both play a role.
  the effect of the use upon the potential market
    If you reduce the market for the original work, that’s a problem.
Fair use in code is tricky at best.
  APIs sometimes fit here (see Oracle America vs. Google Inc.)
http://fairuse.stanford.edu/overview/fair-use/four-factors/

## Slide 13: Start on Linux
Many figures and text in this section taken from Embedded Linux Primer, second edition
We (kind of) have on-line access to the book. Also http://freesoftwaremagazine.com/articles/drivers_linux/ is used a lot!

## Slide 14: Two main tasks
Introduce Linux and in particular embedded Linux.
  Pretty high-level.
  Lots of material coming pretty quickly.
How to write device drivers for Linux.
  Much more detailed
  Pretty complex coding
  Will do in lab 4.

## Slide 15: Linux Introduction
Background
  Kernel overview, legal issues, versioning, building, user basics, FHS, booting
Embedded Linux (common but not required attributes)
  Small footprint (BusyBox)
  Flash file system
  Real time support
Warning: We are going to do this section very quickly indeed. There is a lot of stuff I want you to see. There is enough stuff in this section of this lecture for 20 hours of discussion. We don’t have that kind of time. Just going to lightly touch on some stuff.

## Slide 16: Linux
The software commonly referred to as “Linux” is really a number of things glued together
  The Linux Kernel
  GNU tools (bash, ls, emacs, etc.)
  Usually also
    A package manager (dpkg, RPM, etc.)
    A desktop environment (GNOME, KDE, etc.)
Linux distributions (“distros”)
  Collections of the above tools (Debian, Red Hat, etc.)
  These distros are often labeled as a “Linux-based OS”
The Kernel isn’t an OS by itself
  The distros are
https://itsfoss.com/what-is-linux-distribution/

## Slide 17: What is a kernel? (1/2)
The kernel’s job is to talk to the hardware and software, and to manage the system’s resources as best as possible.
  It talks to the hardware via the drivers that are included in the kernel (or additionally installed later on in the form of a “kernel module”).
    This way, when an application wants to do something (say change the volume setting of the speakers), it can just submit that request to the kernel, and the kernel can use the driver it has for the speakers to actually change the volume.
http://www.makeuseof.com/tag/linux-kernel-explanation-laymans-terms/
Background: kernel

## Slide 18: What is a kernel? (2/2)
The kernel is highly involved in resource management.
  It has to make sure that there is enough memory available for an application to run, as well as to place an application in the right location in memory.
  It tries to optimize the usage of the processor so that it can complete tasks as quickly as possible.
    It also aims to avoid deadlocks.
  It’s a fairly complicated circus act to coordinate all of those things, but it needs to be done and that’s what the kernel is for.
Background: kernel

## Slide 19
Background: kernel
Background: kernel

## Slide 20: Linux kernel history
3.0 isn’t a radical change from 2.6, instead a 2.6 upgrade was move to 3.0 for Linux’s 20th anniversary.
  “So what are the big changes? NOTHING. Absolutely nothing. Sure, we have the usual two thirds driver changes, and a lot of random fixes, but the point is that 3.0 is *just* about renumbering…” [https://lkml.org/lkml/2011/5/29/204]
  And 4.0 is more of the same.
  http://www.itworld.com/article/2887558/linus-torvalds-bumps-linux-kernel-to-version-4x.html
Figure from “Linux kernel version history” article on Wikipedia.
Background: Linux kernel versions
I’d like to point out (yet again) that we don’t do feature-based releases, and that “5.0” doesn’t mean anything more than that the 4.x numbers started getting big enough that I ran out of fingers and toes.
Linus Torvalds

## Slide 21: What version am I working with?
If running, use “uname” command
  “uname -a” for all information
If looking at source
  First few lines of the top-level Makefile will tell you.
Background: versions

## Slide 22: How do I download and build the kernel?
Use git.
Typing “make” with no target at the top-level should build the kernel.
  Need gcc installed (no other compiler will do).
  Should generate an ELF file called “vmlinux”
    But lots of configuration stuff
Background: building

## Slide 23: Kernel configuration
There is a file, “.config” which drives the build.
  It determines the functionality (including cross-compling?) of the kernel.
    Things like USB support, etc.
  It is setup in any number of ways.
    The default is to ask a huge number of questions.
    There are editors and defaults you can use instead.
      make defconfig should just do all defaults for example.
    make help should give a solid overview of options
The .config file scheme has some problems.
  It is easy to miss, as files that start with a “.” (dot) are hidden files in Linux ("ls -a" will show them)
  It is easy to blow away.
    make distclean will delete it for example…
Background: building

## Slide 24: Linux user basics--shell
You have a shell which handles user commands
  May just search for an executable file (application) in certain locations
  Allows for moving data between those applications.
    Pipes etc.
  Is itself a programming language.
  There are many of these (bash, sh, tcsh, csh, ksh, zsh)
    Most have very similar interfaces (type application name, it runs), but the programming language part varies quite a bit.
    Geek humor:
      sh is called the Bourne shell, written by Stephen Bourne
      bash, often treated as an upgrade to sh, is the “Bourne again shell”
Background: user basics

## Slide 25: Linux user basics—file systems
Linux supports a huge variety of file systems.
  But they have some commonalities.
Pretty much a standard directory structure with each directory holding either other directories or files.
  Each file and directory has a set of permissions.
    One owner (a single user)
    One group (a list of users who may have special access)
    There are three permissions, read, write and execute
      Specified for owner, group, and world.
There are also links (hard and soft)
  So rather than copying files I can point to them.
Background: user basics

## Slide 26: FHS: File System Hierarchy Standard
There is a standard for laying out file systems
  Part of this is the standard top-level directories
Background: FHS

## Slide 27: A “minimal” file system
Busybox is covered later
Background: FHS

## Slide 28: Background: booting
Some circuit magic happens
  Get clock running, reset registers etc.
Bootloader starts
  Initialize devices such as I2C, serial, DRAM, cache, etc.
  Starts the OS
Kernel starts
  Might set up other things needed
Init gets called
  Lots of stuff…
Background: booting
Note: there are some hidden slides that cover a bit more on this in the posted pptx.

## Slide 29
Background: booting
Notes: uboot (Das U-boot) is common embedded bootloader. GRUB for mainstream Linux is most common.

## Slide 30: Handoff from the Kernel
Kernel tries to start init.
  Tries a few locations
    Doesn’t return if successful, so first that succeeds is all that runs.
Background: booting

## Slide 31: The init process
Init is the ultimate parent of all user-space processes.
  Provides all default environment variables including PATH
Init uses a text file, /etc/inittab.
  That file includes a number of “run levels” that are used to determine what init should do.
    Halt, reboot, general-purpose multi-user, etc.
Background: booting

## Slide 32: Init (continued)
init.d holds the scripts for each service.
rcN.d holds symlinks to start or kill each process
associated with that runlevel.
Background: booting

## Slide 33: Outline
Background
  Legal issues, versioning, building, user basics, FHS, booting
Embedded Linux (common but not required attributes)
  Small footprint (BusyBox)
  Flash file system
  Real time support

## Slide 34: What makes a Linux install “embedded”?
It’s one of those poorly defined terms, but in general it will have one or more of the following
  small footprint
  flash files system
  real-time extensions of some sort
Embedded Linux

## Slide 35: Small footprint--Busybox
A single executable that implements the functionality of a massive number of standard Linux utilities
  ls, gzip, ln, vi. Pretty much everything you normally need.
    Some have limited features
      Gzip only does the basics for example.
  Pick which utilities you want it to do
    Can either drop support altogether or install real version if needed
  Highly configurable (similar to Linux itself), easy to cross-compile.
Example given is around 2MB statically compiled!
  addgroup, adduser, ar, ash, awk, basename, blkid, bunzip2, bzcat, cat, chattr, chgrp, chmod, chown, chpasswd, chroot, chvt, clear, cmp, cp, cpio, cryptpw, cut, date, dc, dd, deallocvt, delgroup, deluser, df, dhcprelay, diff, dirname, dmesg, du, dumpkmap, dumpleases, echo, egrep, env, expr, false, fbset, fbsplash, fdisk, fgrep, find, free, freeramdisk, fsck, fsck.minix, fuser, getopt, getty, grep, gunzip, gzip, halt, head, hexdump, hostname, ttpd, hwclock, id, ifconfig, ifdown, ifup, init, insmod, ip, kill, killall, klogd, last, less, linuxrc, ln, loadfont, loadkmap, logger, login, logname, logread, osetup, ls, lsmod, makedevs, md5sum, mdev, microcom, mkdir, mkfifo, mkfs.minix, mknod, mkswap, mktemp, modprobe, more, mount, mv, nc, netstat, nice, nohup, nslookup, od, penvt, passwd, patch, pidof, ping, ping6, pivot_root, poweroff, printf, ps, pwd, rdate, rdev, readahead, readlink, eadprofile, realpath, reboot, renice, reset, rm, rmdir, rmmod, route, rtcwake, run-parts, sed, seq, setconsole, etfont,sh, showkey, sleep, sort, start-stop-daemon, strings, stty, su, sulogin, swapoff, swapon, switch_root, sync, sysctl, syslogd, tail, tar, tee, telnet, telnetd, test, tftp, time, top, touch, tr, traceroute, true, tty, udhcpc, udhcpd, umount, uname, uniq, unzip, uptime, usleep, vi, vlock, watch, wc, wget, which, who, whoami, xargs, yes, zcat
Embedded Linux—small footprint

## Slide 36: Using busybox
Two ways to play
  Invoke from the command line as busybox
    busybox ls /
  Or create a softlink to busybox and it will run as the name of that link.
    So if you have a softlink to busybox named “ls” it will run as ls.
Embedded Linux—small footprint

## Slide 37: Links done for you
Normally speaking, you’ll use the softlink option.
  You can get it to put in all the links for you with “make install”
    Be darn careful you don’t overwrite things locally if you are doing this on the host machine.
      That would be bad.
Embedded Linux—small footprint

## Slide 38: System initialization
Busybot can also be “init”
  But it’s a simpler/different version than the init material covered above.
  More “bash” like
#!/bin/sh
echo “Mounting proc”
mount -t proc /proc /proc
echo “Starting system loggers”
syslogd
klogd
echo “Configuring loopback interface”
ifconfig lo 127.0.0.1
echo “Starting inetd”
xinetd
# start a shell
busybox sh
Embedded Linux—small footprint

## Slide 39: BusyBox Summary
BusyBox is a powerful tool for embedded systems that replaces many common Linux utilities in a single multicall binary.
BusyBox can significantly reduce the size of your root file system image.
Configuring BusyBox is straightforward, using an interface similar to that used for Linux configuration.
System initialization is possible but somewhat different with BusyBox
From Embedded Linux Primer, second edition
Embedded Linux—small footprint

## Slide 40: Outline
Background
  Legal issues, versioning, building, user basics, FHS, booting
Embedded Linux (common but not required attributes)
  Small footprint (BusyBox)
  Flash file system
  Real time support

## Slide 41: Flash storage devices
Significant restrictions on writing
  data can be changed from a 1 to a 0 with writes to the cell’s address
  0 to 1 requires an entire block be erased.
Therefore, to modify data stored in a Flash memory, the block in which the modiﬁed data resides must be completely erased.
  Write times for updating data in Flash memory can be many times that of a hard drive.
Also very limited write cycles (100 to 1,000,000 or so) before wear out.
  Wear leveling, conservative specifications generally make things okay.
Embedded Linux—flash filesystem

## Slide 42: Outline
Background
  Legal issues, versioning, building, user basics, FHS, booting
Embedded Linux (common but not required attributes)
  Small footprint (BusyBox)
  Flash file system
  Real time support
    RT Linux patch
    Other solutions

## Slide 43: Real-time Kernel Patch
The patch had many contributors, and it is currently maintained by Ingo Molnar; you can find it at:
  www.kernel.org/pub/linux/kernel/projects/rt/
  https://ubuntu.com/blog/real-time-kernel-technical
  Since about Linux 2.6.12, soft real-time performance in the single-digit milliseconds on a reasonably fast x86 processor is readily achieved
  Some claim “nearly-worst-case” latency of 30us!
Embedded Linux—real time?

## Slide 44: Features
The real-time patch adds a fourth preemption mode called PREEMPT_RT, or Preempt Real Time.
  Features from the real-time patch are added, including replacing spinlocks with preemptable mutexes.
    This enables involuntary preemption everywhere within the kernel except for areas protected by preempt_disable().
    This mode significantly smoothes out the variation in latency (jitter) and allows a low and predictable latency for time-critical real-time applications.
  The problem is…
    Not all devices can handle being interrupted.
    This means that with the RT patch in play you might get random crashes.
Embedded Linux—real time?

## Slide 45: There are lots of other attempts and discussions about a real-time Linux
RTLinux
  Wind River had something up and running for years.
    Ended support in 2011.
    Seems fairly restrictive.
Real Time Linux Foundation, Inc.
  Holding workshops on this for 13 years.
http://lwn.net/Articles/397422/
  Nice overview of some of the issues
Zephyr is an RTOS that is developed as part of the Linux Foundation.
  Looks like a traditional RTOS.
  Much more stuff (closer to a traditional OS)
Embedded Linux—real time?

## Slide 46: Windows for IoT
A stripped down version of Windows with a focus on IoT issues.
  Appears to be fairly popular.
  Latest version appears to require 4 GB of RAM and 64 GB of storage.
    Stripped-down version may get to 256MB RAM? It’s a bit unclear what you can really get to, but 4 GB is the official number.
Multiple versions all supported by Visual Studio.
  Reasonable choice for things that are plugged in.
  Remember, the best engineering solution isn’t always the best solution
    What I mean is that the “best” solutions require a lot of engineering time and therefore $$$$.
    Might be best to use this (programmers familiar with the environment, lots of stuff done for you) to reduce total cost even if the parts are more expensive.

## Slide 47: EECS 473 Advanced Embedded Systems
Linux device drivers and
loadable kernel modules

## Slide 48: Linux Device Drivers
Overview
  What is a device driver?
    Linux devices
  User space vs. Kernel space
Modules and talking to the kernel
  Background
  Example
  Some thinky stuff
A fair bit of this presentation, including some figures, comes from
http://www.freesoftwaremagazine.com/articles/drivers_linux#
Other sources noted at the end of the presentation.

## Slide 49: Linux Device Drivers
Overview
  What is a device driver?
    Linux devices
  User space vs. Kernel space
Modules and talking to the kernel
  Background
  Example
  Some thinky stuff

## Slide 50: Device driver (Thanks Wikipedia!)
A device driver is a computer program allowing higher-level computer programs to interact with a hardware device.
  A driver typically communicates with the device through the computer bus or communications subsystem to which the hardware connects.
  When a calling program invokes a routine in the driver, the driver issues commands to the device.
  Drivers are hardware-dependent and operating-system-specific.
Overview

## Slide 51: Devices in Linux (1/2)
There are special files called “device files” in Linux.
  A user can interact with it much like a normal file.
  But they generally provide access to a physical device.
  They are generally found in /dev and /sys
    /dev/fb is the frame buffer
    /dev/ttyS0 is one of the serial ports
Not all devices files correspond to physical devices.
  Pseudo-devices.
    Provide various functions to the programmer
    /dev/null
      Accepts and discards all input; produces no output.
    /dev/zero
      Produces a continuous stream of NULL (zero value) bytes.
    etc.
crw-rw---- 1 root dialout 4, 64 Jun 20 13:01 ttyS0
Overview

## Slide 52: Devices in Linux (2/2)
Pretty clearly you need a way to connect the device file to the actual device
  Or pseudo device for that matter
We want to be able to “fake” this by writing functions that handle the file I/O.
  So we need to associate functions with all the things we can do with a file.
    Open, close.
    Read, write.
Today we’ll talk about all that…
Overview

## Slide 53: Kernel vs. User space
User Space
  End-user programs. They use the kernel to interface to the hardware.
Kernel Space
  Provides a standard (and hopefully multi-user secure) method of using and sharing the hardware.
    Private function member might be a good analogy.
  A lot of things are different here.
    Many calls to the kernel can’t be made from the kernel.
      E.g. malloc.
Overview

## Slide 54: Linux Device Drivers…
Overview
  What is a device driver?
    Linux devices
  User space vs. Kernel space
Modules and talking to the kernel
  Background
  Example
  Some thinky stuff

## Slide 55: Kernel and Kernel Modules
Often, if you want to add something to the kernel you need to rebuild the kernel and reboot.
  A “loadable kernel module” (LKM) is an object file that extends the base kernel.
  Exist in most OSes
    Including Windows, FreeBSD, Mac OS X, etc.
  Modules get added and removed as needed
    To save memory, add functionality, etc.
Modules

## Slide 56: Linux Kernel Modules
In general must be licensed under a free license.
  Doing otherwise will taint the whole kernel.
    A tainted kernel sees little support.
    Might be a copyright problem if you redistribute.
The Linux kernel changes pretty rapidly, including APIs etc.
  This can make it a real chore to keep LKMs up to date.
  Also makes a tutorial a bit of a pain.
    Though honestly it seems fairly stable over the last 5 years.
Modules

## Slide 57: Creating a module
All modules need to define functions that are to be run when:
  The module is loaded into the kernel
  The module is removed from the kernel
We just write C code (see next slide)
We need to compile it as a kernel module.
  We invoke the kernel’s makefile.
  sudo make –C /lib/modules/xxx/build M=$PWD modules
    This makes (as root) using the makefile in the path specified.
    I think it makes all C files in the directory you started in
    Creates .ko (rather than .o) file
    Xxx is some kernel version/directory
Modules

## Slide 58: Simple module
#include <linux/init.h>
#include <linux/module.h>
#include <linux/kernel.h>
MODULE_LICENSE("Dual BSD/GPL");
static int hello_init(void) {
printk("<1> Hello World!\n");
return 0;
}
static void hello_exit(void) {
printk("<1> Bye world!\n");
}
module_init(hello_init);
module_exit(hello_exit);
MODULE_LICENSE
  Required.
  Short list of allowed licenses.
Printk()
  Kernel print.
    Prints message to console and to log.
    <1> indicates high priority message, so it gets logged.
Module_init()
  Tells system what module to call when we first load the module.
Module_exit()
  Same but called when module released.
Modules
Notes: There's more than one way to do it

## Slide 59: Modules: Listing, loading and removing
From the command line:
  lsmod
    List modules.
  insmod
    Insert module into kernel
      Adds to list of available modules
    Causes function specified by module_init() to be called.
  rmmod
    Removes module from kernel
Modules

## Slide 60: lsmod
Module Size Used by memory 10888 0 hello 9600 0 binfmt_misc 18572 1 bridge 63776 0 stp 11140 1 bridge bnep 22912 2 video 29844 0
Modules

## Slide 61: insmod
Very (very) simple
  insmod xxxxx.ko
    Says to insert the module into the kernel
Modules

## Slide 62: Other (better) way to load a module
Modprobe is a smarter version of insmod.
  Actually it’s a smarter version of insmod, lsmod and rmmod…
    It can use short names/aliases for modules
    It will first install any dependent modules
We’ll use insmod for the most part
  But be aware of modprobe
Modules

## Slide 63: So?
When insmod, log file gets a “Hello World!”
When rmmod, that message prints to log (and console…)
It’s not the name, it’s the module_init().
#include <linux/init.h>
#include <linux/module.h>
#include <linux/kernel.h>
MODULE_LICENSE("Dual BSD/GPL");
static int hello_init(void) {
printk("<1> Hello World!\n");
return 0;
}
static void hello_exit(void) {
printk("<1> Bye world!\n");
}
module_init(hello_init);
module_exit(hello_exit);
Modules

## Slide 64: Modules?
There are a number of different reasons one might have a module
  But the main one is to create a device driver
  It’s not realistic for Linux to have a device driver for all possible hardware in memory all at once.
    Would be too much code, requiring too much memory.
  So we have devices as modules
    Loaded as needed.
Modules

## Slide 65: What is a “device”?
As mentioned in the overview, Linux devices are accessed from user space in exactly the same way files are accessed.
  They are generally found in /dev and /sys
To link normal files with a kernel module, each device has a “major number”
  Each device also has a “minor number” which can be used by the device to distinguish what job it is doing.
% ls -l /dev/fd0 /dev/fd0u1680
brwxrwxrwx 1 root floppy 2, 0 Jul 5 2000 /dev/fd0
brw-rw---- 1 root floppy 2, 44 Jul 5 2000 /dev/fd0u1680
Two floppy devices. They are actually both the same bit of hardware using the same driver
(major number is 2), but one is 1.68MB the other 1.44.
Modules: device review

## Slide 66: Creating a device
mknod /dev/memory c 60 0
  Creates a character device named /dev/memory
  Major number 60
  Minor number 0
Minor numbers are passed to the driver to distinguish different hardware with the same driver.
  Or, potentially, the same hardware with different parameters (as the floppy example)
Modules: devices

## Slide 67: Linux Device Drivers
Overview
  What is a device driver?
    Linux devices
  User space vs. Kernel space
Modules and talking to the kernel
  Background
  Example
  Some thinky stuff

## Slide 68: A complete pseudo-device
We are going to create a pseudo-device that is just a single byte of memory.
  Whatever the last thing you wrote to it, is what will be read.
For example
  echo -n abcdef >/dev/memory
  Followed by cat /dev/memory
    Prints an “f”.
Silly, but not unreasonable.
  It’s also printing some stuff to the log.
    Not a great idea in a real device, but handy here.
Almost entirely from http://www.freesoftwaremagazine.com/articles/drivers_linux#
Modules: single character memory example

## Slide 69: includes
/* Necessary includes for device drivers */ #include <linux/init.h> #include <linux/module.h> #include <linux/kernel.h> /* printk() */ #include <linux/slab.h> /* kmalloc() */ #include <linux/fs.h> /* everything... */ #include <linux/errno.h> /* error codes */ #include <linux/types.h> /* size_t */ #include <linux/proc_fs.h> #include <linux/fcntl.h> /* O_ACCMODE */ #include <asm/system.h> /* cli(), *_flags */ #include <asm/uaccess.h> /* copy_from/to_user */
Modules: single character memory example

## Slide 70: License and function prototypes
MODULE_LICENSE("Dual BSD/GPL"); int memory_open (struct inode *inode, struct file *filp);
int memory_release (struct inode *inode, struct file *filp);
ssize_t memory_read (struct file *filp, char *buf, size_t count, loff_t *f_pos);
ssize_t memory_write (struct file *filp, char *buf, size_t count , loff_t *f_pos);
void memory_exit (void); int memory_init (void);
Modules: single character memory example

## Slide 71: Setting up the standard interface
struct file_operations memory_fops = { read: memory_read, write: memory_write, open: memory_open, release: memory_release };
struct file_operations
memory_fops = {
.read = memory_read,
.write = memory_write,
.open = memory_open,
.release = memory_release
};
This is a weird bit of C syntax.
  Initializes struct elements.
    So “read” member is now “memory_read”
  Technically unsupported these days?
    gcc supports it though
  dot notation is in the C99 standard.
    But some kernel code still uses colon.
Modules: single character memory example

## Slide 72: file_operations struct
struct file_operations {
ssize_t(*read) (struct file *, char __user *, size_t, loff_t *);
ssize_t(*write) (struct file *, const char __user *, size_t, loff_t *);
int (*ioctl) (struct inode *, struct file *, unsigned int, unsigned long);
int (*open) (struct inode *, struct file *);
int (*release) (struct inode *, struct file *);
int (*fsync) (struct file *, struct dentry *, int datasync);
int (*aio_fsync) (struct kiocb *, int datasync);
int (*fasync) (int, struct file *, int);
int (*lock) (struct file *, int, struct file_lock *);
ssize_t(*readv) (struct file *, const struct iovec *, unsigned long, loff_t *);
ssize_t(*writev) (struct file *, const struct iovec *, unsigned long, loff_t *);
ssize_t(*sendfile) (struct file *, loff_t *, size_t, read_actor_t, void __user *);
ssize_t(*sendpage) (struct file *, struct page *, int, size_t, loff_t *, int);
unsigned long (*get_unmapped_area) (struct file *, unsigned long, unsigned long,unsigned long,unsigned long);
};
Modules: single character memory example

## Slide 73: file_operations: A few members
struct file_operations {
ssize_t(*read) (struct file *, char __user *, size_t, loff_t *);
ssize_t(*write) (struct file *, const char __user *, size_t, loff_t *);
int (*ioctl) (struct inode *, struct file *, unsigned int, unsigned long);
int (*open) (struct inode *, struct file *);
int (*release) (struct inode *, struct file *);
};
Modules: single character memory example

## Slide 74: Set up init and exit Some globals
module_init(memory_init); module_exit(memory_exit); int memory_major = 60; char *memory_buffer;
Modules: single character memory example

## Slide 75: memory_init
int memory_init(void) { int result; result = register_chrdev(memory_major, "memory", &memory_fops); if (result < 0) { printk("<1>memory: cannot obtain major number %d\n",
memory_major); return result; } /* Allocating memory for the buffer */ memory_buffer = kmalloc (1, GFP_KERNEL); if (!memory_buffer) { result = -ENOMEM; goto fail; } memset(memory_buffer, 0, 1); // initialize 1 byte with 0s. printk("<1> Inserting memory module\n"); return 0; fail: memory_exit(); return result; }
Kmalloc does what you’d expect. The flag provides rules about where and how
To get the memory. See makelinux.com/ldd3/chp-8-sect-1
60, via global
Device name, need not be the same as in /dev
Name of file_operations structure.
Modules: single character memory example

## Slide 76: memory_exit
void memory_exit(void) { unregister_chrdev(memory_major, "memory"); if (memory_buffer) { kfree(memory_buffer); }
Modules: single character memory example

## Slide 77: Open and release (close)
int memory_open (struct inode *inode, struct file *filp) { printk("<1> Minor: %d\n", MINOR(inode->i_rdev)); return 0; } int memory_release (struct inode *inode, struct file *filp) { return 0; }
Modules: single character memory example

## Slide 78
ssize_t memory_read(struct file *filp, char *buf,
size_t count, loff_t *f_pos) {
/* Transfering data to user space */
copy_to_user (buf,memory_buffer,1);
/* Changing reading position as best suits */
if (*f_pos == 0) {
*f_pos+=1;
return 1;
} else {
return 0;
}
}
copy_to_user copies to a location in userspace (the first argument) from kernel space (the second argument), a specific number of bytes. Recall virtual memory…
f_pos is the file position.
What do you think happens if you don’t change *f_pos?
Modules: single character memory example

## Slide 79: memory_write
ssize_t memory_write( struct file *filp, char *buf, size_t count, loff_t *f_pos) { char *tmp; tmp=buf+count-1; copy_from_user(memory_buffer,tmp,1); return 1; }
Modules: single character memory example

## Slide 80: How do you set it up?
Make the module
  make -C /lib/modules/2.6.28-16-generic/build M=$PWD modules
Insert the module
  insmod memory.ko
Create the device
  mknod /dev/memory c 60 0
Make the device read/write
  chmod 666 /dev/memory
Modules: single character memory example

## Slide 81: What did all that do?
We created a device that is just a single byte of memory.
  Whatever the last thing you wrote to it, is what will be read.
For example
  $ echo -n abcdef >/dev/memory
  Followed by $ cat /dev/memory
    Prints an “f”.
Modules: single character memory example

## Slide 82: See also
https://www.apriorit.com/dev-blog/195-simple-driver-for-linux-os looks well done.
  For 5.0
  I’ve not double-checked it all