## Slide 1: EECS 473 Advanced Embedded Systems
Lecture 15:
Antennas and switching regulators
A number of slides taken from UT-Austin’s EE462L power electronics class.
http://users.ece.utexas.edu/~kwasinski/EE462LS14.html -- very useful!

## Slide 2: So, who cares? Noise immunity
Looking at signal-to-noise ratio needed to maintain a low bit error rate.
  Notice BPSK and QPSK have lower error rates.
  And as “M” goes up, we get higher error rates.
    Easier to confuse symbols!
https://en.wikipedia.org/wiki/Eb/N0
Notes: http://www.embedded.com/print/4017668

## Slide 3: Project updates
Largest roadblock; Thing you are most pleased with wrt your project.
  Robot Arm
  FLEX Lift
  Key Oracle
  Canbats
  Transcriber Glasses
  Chess
  Solar Cell

## Slide 4: On to… Antennas and transmission power
Antennas receive power differently depending on where the power is coming from.
  An isotropic antenna is one that receives power equally well from all directions.
    These don’t exist.
Real antennas focus their “effort” more in some directions than others.
  A narrow antenna, like a dish, will be focused in a very narrow range (radiation angle)
  Others, like a traditional dipole (the most common antenna) tend to have less narrow of a range.

## Slide 5: Antennas
Nothing is free here.
  If you have a narrow beam, you get some great gain in that beam but get loss in the other directions.
    This can be good.
    Think about body-area networks or Bluetooth headphones
Toroidal radiation pattern
Dish antenna radiation pattern
Figures from antenna-theory.com (if you couldn’t tell…)

## Slide 6: Radio power
Radio signals are generally measured in Watts
  However embedded systems generally measure power in mW
    Typically 30-100mW for WiFi
  It is often easiest to deal with power on a log scale.
    So we use “dBm” where
Much of this (including graphics) from https://www.allied-automation.com/wp-content/uploads/2019/03/industrial-wireless-guidebook.pdf
dBm is basically just dB but scaled to mW.

## Slide 7: Aside: dB, dBm, dBi
dB itself is a unit-less value
  Generally a ratio between two things
  On a log scale.
dBm a single value where the “ratio” is to 1mW.
  So 20dB means a 100 to 1 ratio
  20dBm means 100mW (100 times 1mW)
We’ll also see dBi when looking at antennas.
  That’s the power ratio of an antenna to an isotropic antenna (that completely non-directional antenna)
  You might see dBd, which is compared to a lossless dipole antenna. It’s 2.15dB lower than dBi.
    Vendors generally use dBi (‘cause it’s bigger) and thus so will we.

## Slide 8: Power received vs. power sent.
The Friis Transmission Formula tells us how much power we’ll receive. It is:
Where:
  Pt is the radiated power
  Pr is the received power
  Gt is the gain of the transmitting antenna
  Gr is the gain of the receiving antenna
  λ is the wavelength
  R is the distance between antennas
However, many of those terms aren’t easily available from real spec. sheets.
Instead we do some algebra and unit changes and get the following equation for range in km:
Where f is the frequency in MHz, pt and pr are in dBm and gt and gr are in dBi.

## Slide 9: Example
You are running an IEEE 802.11b network and you are currently using wireless devices with the following specifications:
  Tx power: 18 dBm @ 11 Mbps
  Rx sensitivity: -81dBm @ 11 Mbps
  Antenna gain: 2 dBi (both)
  802.11b is at 2.4GHz.
Notes:
  We are looking at 63mW of broadcast power.
  If we had dish antennas pointed at each other with a gain of 25dBi, we’d have (18+50+81)/20=275km!
  Note that this assumes an unobstructed line-of-sight signal with no significant interference.
    Sometimes realistic, often not.
50kW@720KHz
Notes: 720 KHz
WGN is a clear channel Class A station operating with the maximum AM Radio power of 50,000 watts, using a non-directional antenna. During daytime hours, it can be heard as far as Windsor, Ontario, around 250 miles away, and during the nighttime hours, is often audible over much of the central United States and Canada.
50,000W is 76.9897dBm

## Slide 10: Looking at a real antenna (ANT-WSB-ANF-09)
9dBi
  Gets there by radiating in a toroid
    Spread evenly along the ground (half power beam width is 360)
    Doesn’t go up or down at all.
      Half power beam width is at 10
HPBW: Half power beam width—where you get ½ power.
VSWR (viz-wer): impedance matching stuff, not covered by us.

## Slide 11: Switching regulators

## Slide 12: What are DC converters?
DC converters convert one DC voltage level to another.
  Very commonly on PCBs
    Often have USB or battery power
    But might need 1.8V, 3.3V, 5V, 12V and -12V all on the same board.
  On-PCB converters allow us to do that
Images from http://itpedia.nyu.edu/wiki/File:V_reg_7805.jpg, http://www.electronics-lab.com/blog/wp-content/uploads/2007/10/p1000255.JPG both now dead links...

## Slide 13: Different types of DC converters
Linear converters
Switching converters
Simpler to design
Low-noise output for noise-sensitive applications
Can only drop voltage
  And in fact must drop it by some minimum amount
  The larger the voltage drop the less power efficient the converter is
Can be significantly more complex to design
  Worth avoiding for this class unless you have to do it.
Can drop voltage or increase voltage
  “buck” and “boost” respectively
Generally very power efficient
  75% to 98% is normal

## Slide 14: Characteristics of DC Converters
To better understand how to pick a converter we will go over the following characteristics seen in all DC converters
  Power wasted (as heat)
  Quiescent current,
    The leakage current that occurs regardless of operation.
  Power supply rejection ratio (PSRR)
    The ability to reject output noise at different frequency
  External capacitors and equivalent series resistance(ESR)
    Output noise filter that helps keeping the signal clean
These characteristics are what people generally look for when selecting converters, but they’re not by any means the only characteristics that matter.

## Slide 15: Quick look at the options
Linear converter
  LDO
Switching converter
  Buck
  Boost
  Buck-Boost

## Slide 16: Linear converter
One can think of a linear converter as a “smart” voltage divider.
  If we were using a very small amount of current, that would work.
  But hugely wasteful.
Instead, we want the top resistor to vary with the load.
  As load draws more current, R1 drops resistance to keep voltage constant.
Figures on this slide and the next taken from https://www.analog.com/media/en/technical-documentation/application-notes/an170f.pdf, which is a great app-note.

## Slide 17: Voltage converters/regulators: Review Linear
Drops voltage
  Heat waste > (Vin-Vout)/Vin
    That’s a lot if we are dropping much voltage
  Has minimum drop
  Uses current even if no load (quiescent current)
  Often needs an output (and maybe input) cap.
LDO – low dropout is main variation.
  Minimum drop is often very small (though can vary by current draw…)
  Generally needs larger caps.
  Can have larger quiescent current
    Depends on if “resistor” is BJT or FET, FET more common these days.

## Slide 18: Stability
The opamp adjusts the effective resistance of the transistor to control the voltage.
  Clearly we’ve got a control loop and there is delay in that loop.
    That means that if the load (or source…) is varying at a certain frequencies, we could get positive feedback.
    The output (and sometimes input) cap can filter out those frequencies.
An MOSFET LDO.
http://www.ti.com/lit/an/snva020b/snva020b.pdf provides a very nice, detailed overview with Bode plots etc., though it is a bit dated.

## Slide 19: Is stability a real issue for linear regulators?
Well yes.
  But these days, the requirements are pretty lax.
    The LT3007 wants a 2.2μF ceramic cap at the output and maybe a ~1 μF input cap.
      Needs moderately low ESR.
      Data sheet expresses concerns about cheap ceramic caps.
  Older linear regulators had a lot more restrictions
    Often required some additional ESR, but not too much.
Older and cheaper devices might have some pretty significant (and sometimes costly) needs.
  Just be aware that in the early 2000s this was a pretty big issue.

## Slide 20: Switching Converters
Once you leave the realms of linear converters it gets more complex.
  Introducing common switching converters!
    All include a diode, transistor, inductor and a capacitor
Table from http://www.nxp.com/documents/application_note/APPCHP2.pdf
Converters | General Topology | Application
Buck |  | Drop voltage
Boost |  | Increase voltage
Buck-boost(inverting) |  | Increase or decrease voltage and inverse polarity

## Slide 21: Functionality – Switching Converters
Common switching converters
  Converters now include a transistor and diode used for switching and an inductor as energy storage.
    In general, a switching converters works by controlling the frequency and duty cycle that the transistor is operating at
  Similar to linear converters, most of the work is already done.
  Only have to pick IC with the right parameter and follow the datasheets given for appropriate inductors and capacitors.
Size of inductor in relation to the rest of the component
Example switching regulator from http://ycprojects.wordpress.com/

## Slide 22: Functionality – Switching Converters
Common switching converters
  Aside from the noble goal of making circuit analysis more complex () both the inductor and capacitor play important roles in switching converters.
    Capacitor
      Used to store energy due to the voltage applied thus maintaining a constant voltage
      Generally selected to limit ripple to the correct specification
    Inductors
      Similar to the capacitor, but an inductor is used to store energy due to current flow. This in turn maintains a constant current or is used to limit the rate of change of current flow.
      This will also determine the peak to peak current in the circuit which affects the transistor, diode and the “mode” the converter will operate at.

## Slide 23: Functionality – Buck
Common switching converters
  Let’s start with the buck converter
    Note the drive circuit, this is what the IC is
    For simplicity’s sake let’s disregard and , the internal resistance of the inductor and capacitor
    It looks pretty complex, so let’s try to understand why we need each component!

## Slide 24
Capacitors and Inductors
In capacitors:
Capacitors tend to keep the voltage constant (voltage “inertia”). An ideal
capacitor with infinite capacitance acts as a constant voltage source.
Thus, a capacitor cannot be connected in parallel with a voltage source
or a switch (otherwise KVL would be violated, i.e. there will be a
short-circuit)
The voltage cannot change instantaneously
In inductors:
Inductors tend to keep the current constant (current “inertia”). An ideal
inductor with infinite inductance acts as a constant current source.
Thus, an inductor cannot be connected in series with a current source
or a switch (otherwise KCL would be violated)
The current cannot change instantaneously

## Slide 25: Switching – lossless conversion of 39V to average 13V
If the duty cycle D of the switch is 0.33, then the average voltage to the expensive car stereo is 39 ● 0.33 = 13Vdc. This is lossless conversion, but will it work?
Rstereo
+
39Vdc
–
Switch state, Stereo voltage
Closed, 39Vdc
Open, 0Vdc
Switch open
Stereo voltage
39
0
Switch closed
DT
T

## Slide 26: Convert 39Vdc to 13Vdc, cont.
Try adding a large C in parallel with the load to control ripple. But if the C has 13Vdc, then when the switch closes, the source current spikes to a huge value and burns out the switch.
Rstereo
+
39Vdc
–
C
Try adding an L to prevent the huge current spike. But now, if the L has current when the switch attempts to open, the inductor’s current momentum and resulting Ldi/dt burns out the switch.
By adding a “free wheeling” diode, the switch can open and the inductor current can continue to flow. With high-frequency switching, the load voltage ripple can be reduced to a small value.
Rstereo
+
39Vdc
–
C
L
Rstereo
+
39Vdc
–
C
L
A DC-DC Buck Converter
lossless

## Slide 27: Functionality – Buck
Common switching converters - buck
  During operation, the buck converter functions differently depending on the switch
    On state
      Current flows through the transistor but reverse bias prevents current flow through the diode
      Inductor begins to charge and a smaller current becomes
    Off state
      Switch opens and the inductor starts discharging as the only power source
    This on-off state will determine the “mode” the converter operate in
Buck: switch on
Buck: switch off
Figures from Wikipedia

## Slide 28: Functionality – Switching Converters
The duty cycle of the switching will determine the mode each converter operate at various loads
  Continuous Mode
    The inductor current will never fall to zero when the switch is off
  Discontinuous Mode
    Inductor current will reach zero before the end of the full duty cycle
  Each mode has its advantages and disadvantages depending on the switching converters.
    In generally it’s how they change the frequency response.

## Slide 29: Net effect—avoiding discontinuous mode
Lower load current, lower inductance and lower switching frequency move us toward discontinuous mode.
There are pros and cons
to both modes, but one
real issue is that switching
between them can cause ringing on the inductor’s output.
(See UT slides for why, has to do with parasitic
cap in transistor and diode.)

## Slide 30: Functionality – Boost (Doing this much more quickly)
On state
  Current flows through the transistor(least resistance) making the diode reverse bias and no
  Inductor is charged in the process
Off state
  The energy discharged by the inductor is superimposed to the input, generating a higher output
Generic boost schematic
Boost: on state
Boost: off state
Schematics from http://en.wikipedia.org/wiki/Boost_converter

## Slide 31
V
in
+
V
out
–
C
i
C
I
out
i
in
Buck converter
i
L
L
+ v
L
–
Boost converter
V
in
+
V
out
–
C
i
C
I
out
i
in
i
L
L
+ v
L
–

## Slide 32
Boost converter
This is a much more unforgiving circuit than the buck converter
V
in
+
V
out
–
C
i
C
I
out
i
in
i
L
L
+ v
L
–
i
D
If the MOSFET gate driver sticks in the “on” position, then there is a short circuit through the MOSFET – blow MOSFET!
If the load is disconnected during operation, so that Iout = 0, then L continues to push power to the right and very quickly charges C up to a high value (250V) – blow diode and MOSFET!
Before applying power be sure that a load is solidly connected
!

## Slide 33: Functionality – Switching Converters
Common switching converters
  Buck-boost(inverting)
    The baby of buck and boost…
    On state
      Diode is reverse biased and the inductor is charged but input and output is isolated from each other
        Creates more stress on the diode!
      is now the charged from off state but different polarity
    Off state
      Inductor voltage reverses, passing energy to the capacitor and load through forward biased diode
    Due to the characteristics of boost, buck-boost suffers the same problem. Therefore a discontinuous mode is favored
Generic buck- boost schematic
Buck-boost: on state
Buck-boost: off state
Schematics from http://en.wikipedia.org/wiki/Buck%E2%80%93boost_converter

## Slide 34: Functionality – Switching Converters
To give you a better idea of how duty cycle affect the output of each converter in continuous mode refer to the table below
  In discontinuous mode these equations are no longer true, but we will not discuss them here and they can also be found online
  More information on switching converters can be found at http://educypedia.karadimov.info/library/APPCHP2.pdf https://web.archive.org/web/20120306171808/http://ecee.colorado.edu/copec/book/slides/Ch5slide.pdf http://www.ti.com/lit/an/slva057/slva057.pdf
Converters | Duty cycle impact on output Voltage
Buck | Vout=Vin*D
Boost | Vout=
Buck-boost(inverting) | Vout=
Converters | Duty cycle impact on output Voltage
Buck | Vout=Vin*D
Boost | 
Buck-boost(inverting) | 

## Slide 35: Picking converters
Hopefully at this point you can start to see how much more complicated a switching converter is relative to a linear converter
  Every change made to the capacitor, inductor, transistor or diode will have an significant effect in not only the efficiency of each converter but also the life and way they operate
  Fortunately it won’t be the end of the world if you decide to use switching converters
    Using mic2168a, a controller for buck converter, as example. We can see not only do they provide information on the controller but also the external components needed for proper functionality (9pages!).
  ON semiconductor also provide a detailed, though dated, published paper on both linear and switching regulator, covering the theory and design consideration needed.

## Slide 36: Efficiency of switchers
It’s going to vary a lot.
  Depends on the converter, the output current, etc.
  Graph on the right is of a TPS5420 under reasonable conditions.
    Typically has only 18μA current when you shut it down (needs a control pin)
TPS5420